## Slide 1
Standalone DRRS Workshop 2
March 27, 2024

## Slide 2: Comparison of Options with and without On-line DRRS
Options | Off-Line DRRS only | Off-Line + On-Line DRRS
Qualified MW | Eligible capacity from only Off-Line Resources, potentially including Off-Line ESRs*. Expected to exclude Controllable Load Resources | Eligible capacity from both On-Line and Off-Line Resources
Liquidity/ Market Efficiency | Smaller pool of eligible Resources, particularly in the short-term | Lager pool of eligible Resources, particularly in the short-term
Incentives | Resources that can be Off-Line with a cold start up time <=2 hours | All dispatchable Resources, including Resources that have long start up times (>2 hours) but can be dispatched if brought On-Line in advance
Complexity | Less complex Avoids Real-Time changes associated with energy and Ancillary Service offer floors Avoids RUC changes necessary for the optimization to recognize and utilize On-Line DRRS capacity before recommending the commitment of an additional Resource Reduces effort for evaluating failed DRRS quantities and compliance | More complex Requires Real-Time changes associated with energy and Ancillary Service offer floors Requires RUC changes necessary for the optimization to recognize and utilize On-Line DRRS capacity before recommending the commitment of an additional Resource Increases effort for evaluating failed DRRS quantities and compliance Increases complexity for state of charge considerations for ESRs.
Additional Considerations | Clearer relationship between Operator’s options to deploy DRRS vs. issuing a RUC instruction | Reintroduction of “offer floor” or “HASL”-like concepts reintroduces some of the inefficiencies otherwise addressed by RTC
* Current rules for ESRs under NPRR1014 is that ESRs will not use a Resource Status of OFF (i.e., can’t be Off-Line and available)