## Slide 1: Demand Response Monitor
For the ERCOT Operator
Floyd J. Trefny
January 16, 2024

## Slide 2: Demand Response in ERCOT
Since the inception of ERCOT, Demand Response from loads has increased.
Significant amounts of new Demand Responsive Load is forecast to continue over the next few years.
ERCOT operators need a better understanding of demand response occurring in real-time to better understand risks during projected critical shortages of generation capacity to serve load.
A Demand Response Monitor is proposed to assist operators in making judgements of near-future capacity needs. The Monitor would detect a response by loads attributable to:
  LMP Energy Price
  4CP
  Near 4CP
  Conservation Alerts
Over time, empirical data collected by ERCOT could also used by ERCOT to predict future Demand Response for other reliability applications.

## Slide 3
How Can the System Operator Know When a MW Peak Has Occurred?
ERCOT Total Load* 72,327 Mw
Peak 72,548 Mw
Time @ Measured Peak 16:47
* Total ERCOT Load is calculated as sum of total generation and DC tie telemetry
(total generation could exclude renewables if the objective is to determine peak NET Load)
System Time 17:08
Time 17:08
For Example: Total ERCOT Demand

## Slide 4
Gulf Coast
765 Mw
802 Mw
13:55
Valley
318 Mw
320 Mw
14:08
East
5 Mw
175 Mw
13:31
West
22 Mw
705 Mw
13:10
Central
920 Mw
920 Mw
14:08
Demand Response Monitor
Current Responsive Load 2012 Mw
Peak 2922 Mw
Observed Response 910 Mw
Time 14:08
Chart: Demand Response Monitor
| 120 | 115 | 110 | 105 | 100 | 95 | 90 | 85 | 80 | 75 | 70 | 65 | 60 | 55 | 50 | 45 | 40 | 35 | 30 | 25 | 20 | 15 | 10 | 5
Demand Responce | 2 | 3.22 | 0.29501 | 0 | 50 | 30 | 40 | 60 | 118.6016 | 129.6527 | 149.77 | 163.1 | 189.21 | 214.21 | 208.1 | 210.24 | 243.44 | 280.75 | 348 | 575 | 775 | 879 | 863.77 | 914
System LMP | 50 | 52 | 51.22 | 49.075 | 49.2 | 52.1034 | 52.7519 | 57.88 | 59.1689 | 59.4327 | 70.22 | 79.55 | 83.55 | 105.66 | 108.55 | 99.55 | 110.69 | 132.75 | 148 | 200 | 375 | 400 | 479 | 384.77
LMP $1000
LMP $50
LMP $50
LMP $75
LMP $400
LMP

## Slide 5: Demand Response Monitor
The Demand Response Monitor, if implemented, would select various loads by analysis of past operations using historical State Estimator data. ERCOT staff has indicated this is doable.
The methodology would be very similar to that employed in the past by ERCOT to analyze demand response using changes in kWh meter readings.
  Presentations were made periodically to the Demand Side Working Group and WMS that showed aggregate load response.
ERCOT would select substation loads that have response characteristics.
  It is not necessary to be precise to gain insight into real-time load changes.
Display would only be accessible by ERCOT Operations.
The Demand Response Monitor would obviate the need for imposition of highly intrusive data reporting requirement on retail loads.

## Slide 6: Questions