## Slide 1: HEN RTC ASDC Proposal
Shams Siddiqi, Ph.D.
Hunt Energy Network (HEN)
(512) 619-3532
shams@crescentpower.net
RTCBTF Meeting
April 10, 2024

## Slide 2: RTC ASDC Design for Reliable Procurement of Essential Ancillary Services
Current ASDCs used to procure AS in DAM are at SWCAP for all AS and IRRs do not provide any Up-AS (curtailed IRR may provide Up-AS under RTC)
ASDC under current RTC design for RRS, ECRS and Non-Spin can be significantly lower (e.g. $265/MW for Non-Spin) than SWCAP based on shape of ORDC and would routinely forgo AS procurement during scarcity
Current RTC ASDCs use AORDC based on historical ORDC adders that:
  ORDC was never used for AS procurement – only used for capacity OR price; and
  Current RTC ASDCs are significantly suppressed and undervalued due to (i) reducing VOLL by System Lambda and (ii) overly crediting Offline capacity.
HEN’s proposed RTC ASDC changes would ensure more reliable procured amounts of AS under RTC and avoid undervaluing AS:
  Since under RTC there is no Offline ORDC adder and to ensure adequate Online Reserves, do not count Offline capacity when forming AORDC for ASDC purposes
  Since (VOLL-System Lambda) was used to reduce ORDC adder to keep prices at or below VOLL but not for actually procuring AS, do not reduce VOLL by System Lambda when forming AORDC for ASDC purposes
  Thus, AORDC=(𝟏−CDF(𝑹𝑻𝑶𝑳𝑪𝑨𝑷−𝑿, 𝟗𝟐𝟓, 𝟏𝟐𝟏𝟑))∗𝑽𝑶𝑳𝑳 if X>3000 or = 𝑽𝑶𝑳𝑳 if X<=3000 where CDF=Cumulative Distribution Function of norm. distr. and X=MCL
Note: proposed RTC ASDC changes may still forgo Non-Spin, ECRS, and some RRS during scarcity compared to today’s much higher pre-RTC ASDCs in DAM

## Slide 3: ASDC Design to Ensure Procurement of Critical AS during Scarcity
During severe scarcity under RTC, SCED should award critical reliability RRS and Reg-Up instead of ECRS and Non-Spin but SCED may not under current RTC ASDC design:
  If remaining MWs have ECRS offer lower than RRS or Reg-Up Offer by even a penny and max ASDCs for both=$5,000/MW, then SCED will award ECRS and not RRS or Reg-Up
Lessons learned from Uri: Grid needs to maintain at least 1,500MW of RRS to prevent total collapse from an additional 1,500MW of GR tripping even if it requires firm Load shed – this implies ASDC for first 1,500MW of RRS must be set high enough
  Set ASDC for at least 1,500MW of RRS at $9,000.02/MW (assumes Operations will shed Load to maintain 1,500MW of PRC that can be awarded RRS by SCED)
  Set ASDC for Reg-Up at $7,000.01/MW
  Set Power Balance Penalty at $11,000.03/MW
  MCPC Cap=$5,000/MW and System Lambda Cap=$5,000/MWh
Ensures 1,500MW of RRS is given procurement priority over all other Up-AS then priority given to Reg-Up
Since all MCPCs are capped and System Lambda is capped at SWCAP – proposed change ensures AS critical for reliability – RRS and Reg-Up – are given a higher priority in procurement instead of capacity price AS – ECRS and Non-Spin
  So, MCPCs during severe scarcity will remain the same with this change; however, critical AS would be procured