## Slide 1
2023 UFE Analysis Report
Joe Lara
June 2024 WMS

## Slide 2: UFE Basics 1
UFE (Unaccounted For Energy) is computed as follows:
UFE = Generation – (Load + Losses)
Negative UFE indicates load/losses are overestimated
Sources of UFE include:
■ Generation Measurement Errors
■ DC Tie Inadvertent Energy
■ Load - Missing/Erroneous Usage Data
- Backcast Profile Error
- Load Profile ID Assignment Error
- Theft
■ Losses - Model Error
- Loss Calculation Error
- Loss Code Assignment Error

## Slide 3: UFE Basics 2
Net Generation for Settlement Interval
Profiled Energy Usage
Non-Metered Accounts
Interval Data
Energy Usage
Losses:
Transmission & Distribution
UFE
Net Generation
Compared to
Load Buildup
GAP - - - - - - >

## Slide 4: Protocol Language 11.6 – Unaccounted for Energy Analysis
11.6.1 Overview
(1) ERCOT will provide an annual Unaccounted For Energy (UFE) analysis report consisting of UFE data analysis from the preceding calendar year. This report will be based on final Settlement data and will be posted to the Market Information System (MIS) Public Area by April 30th. The appropriate …
11.6.2 Annual Unaccounted For Energy Analysis Report
The annual UFE analysis report will contain both ERCOT-wide and UFE allocation category quantities as follows:
(a) Total UFE MWHs;
(b) Total UFE cost;
(c) Percent of total UFE to ERCOT Load;
(d) Percent of total UFE cost; and
(e) Notice of any factors that may be contributing to UFE.

## Slide 5: Data Required Per Protocol Section 11.6.2
 | A – Total UFE MWHs | B – Total UFE Cost | C – Percent of Total UFE to ERCOT load | D – Percent of Total UFE Cost
TOTUFE_U1 | -1,078,199 | -$92,779,500 | -0.2412% | 100.00%
UFEIDR_U1 | -1,012,282 | -$88,198,181 | -0.2265% | 95.06%
UFENIDR_U1 | -7,757 | -$529,209 | -0.0017% | 0.57%
UFETRANS_U1 | -58,160 | -$4,052,109 | -0.0130% | 4.37%
Legend: | 
TOTUFE_U1 - Total ERCOT Wide UFE | 
UFEIDR_U1 - Distribution IDR UFE | 
UFENIDR_U1 - NIDR UFE | 
UFETRANS_U1 - Transmission IDR UFE | 

## Slide 6: Average Daily % UFE (sorted low to high)

## Slide 7: UFE Monthly MWH

## Slide 8: UFE Monthly Cost

## Slide 9: Historical Yearly Values
 | MWH | COST | % of LOAD | AVG MCP
2004 | 1,344,289 | $102,693,690 | 0.40% | $42.00
2005 | 1,082,561 | $174,154,088 | 0.30% | $65.91
2006 | 2,304,458 | $187,975,534 | 0.70% | $51.26
2007 | 2,914,297 | $206,949,832 | 0.90% | $52.77
2008 | 1,541,086 | $134,692,211 | 0.40% | $68.04
2009 | 1,351,187 | $44,857,873 | 0.40% | $30.89
2010 | 1,756,344 | $85,406,714 | 0.55% | $35.74
2011 | 1,453,256 | $31,666,952 | 0.43% | $43.30
2012 | 1,002,761 | $25,945,816 | 0.31% | $26.60
2013 | -395,393 | -$17,061,127 | -0.12% | $31.71
2014 | 298,578 | $2,286,431 | 0.09% | $38.02
2015 | 240,091 | $1,441,929 | 0.07% | $24.80
2016 | 644,293 | $11,037,155 | 0.18% | $22.60
2017 | -452,775 | -$20,469,613 | -0.13% | $26.53
2018 | 657,974 | $7,209,457 | 0.17% | $32.28
2019 | 252,851 | -$22,095,272 | 0.07% | $38.83
2020 | -265,915 | -$20,023,844 | -0.07% | $24.03
2021 | 356,388 | $246,439,449 | 0.09% | $150.40
2022 | 1,126,521 | $20,085,214 | 0.26% | $64.89
2023 | -1,078,199 | -$92,779,500 | -0.24% | $50.68
Note: Avg MCP excludes NOIE load zones

## Slide 10: Transmission Loss Factor Calculation Review
13.2.3 Transmission Loss Factor Calculations
  The following formulas shall be used to translate the seasonal on-peak and off-peak TLFs into Settlement Interval TLFs.
    TLFi = (SSC * SIELi) + SIC

## Slide 11: 2023 Deemed Transmission Loss vs. UFE

## Slide 12: 2024/2025 Transmission Losses & Actual UFE To Date

## Slide 13: 2024/2025 Higher TLFs
ERCOT has not performed a deep analysis but believe the higher TLFs are due to the reasons below.
Increase in wind generation which results in more load flowing through CREZ lines from wind generation areas to large population centers
Higher load from large flexible loads (LFLs)
The need for additional voltage tuning in the SSWG cases
System wide trends regarding a change in generation and load mix

## Slide 14: NPRR1145 – Use of State Estimator-Calculated ERCOT-Wide TLFs in Lieu of Seasonal Base Case ERCOT-Wide TLFs for Settlement
Approved By Public Utility Commission on 5/11/2023
Priority – 2024
Rank – 4010
Comments
  $50k-$80k, 3-6 months
  Impacted Systems: S&B, EMS, Data Analytics
  Project delayed due to EMS upgrade/freeze
ERCOT is currently considering a Q3 2024 start for this project

## Slide 15: QUESTIONS?