## Slide 1
Review of the Energy and AS Offer Caps in the Context of Current Policy
Sai Moorty
Market Design
RTCTF
May 8, 2024

## Slide 2: RTC+B : SWCAP, VOLL, max ASDC settings
 | HCAP $/MWh | LCAP $/MWh | SWCAP $/MWh | VOLL $/MWh | Power Balance penalty $/MWh
DAM | 5000 (DAM) | 2000 | If PNM<=315K SWCAP=HCAP(DAM) Else SWCAP=LCAP | If PNM<=315K VOLL=5000 (DAM HCAP) Else VOLL=2000 (DAM LCAP) | NA
RTM | 2000 (RTM) | 2000 | If PNM<=315K SWCAP=HCAP(RTM) Else SWCAP=LCAP |  | VOLL+2000+0.01$/MWh
Peaker Net Margin (PNM) threshold = 315,000 $/MW-year
In DAM and RTM, the maximum price ($/MW/h) on ASDC is the prevailing VOLL (DAM HCAP or LCAP)
Price Caps in Post Processing of DAM and RTM:
  LMP
    DAM: Not capped
    RTM: LMP, exclusive of congestion, capped at prevailing VOLL
  AS MCPC
    For DAM and RTM, AS MCPCs are capped at prevailing VOLL. Note that AS MCPC also cannot exceed the max price on the ASDC

## Slide 3: Comment on Opportunity Costs
Energy $/MWh
1700 $/MWh
80GW
GTBD
EOC
AS
$/MW/h
5000 $/MW/h
7GW
ASDC
AS Offer
AS MCPC
10 $/MW/h
No congestion
AS shortage pricing kicks in, AS MCPC set by ASDC
  AS MCPC = 500 $/MW/h
Marginal Energy Offer = 1700 $/MWh
Marginal AS Offer = 10 $/MW/h
What is the LMP? Need to consider opportunity cost
  Profit from AS = AS MCPC – AS offer = 500-10=490 $/MW/h
  Profit from energy should be at least 490 $/MWh
    LMP=Marginal Energy Offer + Opportunity Cost = 1700+490 = 2190 $/MWh
500 $/MW/h

## Slide 4: Query from Market Participant
With a bit of paraphrasing
Concerned with the impacts of having an offer cap for ESRs in RTC that was below the price cap.
Scenario expressed by the market participant :
We expect the market to be tightest in HE20
It is a peak summer or winter day
We are in RTC and the bid/offer cap for ESRs is $2,000
It is currently HE17 and we are not in an EEA scenario, and prices are printing $2,500. This signals that the market is tight, but it is not yet at its tightest point (we/ERCOT expect the market to be tightest in HE20).
Under this framework, I will not be allowed to charge my battery in HE17, and instead, I would likely be discharging in HE17.
ERCOT would benefit from us charging in HE17 because we could then be able to discharge in the tightest hours of the day.
  I could help the system in this instance by providing regulation up and charging simultaneously (I would have a charging basepoint, and then reduce my charging levels based on regulation up signals).
CAISO faced this issue once already where they had an offer cap for batteries at $1000 and they all were forced to discharge ahead of the evening peak. Prices a couple hours later went to $2,000, and CAISO was left with little battery capacity to help when the market was truly the tightest.

## Slide 5: ERCOT Response
If ESR offer side (or the bid/offer curve) is set at 2000 $/MWh and the LMP at ESR = 2500 $/MWh does not necessarily imply that the ESR must get a discharging Base Point. It depends upon the individual AS offers and MCPCs. Depending on the AS MCPCs, the ESR may even get a charging Base point.
In RTC+B, RTC SCED is procuring energy and the individual AS products in a co-optimized manner. Given the pricing outcomes from the SCED optimization (no energy price caps), the MW awards for energy and individual AS would be such that it provides the best financial outcome to a Resource based on the submitted bid/offer for energy and offer for AS.
So in the scenario provided (assume that there are NO transmission constraints.), the ESR LMP =2500 $/MWh when the ESR Offer is 2000 $/MWh. Whether this ESR gets a discharging or charging Base Point depends upon:
Marginal energy offer cleared, and
AS offers submitted for this ESR and the SCED AS MCPCs.
A SCED LMP of 2500 $/MWh when the SWCAP = 2000 $/MWh implies that the SCED LMP has AS opportunity costs included.

## Slide 6: ERCOT Response
Lets look at a couple of scenarios. ESR is a +-100 MW, SOC = 50%, qualified to provide 200 MW of AS (HSL-LSL). ESR bid offer is a flat 2000$/MWh from LSL (-100 MW) to HSL (+100 MW), AS offer for 200 MW = 0 $/MW/h
Scenario 1: No congestion, LMP=2500 $/MWh, AS MCPC = 800 $/MW/h (consider only one type of AS for simplicity), Marginal Resource Offer cleared is 1700 $/MWh.
In this scenario:
power balance constraint is not violated (LMP <= power balance penalty)
ESR is willing to pay up to 2000 $/MWh to charge.
LMP of 2500 $/MWh has AS opportunity cost of 800 $/MW/h included.
With AS MCPC = 800 $/MW/h, ASDC is setting price and system is going short on AS
From the above, the outcomes for the ESR are:
AS awards as much as possible subject to SOC constraints
ESR can get a charging Base Point if there is SOC charging headroom and generation capacity available in the system. RTC-SCED will prefer giving the ESR a charging Base Point rather than increasing the AS shortage because for each MW of charging Basepoint, the system will benefit by 2000*1 = 2000$, whereas increasing the AS shortage will increase the system benefit by 800*1=800

## Slide 7: ERCOT Response
Scenario 2: No congestion, LMP=2500 $/MWh, AS MCPC = 500 $/MW/h (consider only one type of AS for simplicity), Marginal Resource Offer cleared is 2000 $/MWh.
In this scenario:
power balance constraint is not violated (LMP <= power balance penalty)
ESR is willing to pay up to 2000 $/MWh to charge.
LMP of 2500 $/MWh has AS opportunity cost of 500 $/MW/h included.
With AS MCPC = 500 $/MW/h, ASDC is setting price and system is going short on AS
From the above, the outcomes for the ESR are:
AS awards as much as possible subject to SOC constraints as the best financial outcome for the ESR is maximizing profits from AS
  Profit from AS = AS MCPC – AS offer = 500-0
AS ESR bid/Offer is marginal, the ESR could get a charging or discharging Basepoint depending on system conditions. Note: If the result is a discharging Base Point, It can be only a maximum of HSL- AS award.