## Slide 1
Dispatchable Reliability Reserve Service (DRRS) Workshop III
ERCOT Staff
June 3, 2024
ERCOT Public

## Slide 2: Recap
Overview of Dispatchable Reliability Reserve Service (DRRS)
  Required by PURA § 39.159(d) as adopted by H.B. 1500 (88th Leg.)
  Quantities will be determined during the annual Ancillary Service Methodology process
  Is procured in the Day-Ahead Market (DAM)
  Is not co-optimized with energy or other Ancillary Services in the Real-Time Market (RTM)
  A QSE may self-arrange DRRS
  Deployed through Reliability Unit Commitment (RUC) processes
  The RUC engine will be modified to:
    Consider DRRS capacity as available to meet committed capacity margin deficiencies and any other issues identified by the RUC optimization
    Prioritize the use of DRRS over committing other off-line Generation Resources
  ERCOT-directed deployment of DRRS will be considered in the determination of the Real-Time Reliability Deployment Price Adder
  Settlement to include:
    RUC Make-Whole Cost allocation based on DRRS shortfall
    Failed Quantity charge and payment

## Slide 3: Updates to NPRR 1235 from Previous Design Workshops
Eligibility
  Previous workshops (1 and 2) contemplated a design for DRRS that could be provided by both on-line and off-line Resources with a start time of 2 hours or less that are SCED dispatchable and are able to provide the service at their HSL for 4 consecutive hours
  Based on further internal discussion ERCOT is proposing to limit the eligibility to provide DRRS to off-line Resources only
    Resources without an off-line Resource Status (e.g., Energy Storage Resources (ESRs)) are not able to provide this service
  Controllable Load Resources (CLRs) are precluded by current statute*
  *CLRs precluded by PURA § 39.159(d)(2)(A) because they would not be running at their HSL (defined for Load Resources in Protocol § 2 as Maximum Power Consumption)

## Slide 4: Updates to NPRR 1235 from Previous Design Workshops
Settlement
  For Combined Cycles, additional language included to:
    Analyze for incremental Startup costs due to a transition to a different configuration between a DRRS deployment and RUC-commitment between two contiguous hours
    Analyze for incremental Startup costs when a DRRS deployed Resource is RUC-Committed for Additional Capacity (RUCAC)
    Calculate the incremental Minimum Energy Cost and Minimum Energy Revenue when a DRRS-deployed Resource is RUCAC
    The additional Startup and Minimum Energy costs listed above will be included in the RUC Guarantee. The additional Minimum Energy Revenue will be used to offset the RUC Guarantee.
  Included DRRS in Section 9.14.10, Settlement for Market Participants Impacted by Omitted Procedures or Manual Actions to Resolve the DAM

## Slide 5: Rationale for Changes (Off-Line Only)
Including on-line Resources would have required:
  New energy and Ancillary Service offer floors in Real-Time
  Changes to the RUC optimization to recognize and utilize On-Line DRRS capacity before the commitment of an additional Resource.
Including ESRs would have introduced:
  Requirements to preserve state of charge (SOC)
  A new “off-line” Resource Status concept for ESRs
During previous workshops, several stakeholders voiced concerns with how these changes might work.
A straightforward design will allow DRRS to move ahead in accordance with OKR deadline and reduce the time to implement.

## Slide 6: Next Steps
NPRR 1235 and associated Preliminary IA to be discussed at June 13 PRS meeting
Open to future evolution of DRRS through design enhancements