## Slide 1: Demand Response Monitor
Demand Side Working Group
Floyd J. Trefny
June 21 2024

## Slide 2: Demand Response in ERCOT
Since the inception of ERCOT, Demand Response from loads has increased.
Significant new Demand Responsive Load is forecast to continue increasing over the next few years. Today, over 3000 MWs of new Flexible Load is operating in real-time.
  ERCOT operators need a better understanding of demand response occurring in real-time to better understand risks during projected critical shortages of generation capacity to serve load.
A Demand Response Monitor is proposed to assist operators in making judgements of near-future capacity needs. The Monitor would detect responses by loads attributable to:
  LMP Energy Price
  4CP
  Near 4CP
  Conservation Alerts
Over time, empirical data collected by ERCOT could also used by ERCOT to predict future Demand Response for other reliability applications.

## Slide 3
How Can the System Operator Know When a MW Peak Has Occurred?
ERCOT Total Load* 72,327 MWs
* Total ERCOT Load is calculated as sum of total generation and DC tie telemetry
(total generation could exclude renewables if the objective is to determine peak NET Load)
System Time 17:08
Time 17:08
For Example: Total ERCOT Demand
Peak 72,548 MWs
Time @ Measured Peak 16:47

## Slide 4
Gulf Coast
765 Mw
802 Mw
13:55
Valley
318 Mw
320 Mw
14:08
East
5 Mw
175 Mw
13:31
West
22 Mw
705 Mw
13:10
Central
920 Mw
920 Mw
14:08
Demand Response Monitor
Current Responsive Load 2012 Mw
Peak 2922 Mw
Observed Response 910 Mw
Time 14:08
LMP $1000
LMP $50
LMP $50
LMP $75
LMP $400
LMP
Chart: Demand Response Monitor
| 120 | 115 | 110 | 105 | 100 | 95 | 90 | 85 | 80 | 75 | 70 | 65 | 60 | 55 | 50 | 45 | 40 | 35 | 30 | 25 | 20 | 15 | 10 | 5
Demand Response | 2 | 3.22 | 0.87835 | 0 | 50 | 30 | 40 | 60 | 122.6146 | 132.4155 | 149.77 | 163.1 | 189.21 | 214.21 | 208.1 | 210.24 | 243.44 | 280.75 | 348 | 575 | 775 | 879 | 863.77 | 914
System LMP | 50 | 52 | 51.22 | 49.6584 | 49.2 | 50.8328 | 53.8216 | 57.88 | 60.4191 | 62.1955 | 70.22 | 79.55 | 83.55 | 105.66 | 108.55 | 99.55 | 110.69 | 132.75 | 148 | 200 | 375 | 400 | 479 | 384.77

## Slide 5: Demand Response Monitor
The Demand Response Monitor would select various loads by analysis of past operations using historical State Estimator data. State Estimator Loads are in MWs. ERCOT staff has indicated this is doable.
The methodology used to select which loads to use would be very similar to that employed in the past by ERCOT to analyze energy response using changes in kWh meter readings.
  Presentations were made periodically to the Demand Side Working Group and WMS that showed aggregate load response.
ERCOT would select substation loads that have response characteristics.
  It is not necessary to be precise to gain insight into real-time load changes.
The Demand Response Monitor would obviate the need for imposition of highly intrusive data reporting requirement on retail loads.

## Slide 6: NPRR 1226 – Demand Response Monitor
The Large Flexible Load Task Force has reviewed the need for this monitor and has recommended that the aggregate of the total response being observed be published on the ERCOT website.
  ERCOT Operators would have more detail information.
  ERCOT would make sure any confidential information on loads is not exposed to the public.
NPRR 1226 requires ERCOT to publish
the aggregate demand response from each
SCED run for the last two hours in graphical
format including SCED LMPs.
Market Participants are encouraged to file
supporting comments to PRS.
LMP
Chart: Demand Response Monitor
| 120 | 115 | 110 | 105 | 100 | 95 | 90 | 85 | 80 | 75 | 70 | 65 | 60 | 55 | 50 | 45 | 40 | 35 | 30 | 25 | 20 | 15 | 10 | 5
Demand Response | 2 | 3.22 | 0.87835 | 0 | 50 | 30 | 40 | 60 | 122.6146 | 132.4155 | 149.77 | 163.1 | 189.21 | 214.21 | 208.1 | 210.24 | 243.44 | 280.75 | 348 | 575 | 775 | 879 | 863.77 | 914
System LMP | 50 | 52 | 51.22 | 49.6584 | 49.2 | 50.8328 | 53.8216 | 57.88 | 60.4191 | 62.1955 | 70.22 | 79.55 | 83.55 | 105.66 | 108.55 | 99.55 | 110.69 | 132.75 | 148 | 200 | 375 | 400 | 479 | 384.77

## Slide 7: Questions