## Slide 1
Ancillary Services Study for PUC
- TAC Update
June 24, 2024
Jeff Billo

## Slide 2: Ongoing Ancillary Services Initiatives
Consider changes to ECRS before summer 2024 (TAC request)
Consider changes to AS for 2025, including PUC to approve AS Methodology
AS Study for the Legislature
(PUC/IMM/ERCOT)
Implement DRRS
NPRR1224
NPRR1232
NPRR1222
2025 AS Methodology (July WG meetings)
Due Sept.
Effective?
NPRR1235
Effective?
Effective Jan 2025

## Slide 3: Recent Ancillary Service Quantity Changes
In general, Ancillary Services quantities have increased in recent years due to:
  Increases in variable renewable resources
  Increases in load variability
  Change in summer 2021 to conservative operations; i.e. lower risk level = higher operating reserves
  Addition of ERCOT Contingency Reserve Service (ECRS) in 2023
    Needed to address:
      Increasing net load ramps causing greater intra-hour risk
      Decreasing online reserves available to recover frequency following large unit trip

## Slide 4: Changing System Needs

## Slide 5: Ancillary Services Background
Ancillary Services in the ERCOT market serve two primary purposes
Frequency Control
Regulation (Reg-Up and Reg-Down) Responsive Reserve Service (RRS) ERCOT Contingency Reserve Service (ECRS)
Requirements based on NERC Reliability Standards: BAL-001-2 BAL-002-3 BAL-003-2
Operational Risk of Under Commitment of Resources to Meet Demand plus Unexpected Variations
ERCOT Contingency Reserve Service (ECRS) Non-Spinning Reserve Service (Non-Spin) Future: Dispatchable Reliability Reserve Service (DRRS)
Requirements based on risk analysis as described in the annual Ancillary Services Methodology

## Slide 6: ERCOT Preliminary Recommendation 1
Continue to use current mechanisms that best quantify the risks and meet applicable NERC reliability standard requirements for Regulation, RRS, and the frequency-response portion of ECRS
Change the methodology to calculate non-frequency-restoration portion of ECRS quantities and Non-Spin quantities to use a full statistical analysis of risks
  Current methodology uses a quasi-statistical approach based on combined risk percentiles but does not compute a single risk probability for each AS

## Slide 7: Monte Carlo Analysis of Reserve Need
Load Forecast Error
(Month:x, HE:y)
Solar Forecast Error
(Month:x, HE:y)
Wind Forecast Error
(Month:x, HE:y)
Distribution of Reserve Need (Month:x, HE:y)
Net-Load Forecast Error
(Month:x, HE:y)
MC Draws
Forced Outages/ Derates
(Month:x, HE:y)
Available Non-AS Headroom
(Month:x, HE:y)
MC Draws
MC Draws

## Slide 8: Full Statistical Analysis Open Questions
How to determine the correlation of risk factors? For example, weather forecast errors typically cause corresponding errors in load, wind, and solar forecasts, but are generator trips correlated to forecast errors, also? Further, is the headroom capacity of the online generation fleet correlated to other factors? What data set and how much history should be used? More years of data are generally better, but improvements in forecasting methodologies are better reflected in more recent data.
Should only historic risks be a measure for determining the AS quantities or should increases in risk due to growth in installed capacities also be taken into account? If so, how should increase in variability and uncertainty due to growth be accounted for in the methodology? Historically, as the IRR fleet’s installed capacity has increased, both variability and uncertainty in net load have increased.
What is the appropriate criteria to use for each AS type? Is the criteria simply a matter of avoiding loss of load, or should there be criteria related to avoiding entering into an EEA or a Watch due to insufficient reserves? How should avoiding the need for manual operator actions be included in the criteria?
How should temporal constraints and cumulative factors be accounted? The possibility of multiple generator trips across multiple hours (as occurred on May 13, 2022, for example) presents a risk that needs to be covered by AS. Increasingly, AS is being provided by duration-limited resources (battery energy storage). There is some risk that battery energy storage resources providing AS deplete their storage during a multi-hour forecast error event, even if they are meeting all applicable requirements. Also, AS is needed until other generators can be started or until the conditions causing the need for the reserves from AS change. All these factors present challenges when calculating the probabilistic need for AS.
How much can other types of AS reserves be counted on to address risks for a given AS product? For example, should some or all of ECRS be counted towards meeting the reserve needs covered by NSRS?
What hardware and software capabilities are needed to perform a full statistical analysis of risks?

## Slide 9: ERCOT Preliminary Recommendation 2
Examine the benefits of determining some portion of AS quantities closer to the operating day based on days-ahead forecast conditions rather than strictly through an annual calculation
Net load variability is expected to increase substantially in the future and can also differ significantly on different days and hours
The difference between true minimum quantities or typical quantities of some AS products and the quantity needed to meet reliability risk objectives for worst-case or near worst-case conditions will be greater in the future
ERCOT should work with stakeholders to reexamine the tradeoffs between the certainty of calculating AS quantities on an annual basis and the efficiency of calculating at least some portion of AS quantities closer to the operating day

## Slide 10: ERCOT’s Next Steps
Send feedback to jeff.billo@ercot.com
Board presentation in August
Workshop after TAC meeting on August 28
Final report posted to PUC by September 30
Implementation of changes is dependent on addressing open questions and software tool development
  Any changes will not be incorporated in the 2025 AS Methodology due to timing

## Slide 11
PUC

## Slide 12
Senate Bill 3 from the 87th regular Texas legislative session
Sec. 35.004. PROVISION OF TRANSMISSION SERVICE.
(g) The commission shall: (1) review the type, volume, and cost of ancillary services to determine whether those services will continue to meet the needs of the electricity market in the ERCOT power region; and (2) evaluate whether additional services are needed for reliability in the ERCOT power region while providing adequate incentives for dispatchable generation
How did we get here?

## Slide 13
June 13 Open Meeting: Commissioners extended deadlines by 1 month
June 24: TAC update-study direction
July-August-September: IMM-ERCOT-Staff continue collaboration
August 28: TAC workshop
September 30: Study filed at PUCT with Staff memo including stakeholder questions
Mid to late October: Stakeholder comments due
Second half of October: PUCT held workshop
November-December: PUCT evaluates and approves final study and recommendations
January 2025: Study including PUCT recommendations submitted to the 88th Legislature as part of the Biennial Agency Report
Staff is asking for TAC feedback on:
What should IMM and ERCOT present at the August 28 TAC workshop that would be most helpful for stakeholders to file comments at the PUCT?
Where are we going?