## Slide 1: Updating ERCOT Load Zones - Impacts on Prices and Congestion Rent
Presented by:
Potomac Economics
ERCOT Independent Market Monitor
July 15, 2024

## Slide 2: Purpose
Load Zone definitions have remained the same since 2003, even with significantly changing congestion patterns over the years
  Load growth
  New generation
  Numerous network topological changes
Starting in 2020, the ERCOT IMM has recommended re-evaluation of the Load Zones in order to minimize intra-zonal congestion and provide better incentives for demand response
Chart: Annual Total Congestion Zonal Rent ($) Millions
| 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
Cross Zone | 5704182.3596 | 8948531.6658 | 7496755.8728 | 18957789.462 | 25986390.11 | 20007606.96 | 55123547.57 | 29244631.795 | 226844770.72 | 590105372.83 | 233137497.34
Houston | 45006044.302 | 121959060.38 | 52833730.892 | 129921648.04 | 156472306.29 | 64801231.285 | 41238526.24 | 31962920.82 | 168303458.43 | 247569671.1 | 98805957.2
North | 86920560.618 | 94823601.265 | 72907211.342 | 151829928.21 | 268876257.66 | 316906320.38 | 184297240.65 | 234668456.88 | 361011913.69 | 373248431.19 | 311620817.72
South | 146322624.68 | 283618711.34 | 142476235.09 | 143193892.19 | 313090112.44 | 306740316.18 | 312123644.6 | 450668061.66 | 906870221.41 | 1101693657 | 958265793.35
West | 198003147.77 | 198846660.37 | 76704582.853 | 54094572.603 | 202408069.33 | 555248511.06 | 672547535.05 | 660277948.67 | 389159891.36 | 503412887.43 | 798387191.04

## Slide 3: Methodology
Input dataset time range is real-time 5-minute electrical bus LMPs from January 2021 to April 2024
Only used the congestion components of the LMPs
Then using the load MW at each electrical bus (the same values currently used for calculation of Load Zone LMPs), weigh the congestion components to determine a value at the substation level
Apply k-means clustering process to group substations into set number of new zones
  Randomly assign substations to a group
  Compute the centroid of the group
  Move substations to groups where the distance between the substation to the centroid is least
  Once everything is moved, recalculate the centroid of the newly formed groups
  Repeat process until no substation is moved
Distance computation:
where (xa, ya) and CCa are the coordinates and congestion component for Substation a, and (xb, yb) and CCb are the coordinates and congestion component for the centroid

## Slide 4: Clustering Process Visualization

## Slide 5: Load Zone prices between Current South and New South Zones

## Slide 6: Load Zone prices between Current West and New West Zones

## Slide 7: Load Zone prices between Current Houston and New Coast Zone

## Slide 8: Load Zone prices between Current North and New North Zone

## Slide 9: Real-Time Congestion Rent (in MM) Comparison Between Current Load Zones and New Load Zones
 | Cross Zone | West | South | Houston | North
2021 | $226.8 | $389.2 | $906.9 | $168.3 | $361.0
2022 | $590.1 | $503.4 | $1101.7 | $247.6 | $373.2
2023 | $233.1 | $798.4 | $958.3 | $98.8 | $311.6
2024 | $57.4 | $277.3 | $216.1 | $18.8 | $78.7
 | Cross Zone | FarWest | Panhandle | North | Coast | SouthCentral | South
2021 | $795.7 | $91.5 | $239.1 | $196.3 | $347.6 | $71.9 | $309.2
2022 | $1369.6 | $122.6 | $211.0 | $193.8 | $433.2 | $77.9 | $399.9
2023 | $1189.7 | $60.0 | $351.9 | $199.8 | $254.4 | $71.9 | $255.7
2024 | $336.9 | $4.3 | $140.3 | $25.7 | $31.0 | $28.2 | $82.1

## Slide 10: Real-Time Congestion Rent (in MM) Comparison For Layers with More Groups
 | Cross Zone | FarWest | Panhandle | North | Coast | South Central | South West | South
2021 | $759.5 | $91.5 | $196.3 | $194.1 | $310.1 | $82.5 | $77.3 | $340.0
2022 | $1307.2 | $122.6 | $174.9 | $191.7 | $391.6 | $42.5 | $115.7 | $461.9
2023 | $1043.1 | $60.0 | $279.0 | $200.0 | $235.4 | $121.4 | $145.8 | $298.5
2024 | $294.3 | $4.3 | $137.2 | $18.1 | $34.7 | $17.5 | $36.9 | $105.5
 | Cross Zone | FarWest | Panhandle | North | Coast | South Central | South East | South West | South
2021 | $1017.9 | $91.5 | $196.3 | $191.2 | $209.5 | $92.0 | $75.1 | $30.1 | $147.8
2022 | $1618.6 | $122.6 | $174.9 | $190.3 | $324.7 | $37.0 | $133.9 | $56.0 | $150.0
2023 | $1419.4 | $60.0 | $279.3 | $151.4 | $94.8 | $121.6 | $82.2 | $56.8 | $117.9
2024 | $328.4 | $4.3 | $137.2 | $17.7 | $24.2 | $28.4 | $20.8 | $25.2 | $62.2

## Slide 11: Load zones based on GTCs

## Slide 12: Questions?

## Slide 13: Appendix

## Slide 14: Load Zone prices between Current Zones and New Zones

## Slide 15: Load Zone prices between Current Zones and New Zones