## Slide 1
ERCOT RTC+B SCED Tool Progress Update
Jonas Kersulis
RTCBTF
July 17, 2024

## Slide 2: Outline
Production-scale tool refresher
Update on optimization details
Update on capabilities and limitations
Summary of remaining work; estimated timeline

## Slide 3: Refresher: Overview of Production-scale Tool
Resource Data
Status
Resource Type
Capacity and Ramping Limits
AS Capability and Qualification
Energy and AS Offers
Inputs
Core Optimization
Outputs
System Data
GTBD
AS Plan
ASDC parameters
MCL, VOLL
Transmission Constraints
Shift Factors
Build and solve optimization problem
Resource Outputs
LMPs
Energy Awards
AS MCPCs
AS Awards
System Outputs
System Lambda
Objective Function
Transmission Outputs
Constraint loading
Constraint shadow price
(Details on next slide)

## Slide 4: Optimization Details – Last Update
Decision Variables
Base points
AS awards
ASDC variables
Transmission slack variables
Power balance slack variables
Binary variables
  Carrying NFRC
  ESR Charge/Discharge
Objective
Minimize total system cost:
Energy award costs
AS award costs minus ASDC benefit
Transmission and overgen/undergen penalties
Constraints
Power balance
Total AS award MW = Cleared ASDC MW
Generator limits
  Capacity Limits (LSL, HSL)
  Ramp Limits (LDL, HDL)
  Max AS award (based on qualification, status, ramp capability, overrides)
  Linked AS Offers
Transmission Constraints
System-wide RRS procurement
Regulation Ramping Constraint
NFRC Conditional Constraint
SOC Conditional Constraints
In progress
Implemented
Notes: System-wide RRS procurement constraint
min of 1420 MW RRSPF
limits RRSUF and RRSFF to 60% of total
Max 450 MW RRSFF

## Slide 5: Optimization Details – Today
Decision Variables
Base points
AS awards
ASDC variables
Transmission slack variables
Power balance slack variables
Binary variables
  Carrying NFRC – Not binary after all
  ESR Charge/Discharge
Objective
Minimize total system cost:
Energy award costs
AS award costs minus ASDC benefit
Transmission and overgen/undergen penalties
Constraints
Power balance
Total AS award MW = Cleared ASDC MW
Generator limits
  Capacity Limits (LSL, HSL)
  Ramp Limits (LDL, HDL)
  Max AS award (based on qualification, status, ramp capability, overrides)
  Linked AS Offers
Transmission Constraints
System-wide RRS procurement
Regulation Ramping Constraint
NFRC Conditional Constraint
SOC Conditional Constraints
In progress
Implemented
Postponed
Notes: System-wide RRS procurement constraint
min of 1420 MW RRSPF
limits RRSUF and RRSFF to 60% of total
Max 450 MW RRSFF

## Slide 6: Capabilities and Limitations
Current Functionality
Replicate results of Excel Tool
Solve production-scale cases derived from historical SCED data
Perform non-sequential multi-interval simulation
In-Progress Functionality
Pricing run
Sequential multi-interval simulation
Improved output visualization (compare pre-RTC to RTC outcomes)
Future Functionality
ESR single model
Mitigation
Limitations
Market submission assumptions
Internal tool (ERCOT database access required)
Notes: Key milestones
- Can replicate results of 5-generator Excel Tool
- Can create a case using historical data

## Slide 7: Summary and Next Steps
Refocus on obtaining historical study results, comparing to pre-RTC outcomes.
Each remaining task on the path to historical study results is in progress.
The team is on track for study results in September, barring unforeseen issues.
Questions?