## Slide 1
Proposed 2025 Ancillary Service Methodology
Luis Hinojosa
Ancillary Services & Operations Analytics
ERCOT

## Slide 2: Introduction
ERCOT has reviewed the methodology to determine minimum Ancillary Service (AS) requirements.
ERCOT is proposing the following changes for 2025.
  Change methodology for Regulation Service, to the error in forecasting net load that is used to set dispatch target for SCED (i.e. Generation to be Dispatched (GTBD).
  Change methodology for ERCOT Contingency Reserve Service (ECRS) to (1) Remove the adjustment for risk coverage during sunset hours to be at least 90th percentile, (2) Adjust the frequency recovery portion such that it covers 70% of historic net load and inertia conditions and (3) compute the minimum ECRS requirements as the larger of the capacity needed to recover frequency and capacity needed to support net load forecast errors.
2025 Methodology Review Timeline
July 23, 2024 – WMWG
July 24, 2024 – PDCWG
August 15, 2024 – OWG (Proposed)
August 21, 2024 – PDCWG (Proposed)
August 30, 2024 – WMWG (Proposed)
September 09, 2024 – ROS
September 11, 2024 – WMS
September 15, 2024 – TAC
October 10, 2024 – BoD
Nov or Dec 2024 – PUC
  Change methodology for Non-Spinning Reserve Service (Non-Spin) quantities specifically for HE23 to HE06 to be computed using 4 Hours Ahead (HA) hourly average net load forecast error. Non-Spin quantities during rest of the hours will be based on 6 HA hourly average net load forecast error to compute Non-Spin quantities.
ERCOT is not proposing any changes in the methodologies used to compute Responsive Reserve Service.
  NERC’s preliminary BAL-003 Interconnection Frequency Response Obligation (IFRO) for Operating Year (OY) 2025 assessment for ERCOT shows a decrease in ERCOT’s IFRO. In order to align with ERCOT’s new IFRO, the minimum RRS-PFR limit for 2025 will change to 1,365 MW.
The following slides share the preliminary quantities for each AS based on the proposed methodologies.
Note that, while the quantities of each AS are set based on an analysis of certain risks, these are not necessarily the only reasons why each AS is needed.
Notes: ****************Preliminary Quantities****************************

## Slide 3: Hourly Average Regulation Comparison
Reg-Up 2025:
On avg. 77 MW increase from prev. year
Largest increase is in July by 96 MW
Reg-Up 2025 (Proposed):
On avg. 33 MW increase from prev. year
Largest increase is in July by 49 MW
Reg-Down 2025:
On avg. 68 MW increase from prev. year
Largest increase is in Jan by 83 MW
Reg-Down 2025 (Proposed):
On avg. 23 MW increase from prev. year
Largest increase is in July by 40 MW

## Slide 4: Hourly Average ECRS Comparison
2025 ECRS proposed:
On avg. 273 MW decrease compared to previous year
On avg. 517 MW decrease compared to 2025

## Slide 5: Hourly Average NSRS Comparison
2025 NSRS (6HA):
On avg. 246 MW increase from prev. year
Largest increase is in Jan by 388 MW
2025 NSRS (6HA+4HA):
On avg. 169 MW increase from prev. year
Largest increase is in Mar by 311 MW
On avg. 77 MW decrease compared to 2025 (6HA)
Largest decrease is in Feb by 189 MW

## Slide 6: Hourly Average RRS Comparison
2025 RRS:
On avg. 13 MW increase from prev. year
Largest increase is in Feb by 122 MW
Largest decrease is in Jan by 59 MW

## Slide 7: Summary
Below is a summary of the proposed changes to the methodology used for computing minimum AS quantities for 2025,
  ERCOT is proposing changes in the methodologies used to compute Regulation Service (one change), ERCOT Contingency Reserve Service (three changes) and Non-Spinning Reserve Service (one change) requirements.
  ERCOT is not proposing any changes in the methodology used to compute Responsive Reserve Service.
Spreadsheets that contain the preliminary quantities from Jan to Jul 2025 and a redline version of the AS Methodology document have been posted on today’s meeting page.
ERCOT is seeking endorsement on ERCOT’s proposed methodology for computing minimum AS quantities for 2025.