## Slide 1
TAC
September 19, 2024
Luis Hinojosa
Manager Ancillary Services & Operations Analytics
Proposed 2025 Ancillary Service Methodology Discussion

## Slide 2: Ongoing Ancillary Services Initiatives
Consider changes to ECRS before summer 2024 (TAC request)
NPRR1224
NPRR1232
AS Study for the Legislature
(PUC/IMM/ERCOT)
Due Sept. 2024
Effective?
Implement DRRS
NPRR1235
Effective?
Consider changes to AS for 2025, including PUC to approve AS Methodology
NPRR1222
2025 AS Methodology (July WG meetings)
Effective Jan 2025
Today’s Topic

## Slide 3: Introduction
To fulfill requirements in ERCOT Protocol Section 3.16, AS Methodology is reviewed annually.
Excerpts from Protocol 3.16 Standards for Determining Ancillary Service Quantities
(2) ERCOT shall, at least annually, determine with supporting data, the methodology for determining the quantity requirements for each Ancillary Service needed for reliability…
(3) The ERCOT Board shall review and recommend approval of ERCOT's methodology for determining the minimum Ancillary Service requirements… Any such recommendations require approval by the Public Utility Commission of Texas (PUCT) prior to implementation.
ERCOT kicked off 2025 AS Methodology review at TAC on June 25, 2024.
ERCOT is back today with the proposed methodology for computing minimum Ancillary Service quantities for 2025.
The following slides share details on the proposed changes.
2025 Methodology Review Timeline
July 23, 2024 – WMWG
July 24, 2024 – PDCWG
August 15, 2024 – OWG (Proposed)
August 21, 2024 – PDCWG (Proposed)
August 30, 2024 – WMWG (Proposed)
September 09, 2024 – ROS
September 11, 2024 – WMS
September 19, 2024 – TAC
October 10, 2024 – BoD
Nov or Dec 2024 – PUC
*Note that, while the quantities of each AS are set based on an analysis of certain risks, these are not necessarily the only reasons why each AS is needed.

## Slide 4: Regulation Service
    Preliminary assessments of January through July data show,
  Regulation Up: A 34 MW (~8.3%) increase in average hourly requirement vs. 2024.
    Average hourly requirement would have been 77 MW (~18.9%) higher vs. 2024 if 2024 methodology was retained.
  Regulation Down: A 23 MW (~5.9%) increase in average hourly requirement vs. 2024.
    Average hourly requirement would have been 68 MW (~17.5%) higher vs. 2024 if 2024 methodology was retained.
2025 with Current Methodology:
On avg. 77 MW (~18.9%) increase from prev. year
Largest change is in July (96 MW increase).
2025 with Proposed Methodology:
On avg. 34 MW (~8.3%) increase from prev. year
Largest change is in January (76 MW increase).
2025 with Current Methodology:
On avg. 68 MW (~17.5%) increase from prev. year
Largest change is in January (83 MW increase)
2025 with Proposed Methodology:
On avg. 23 MW (~5.9%) increase from prev. year
Largest change is in July (40 MW increase)
What is it? Capacity that is deployed every 4 seconds to balance supply and demand and maintain frequency close to 60Hz between 5-minute SCED execution.
Methodology Change: Compute Regulation Service quantities using the historic error in forecasted net load used in SCED.
    Why? Now that intra hour solar and wind forecasts are being used by SCED, Regulation deployments are used in response to errors in SCED’s net load forecast. The proposed change aligns Regulation quantity determination with issue that drives its use in Real Time.
Key Takeaway: Regulation Service quantities are increasing in 2025 vs. 2024 due to increasing intra hour net load forecast errors but would have been higher without the change in methodology.

## Slide 5: Responsive Reserve Service
What is it? Capacity that is procured to respond to low frequency events typically triggered by generating unit trips.
Methodology Summary: RRS quantities are computed using historical inertia data and studies that determine the capacity needed following a large unit trip to arrest frequency such that the criteria established by NERC’s BAL-003-2 standard is not violated.
Methodology Change: No major change in Responsive Reserve Service. Minimum RRS-PFR limit will change to 1,365 MW.
2025 with Proposed Methodology:
On avg. 9 MW (~0.3%) increase from prev. year
Largest change is in February (122 MW increase).
Key Takeaway: The RRS methodology changes in 2025 are limited to routine changes that are made to align with NERC obligations. Total RRS requirements in 2025 are similar to 2024.
Why? The minimum RRS-PFR limit change aligns this with NERC’s most recent Interconnection Frequency Response Obligation (IFRO) assignment for ERCOT.
Preliminary assessments of January through July data show, a 9 MW (~0.3%) increase in average hourly requirement vs. 2024.
Notes: 1185 to 1,365

## Slide 6: ERCOT Contingency Reserve Service (ECRS)
What is it? Capacity that can respond in 10 minutes to recover frequency, cover forecast errors or ramps and replace deployed reserves.
Methodology Change: (1) Remove the adjustment for risk coverage during sunset hours to be at least 90th percentile, (2) Adjust the frequency recovery portion such that it covers 70% of historic net load and inertia conditions and (3) compute the
2025 with Current Methodology:
On avg. 246 MW (~14.0%) increase from prev. year
Largest change is in July (369 MW increase).
2025 with Proposed Methodology:
On avg. 271 MW (~15.4%) decrease from prev. year
Largest change is in June (428 MW decrease).
minimum ECRS requirements as the larger of the capacity needed to recover frequency and capacity needed to support net load forecast.
Why? Since implementation, there have been very few situations where ERCOT has seen the need to release ECRS both for net load forecast issues and frequency recovery needs. The proposed approach, will result in setting ECRS quantities based on needs of the dominant operational risk in every hour.
Preliminary assessments of January through July data show, a 271 MW (~15.4%) decrease in average hourly requirement vs. 2024. Average hourly requirement would have been 246 MW (~14.0%) higher vs. 2024 if 2024 methodology was retained.
Key Takeaway: ECRS quantities are notably decreasing in 2025 vs. 2024 due to proposed changes in methodology that include accounting for the low likelihood of both of the primary risks ECRS addresses occurring simultaneously.

## Slide 7: Non-Spinning Reserve Service (Non-Spin)
What is it? Capacity that can be started in 30 minutes to cover forecast errors, ramps or forced outages and replace deployed reserves until additional resources can be committed.
Methodology Summary: Non-Spin quantities are computed as the capacity needed to support under-forecast errors in forecasting load and renewable generation and forced thermal resource outages.
Methodology Change? One change in
methodology to compute HE23 to HE06 Non-Spin quantities using 4 hour ahead net load forecast error.
Why? Analysis of 3.5 years of both offline capacity and committed capacity margin between 10pm and 6am have shown sufficient capacity is typically available (or can be brought online in less than 4 hours) to help address sustained net load forecast issues that may occur during these hours.
Preliminary assessments of January through July data show, a 158 MW (~5.5%) increase in average hourly requirement vs. 2024. Average hourly requirement would have been 246 MW (~8.5%) higher vs. 2024 if 2024 methodology was retained.
Key Takeaway: Non-Spin quantities are increasing in 2025 vs. 2024 due to increasing hourly net load forecast errors but would have been higher without proposed changes in methodology.
2025 with Current Methodology:
On avg. 246 MW (~8.5%) increase from prev. year
Largest change is in January (388 MW increase).
2025 with Proposed Methodology:
On avg. 158 MW (~5.5%) increase from prev. year
Largest change is in March (296 MW increase).

## Slide 8: AS Methodology Evolution Road Map
Policy
Determination
Market
Tool/ Methodology Development
2025
2026
2027
Statistical Annual AS
Full Statistical Annual AS
Updated Full Statistical Annual AS
“Closer to Op Day” AS Adjustment
Quantification Approach Used
for Year
AS Methodology
Approval
Current Market
?
RTC+B
“Annual” Full Statistical Analysis Tool Dev
“Closer to Op Day” Dynamic AS Quantity Determination Tool Dev
Policy/Criteria Development
for “Annual”
Policy/Criteria
Development
for “Closer to Op Day”
Approval
Approval
Approval
Statistical Annual AS
Q2
Q3
Q4
Q2
Q3
Q4
Q2
Q3
Q4
Q3
Q4
Current Approach
You
are
Here

## Slide 9: Summary
Below is a summary of the proposed changes to the methodology used for computing minimum AS quantities for 2025,
  ERCOT is proposing changes in the methodologies used to compute Regulation Service (one change), ERCOT Contingency Reserve Service (three changes) and Non-Spinning Reserve Service (one change) requirements.
  ERCOT is not proposing any major change in the methodology used to compute Responsive Reserve Service.
Spreadsheets that contain the preliminary quantities from January to July 2025 and a redline version of the AS Methodology document have been posted on today’s meeting page.
  Same proposed methodology will apply to August to December 2025 quantities as well. The quantities for these months can only be calculated once the corresponding 2024 months are complete.
ERCOT is seeking endorsement on ERCOT’s proposed methodology for computing minimum AS quantities for 2025.