## Slide 1
NPRR1219 Change Implementation / CDR Mockup
Pete Warnken
Resource Adequacy
Supply Analysis Working Group
October 25, 2024

## Slide 2: CDR Changes Summary
Peak Net Load Information: Planning Reserve Margin (PRMs) and associated loads and resource information will be added for the forecasted peak Net Load hour by year and season.
Shift to Effective Load Carrying Capabilities (ELCCs): Instead of using peak average capacity contributions for wind and solar resources, the CDR will now utilize ELCCs to represent their availabilities. ELCCs will also be estimated for battery energy storage systems.
Expanded Reporting Timeframe: The report will now include PRMs, associated loads, and resources for all four seasons (summer, winter, spring, and fall). Previously, only summer and winter seasons were included. The December 2024 CDR will cover the Summer and Winter seasons, whereas full seasonal reporting will be implemented for the May 2025 CDR.
Introduction of New Solar Regions: Three new solar regions (West, Far West, and Other) are introduced to enable more accurate solar capacity availability forecasts. Previously, a single system capacity availability forecast was used.
Updated Criteria for Planned Resources: The criteria for including planned resources in the CDR has been expanded to include ERCOT notification that a project developer has provided the required financial security for interconnection facility construction. See ERCOT Planning Guide Section 6.9(1)(d)(ii)(B).

## Slide 3: CDR Changes Summary, continued
Inclusion of Publicly Announced Planned Retirements: A new category for planned retirements has been added to account for Generation Resources that have a publicly announced retirement plan but haven't yet submitted a formal Notification of Suspension of Operations (NSO) to ERCOT.
Inclusion of Distribution Voltage Reduction (DVR): Distribution voltage reduction will now be included as a load-reducing adjustment for Firm Peak Load calculation.
Inclusion of Energy Storage Resources (ESRs): Existing and planned ESRs will be factored into the PRM calculations as available capacity. Battery ESRs will be categorized based on their maximum (or design) duration capabilities.
Revised Emergency Response Service (ERS) Methodology: The methodology for estimating forecasted ERS capacity has been modified to match the most recent ERS procurement amounts and allow ERCOT to make adjustments based on anticipated ERS program changes. This approach avoids unrealistic forecasted year-to-year volatility caused by averaging three-year historical ERS amounts.
Elevated Probability-of-Return Threshold for Mothballed Generation Resources: The threshold for including mothballed Generation Resources in the PRM calculations has been raised from 50% to 75%.

## Slide 4: CDR Mockup Elements
Refer to the CDR mockup Excel workbook, CDR_Mockup_NPRR1219 - DRAFT_10-25-2024.xlsx
Executive Summary to be similar to the Monthly Outlook for Resource Adequacy (MORA) reporting style
  Canned bullet format
  Suitable data visualizations
  Summarize major report changes (previously reported in Changes tab)
Four seasonal Summary tabs – Summer and Winter for Dec. CDR
The Excel seasonal Capacities tabs to be consolidated and converted into a “flat table” design like the Project Details tabs in the Generator Interconnection Status (GIS) report
  Consolidated tab to be named Unit Details
  Add new CDR STATUS and CDR RESOURCE ATTRIBUTE columns
  Facilitates convenient filtering/sorting
  Data notes are moved to the top of the tabs
New “CDR-Eligible Resources” tab (Changes tab removed)

## Slide 5: CDR Mockup Elements, continued
New Effective Load Carrying Capabilities (ELCC) tab
Modify the “Fuel Type Capacity Mix” tab to more closely match the design of the MORA’s “Capacity by Resource Category” tab
New Acronyms tab
New wind/solar county-to-region mapping tab
Tabs removed:
  Changes tab (contents moved elsewhere)
  Unconfirmed Retirement Capacity
  Fossil Fuel SODG Capacities (future integration into the Unit Details tab)
  Decommissioned Gen. Resources
    To be replaced by a separate posted report updated on a quarterly basis
Battery storage resource design durations are considered Restricted Information per NP 1.3.1.1(1)(m); the CDR will not list unit-specific durations for the time-being
New “Load and Resource Scenario” tab

## Slide 6: Implementation
Full reporting of spring and fall data will be integrated into the May 2025 CDR report
ERCOT plans to show the CDR mockup at the November 12th WMS meeting
ERCOT is evaluating the implementation of the new Unit Details tab; certain elements may need to be postponed to the May 2025 CDR due to impacts on our automated report preparation tools
As noted in the accompanying CDR mockup, development and presentation of load & resource scenarios is a “work in progress”
Update the “Notice of Unavailable Capacity for Switchable Generation Resources form” (per Section 16.5.4(2)) to include spring and fall seasons

## Slide 7: Implementation, continued
ERCOT is still planning to submit at least one additional NPRR to cover:
  Large Load treatment
  Distributed Generation resources
  PUN generator reporting and capacity availability forecasting
Additional potential changes that may be addressed in an NPRR include:
  ELCCs for thermal resources
  Price-responsive demand not already accounted for in the Long-Term Load Forecast
A timeline for future NPRRs has not been determined; much of it will depend on other NPRR implementations and associated CDR/MORA impact analysis