## Slide 1
Large Load Interconnection Status Update
Large Load Integration Team
Oct 30, 2024

## Slide 2: Large Load Queue – Past 12 Months
Changes since September Queue Update
Combination of new standalone and co-located projects, as well as several project cancelations, increased total queue capacity by 5,015 MW.
Chart: Snapshot Date
| 45219 | 45268 | 45310 | 45370 | 45414 | 45446 | 45481 | 45512 | 45543 | 45573
Standalone | 30731 | 30731 | 30764 | 32301.1 | 32805.1 | 33706.1 | 38580.6 | 42647 | 47069 | 48888
Co-Located | 8605 | 8507 | 8507 | 8507 | 8687 | 9977 | 9298 | 9868 | 9885 | 13081
 | 39336 | 39238 | 39271 | 40808.1 | 41492.1 | 43683.1 | 47878.6 | 52515 | 56954 | 61969

## Slide 3: Current Large Load Interconnection Queue
Approved to Energize – Projects that have received Approval to Energize from ERCOT Operations. NOTE: not all MWs in this category have been observed to be operational (see next slide)
Planning Studies Approved – Projects that have received ERCOT approval of required interconnection studies. Any MWs that were not approved are reclassified as No Studies Submitted.
Under ERCOT Review – Projects that have studies under review by ERCOT
No Studies Submitted – Projects that are tracked by ERCOT but that have not yet provided sufficient information for ERCOT to begin review. Additionally, MWs that were not approved by ERCOT after review of planning studies are included in this category until a path to interconnect these MWs is identified, or the customer cancels the interconnection request.
NOTE: In July 2024 ERCOT expanded the queue to include projects with projected in-service dates of 2028. Previously, projects without an in-service date were assigned a default ISD of 12/31/2027. Those projects were reassigned a default ISD of 12/31/2028.

## Slide 4: ERCOT Approvals – Past 12 Months
ERCOT Approvals Since Oct 2023 (Observations)
Total load with planning studies approved increased in Oct 2024 after temporarily decreasing earlier in the year. The past year has seen of 1,771 MW of load approved to energize.
Chart: Approved Large Load - Growth in the Past Year
| 45200 | 45261 | 45292 | 45352 | 45414 | 45446 | 45481 | 45512 | 45543 | 45573
Approved to Energize | 3926 | 4479 | 4479 | 4479 | 4479 | 5479 | 5479 | 5479 | 5496 | 5697
Planning Studies Approved | 10866 | 10751 | 9327 | 9773 | 10288 | 10259 | 9859 | 9982 | 8754 | 12401

## Slide 5: Loads Approved to Energize – By Zone & Project Type
Of the total 5,697 MW Approved to Energize,
  3,055 MW resides in LZ_WEST and 2,642 MW resides in the other load zones.
  4,622 MW consists of standalone projects and 1,075 MW consist of co-located projects.
*
* Includes LZ_NORTH, LZ_SOUTH, and LZ_HOUSTON
Chart: Approved to Energize by Project Type
| Co-Located | Standalone
Observed Non-Simultaneous Peak | 1066.4 | 2447
Remaining Approved to Energize Load | 8.6 | 2175
Chart: Approved to Energize by Load Zone
| LZ_WEST | Other
Observed Non-Simultaneous Peak | 1852 | 1662
Remaining Approved to Energize Load | 1203 | 980

## Slide 6: Loads Approved to Energize – Observations
Of the 5,697 MW that have received Approval to Energize, ERCOT has observed a non-simultaneous peak consumption of 3,514 MW.
  This is calculated as the sum of the maximum value for each individual load regardless of when that maximum occurred
  This value represents how much approved load ERCOT believes is now operational
Chart: Snapshot Date
| 45200 | 45261 | 45292 | 45352 | 45414 | 45446 | 45481 | 45512 | 45543 | 45573
Observed Non-Simultaneous Peak Load | 2379 | 2432 | 2587 | 2843.8 | 2902 | 2990.5 | 3064.6 | 3174 | 3282 | 3514
Remaining Approved to Energize Load | 1547 | 2047 | 1892 | 1635.2 | 1577 | 2488.5 | 2414.4 | 2305 | 2214 | 2183

## Slide 7: Loads Approved to Energize – Observations
ERCOT has observed a simultaneous peak consumption of 2,815 MW.
  This is the maximum value of the sum of all the individual loads
  This value is the maximum amount of large load that ERCOT has had to serve at a single point in time
Chart: Snapshot Date
| 45200 | 45261 | 45292 | 45352 | 45414 | 45446 | 45481 | 45512 | 45543 | 45573
Observed Simultaneous Peak Load | 2030 | 2265 | 2349 | 2537.8 | 2610 | 2610 | 2610 | 2815 | 2815 | 2815
Remaining Approved to Energize Load | 1896 | 2214 | 2130 | 1941.2 | 1869 | 2869 | 2869 | 2664 | 2681 | 2882

## Slide 8: Questions?
email: LargeloadInterconnection@ercot.com