## Slide 1: HEN Strawman for DRRS Design to address Resource Adequacy and PURA § 39.159(d)
Shams Siddiqi, Ph.D.
Hunt Energy Network (HEN)
(512) 619-3532
shams@crescentpower.net

## Slide 2: HEN Strawman for DRRS To Provide Resource Adequacy Consistent with PURA § 39.159(d)
HEN appreciates ERCOT’s initiative and openness to design DRRS to meet all the goals of HB1500 including to meet “a targeted reliability standard”.
Severe winter storms of long duration, with little solar and wind support, are the greatest reliability challenges for ERCOT for foreseeable future
  With ERCOT’s current suite of Ancillary Services, ERCOT meets all operational reliability needs as required by NERC and ERCOT has not identified the need for any additional AS for operational reliability
Since Performance Credit Mechanism is unlikely to move forward, DRRS may be the only tool left (and specifically provided by the legislature) to meet ERCOT’s winter Magnitude challenge in a targeted manner.
There is about 70GW of Long-duration Dispatchable Resources (LDRs) and ERCOT studies have shown about a 25GW LDR deficit to avoid firm Load Shed in a severe winter storm.
PUCT directed ERCOT at the December 19, 2024, Open Meeting to design a resource adequacy component for DRRS that could be utilized in the future.
HEN proposes modifications to ERCOT’s DRRS “Concept 1” (presented at November SAWG) to address resource adequacy to ensure LDRs are built and existing LDRs are supported at the lowest cost to consumers while simplifying implementation.

## Slide 3: Implications of the HEN Strawman Proposal
Ensures new LDRs are built at least to meet the Magnitude limit of the ERCOT market’s targeted reliability standard as required by statute while providing support to existing competitive LDRs.
Effectively reduces and/or eliminates all RUCs
Is procured both in DAM (virtual) and RTM and thus complies with the statute.
Minimizes consumer costs by bifurcating DRRS between new and existing LDRs.
Should not cause an increase in energy and AS prices since LDR capacity is not withheld from the energy and AS markets.
Even with RDPA for Offline LDR commitments by ERCOT, the significant addition of new LDRs may suppress market prices. If so, after some years of experience with DRRS, it may be necessary to revisit the ASDCs for the other AS products and AS and Energy prices caps to better align with VOLL.

## Slide 4: HEN’s Strawman DRRS Design
Procured in both DAM and Real-Time, using the same Ancillary Service Demand Curve (ASDC) but not co-optimized with other AS and Energy (simple intersection of DRRS ASDC and DRRS supply sets DRRS MCPC).
Thus, LDRs awarded DRRS can also be awarded other AS and Energy for the same capacity – ensuring no upward pressure on market prices but likely to create downward pressure – so Energy Offer Curves of LDRs must be greater than or equal to marginal cost.
Like other AS, DAM is financial and voluntary and DRRS-qualified LDRs must offer into SCED or proxy DRRS Offer Curve will be created.
DRRS qualifications:
  Dispatchable by SCED when On-line
  If Off-line, capable of starting within 2 hours
  Able to sustain their HSL for at least 12 hours in Dec-Feb and 6 hours in all other months
All Offline DRRS-qualified LDRs will submit “DRRS” COP status unless “OUT” and RUC will prioritize committing an Off-Line Resource with a “DRRS” COP status before one with an “OFF” COP status.

## Slide 5: HEN’s Strawman DRRS ASDC
To reduce consumer costs of DRRS, HEN proposes bifurcating DRRS into New LDR DRRS and Existing LDR DRRS since the cost of supporting existing LDRs is generally lower than CONE of new LDRs.
Existing LDRs are those with COD prior to a date certain (e.g., 1/1/2026) and New LDRs are those with COD after that date. Ten years after COD, New LDRs become part of Existing LDRs.
DRRS ASDC is designed to ensure recovery of PUCT-set CONE for New LDRs and competitively set cost recovery to maintain Existing LDRs.
Since meeting the winter storm challenge with LDRs is one of the goals of DRRS and this exposure is throughout the day, capacity needed to meet Magnitude of Reliability Standard sets ASDC at ASDC cap for New DRRS for every hour sloping linearly down to $0 at 150% of firm Load Shed amount.
  E.g., 25GW Load Shed exposure and 8GW Magnitude limit would imply first 17GW at ASDC cap and then linearly decreasing to $0 at 29GW.
ASDC caps for New DRRS in non-winter months add up to 10% of CONE allocated monthly blocks for hours based on LOLE.
ASDC cap for New DRRS in Dec-Feb is set just prior to Dec equal to (2 x LDR CONE minus prior 21-month LDR Net Margin)/(No. of hours in winter)
  E.g., for LDR CONE of $200/kW-yr and 21-month of LDR Net Margin of $300/kW, Dec-Feb ASDC cap = 100,000/(90x24) = $46/MW/Hour)

## Slide 6: HEN’s Strawman DRRS ASDC (cont.)
Existing DRRS ASDCs are set as follows:
  Existing DRRS ASDC cap will extend to 80% of existing LDR capacity and then the Existing DRRS ASDC would slope down linearly to $0 at 110% of existing LDR capacity.
  E.g., for 70GW existing LDR, the Existing DRRS ASDC would be at the cap for 56GW and the slope down to $0 at 77GW. This implies that all existing LDRs would be supported only if their cost of maintaining those LDRs was 33% of that of new resource. Existing ASDCs ensure that Existing DRRS MCPCs are competitively set. [Note: New DRRS MCPCs are set at the ASDC cap until New LDRs are sufficient to meet or exceed the capacity deficiency to meet the Magnitude limit.]
The proposed DRRS ASDC design ensures that existing LDRs compete to ensure DRRS award while new LDRs are assured their CONE recovery for at least 10 years until sufficient LDRs are built to address the winter storm challenge.

## Slide 7: Impact on RUC from HEN’s Proposal
RUC will commit DRRS LDRs prior to any other capacity.
ERCOT Commitment of DRRS LDR does not provide RUC make-whole payment to the LDR; however, such commitment is treated as a RUC for RDPA purposes to undo the price suppression caused by such commitment.
Since almost all LDRs would qualify for DRRS, there would likely be no RUC-related charges once DRRS is implemented – a statutory goal of DRRS.
The only way LDRs can be RUCed and receive RUC make-whole guarantee is when the LDR decides not to register as a DRRS-eligible resource.