## Slide 1: Proposal for Real-Time Procurement of Offline DRRS
Andrew Reimers, Ph.D.
Deputy Director
Potomac Economics | ERCOT IMM
SAWG
January 24, 2025

## Slide 2: Resolving the Handoff between SCED and RUC
The IMM has recommended that DRRS be allowed to be provided by both online and offline units and be co-optimized in real-time so that any shortages in the supply of DRRS are factored into price formation
With regard to offline DRRS, what is SCED actually buying each interval if the resource has to be committed by RUC, which only runs at the beginning of each hour and takes 15-30 mins to run?
Solution: implement a version of RUC with a shorter study period that can execute more quickly (appx 5 mins) on an as needed basis

## Slide 3: How Would this Quicker Instance of RUC Work?
This new version of RUC would incorporate the most recent SCED awards for offline DRRS into its commitment logic just like in ERCOT’s proposed concepts
The study period would be reduced to 4-5 hours to account for the full range of time DRRS units are required to be online per statute
The first interval of the study period would be an hour after the time at which this RUC process was initiated
Reducing the study period would reduce the solve time both by reducing the number of hourly decision variables and by implicitly ruling out commitment of resources with longer start times
Being able to run RUC quickly on an as-needed basis would make deploying offline DRRS more akin to deploying offline NSPIN, a 30-min reserve that also has to be committed outside of SCED

## Slide 4: Additional Considerations
Another concern we’ve heard regarding procuring and co-optimizing DRRS in real time relates to the two-hour start time criteria
If the two-hour start time is a concern, the statute appears to allow for reducing the start time. The statute requires that DRRS reserves “be online and dispatchable not more than two hours after being called on for deployment.”
Reducing the start time to 60-minutes could address this concern without violating the statute, has limited downsides, and has some modest upsides:
  The available offline capacity in situations in which DRRS would be deployed tends to have start-times of 60-minutes or less or greater than two hours
  A 60-minute start time could allow for an even shorter study period and quicker RUC execution time

## Slide 5: Summary of Proposal
ERCOT should implement a new, faster-running RUC process with a study period of only 4-5 hours that could be run on an as needed basis and that incorporates the most recent DRRS awards from SCED in its commitment decisions
If ERCOT still has concerns with the two-hour start time criteria, the statute allows for them to reduce the start time to 60-minutes