## Slide 1
Monthly Review of Reliability Unit Commitment Market Impacts – December 2024
Wholesale Market Working Group
ERCOT Market Analysis

## Slide 2: RUC Resource-Hours
* The difference between “Instructed” and “Effective” values is a result of Resources starting up, shutting down, receiving partial hour instructions, or otherwise not being dispatchable by SCED.
December 2024 | Total | Opt-Out | Non-Opt-Out
Instructed Resource-Hours |  |  | 
Total Count | 235 | 5 | 230
Effective Resource-Hours* |  |  | 
Total Count | 233.8 | 5 | 228.8
Average Megawatts (MW) for Effective Resource-Hours |  |  | 
Average LSL | 145.6 | 194.8 | 144.6
Average LDL | 156.6 | 240.9 | 154.8
Average BP | 160.2 | 308.4 | 157
Average HSL | 308.9 | 420.4 | 306.5

## Slide 3: RUC Instruction Reasons: Last 13 Months RUC instructions in December 2024 were primarily to resolve congestion.

## Slide 4: RUC Instruction Reasons in December 2024
233.8 RUC effective Resource-hours.
  233.8 hours (100%) for congestion.

## Slide 5: Non-opt-out and Opt-out Totals: Last 13 Months December 2024 had a total of 233.8 non-opt-out effective Resource-hours (97.86%) and 5 opt-out effective Resource-hours (2.14%).

## Slide 6: Non-opt-out and Opt-out Totals: December 2024

## Slide 7: RUC Lead Time Margin: December 2024
Lead time refers to the length of time between a RUC instruction and the start of the commitment window.
Lead time margin is the difference between lead time and the Resource’s startup time.
  In cases where a Resource is committed for multiple back-to-back time blocks, lead time margin is calculated from the first instruction.
Most RUC commitment windows (52%) had a lead time margin of 2 hours or less. However, 9 commitment windows (~33%) had lead times between 2 and 4 hours.

## Slide 8: Average Resource Age: Last 13 Months In December 2024, the average age of RUC-committed Resources was 22.3 years for non-opt-out Resource-hours and 23.5 years for opt-out Resource-hours with DAM Commitments.
Note: For Resource configurations with multiple physical generators, the age of the oldest generator is used.

## Slide 9: Age Category: Last 13 Months Most RUC-committed Resources in December 2024 were less than 10 years old.
Non-opt-out
Opt-out

## Slide 10: RUC-Instructed Resource Dispatch above LDL
December 2024
There were 14.4 effective Resource-hours in which Resources that did not successfully opt out were dispatched above their LDL.
  For 0.0 of these Resource-hours, the LMP for the RUC-instructed Resource was above the RUC offer floor.
  For 14.4 of these Resource-hours, the LMP for the RUC-instructed Resource was below the RUC offer floor.
    For these 14.4 Resource-hours, the RUC-instructed Resource was mitigated.
There were no Exceptional Fuel Cost submissions for any RUC-committed Resources.

## Slide 11: Reliability Deployment Price Adder: Last 13 Months December 2024 had a total of 167.83 RTORDPA hours with an average value of $0.38/MWh.
These graphs show RTORDPA instances by reliability action: 'RUC Only' for instances triggered solely by Reliability Unit Commitment, 'RUC and other triggers' for instances with RUC and additional triggers, and 'Other triggers only' for instances with non-RUC triggers. The daily average RTORDPA is calculated using the total duration across all categories. See ERCOT protocol section 6.5.7.3.1 for details.

## Slide 12: Reliability Deployment Price Adder: December 2024 OD 12/02 had the highest daily time-weighted average RTORDPA of $2.09/MWh.
These graphs show RTORDPA instances by reliability action: 'RUC Only' for instances triggered solely by Reliability Unit Commitment, 'RUC and other triggers' for instances with RUC and additional triggers, and 'Other triggers only' for instances with non-RUC triggers. The daily average RTORDPA is calculated using the total duration across all categories. See ERCOT protocol section 6.5.7.3.1 for more details.

## Slide 13: RUC Clawback, Make-Whole, and Shortfall For December 2024, the total Clawback Charge was $179,587. The total Make-Whole Payment was $147,386.
Of the $179,587 in Make-Whole Payments made in December 2024, $4.00 was uplifted to load due to rounding.
The remaining amount was collected through Capacity-Short Charges.
Data as of January 24th, 2025

## Slide 14: RUC Clawback by Settlement Type
Negative dollars represent a payment from ERCOT to a market participant
“-” indicates settlement has yet to be completed.
Net figures may differ slightly due to rounding.
Month | Initial Settlement ($) | Final Settlement Change ($) | True-up Settlement Change ($) | Net as of January 24, 2024 ($)
Dec ‘23 | 0 | 0 | 0 | 0
Jan ‘24 | 107,176 | -4,657 | 0 | 102,519
Feb ‘24 | 88,220 | 0 | 0 | 88,220
Mar ‘24 | 487,193 | 0 | 0 | 487,193
Apr ‘24 | 2,092,224 | 0 | -11,819 | 2,080,406
May ‘24 | 2,084,416 | 0 | 0 | 2,084,416
Jun ’24 | 58 | 0 | 0 | 58
Jul ‘24 | 47,627 | 0 | -47,627 | 0
Aug ‘24 | 73,690 | 0 | - | -
Sep ‘24 | 140,239 | 0 | - | -
Oct ‘24 | 179,331 | 0 | - | -
Nov ‘24 | 2,022,874 | 0 | - | -
Dec ‘24 | 147,389 | - | - | -

## Slide 15: RUC Make-Whole by Settlement Type
Negative dollars represent a payment from ERCOT to a market participant
“-” indicates settlement has yet to be completed.
Net figures may differ slightly due to rounding.
Month | Initial Settlement ($) | Final Settlement Change ($) | True-up Settlement Change ($) | Net as of January 24, 2024 ($)
Dec ‘23 | -5,316 | 0 | 0 | -5,316
Jan ‘24 | -253,466 | -79,942 | 31,417 | -301,990
Feb ‘24 | -19,673 | 0 | -9,004 | -28,678
Mar ‘24 | -353,562 | 0 | 0 | -353,562
Apr ‘24 | -443,178 | 0 | -35,271 | -478,449
May ‘24 | -2,957 | 0 | 0 | -2,957
Jun ’24 | -76,670 | 0 | -57,341 | -134,011
Jul ‘24 | -4,297 | 0 | -109,781 | -114,078
Aug ‘24 | -305,171 | 0 | - | -
Sep ‘24 | -239,681 | 0 | - | -
Oct ‘24 | -364,395 | 0 | - | -
Nov ‘24 | -164,191 | 0 | - | -
Dec ‘24 | -179,587 | - | - | -