## Slide 1
Update: ASDCs for use in RUC Studies
Ryan King
Manager, Market Design
RTC+B Task Force
March 5, 2025

## Slide 2: Agenda
Recap: ASDCs for RUC
Interpreting
Previous Analysis
Additional Analysis
Proposal

## Slide 3: Recap – ASDCs for RUC
NPRR 1269: RTC+B Three Parameters Policy Issues proposes the ASDCs for use in RUC be the same as those derived for the Day-Ahead Market and Real-Time Market but with the following modifications:
  ASDC for Non-Spin shall not extend beyond the AS Plan for Non-Spin
  Original filing includes of a floor price such that no values on the ASDC curve for each AS fall below $X/MWh
Floor price at the ‘tail’ of the ASDC increases the penalty cost of shortages and helps to ensure RUC better meet the AS plan.
ERCOT has been conducting sensitivity analysis using a developed basecase for testing in the vendor RUC engine to understand the impact of different floor prices on AS procurement

## Slide 4: Interpreting Results
Complex interdependencies in RUC
  RUC recommendations using a given savecase may not be identical or completely intuitive (in terms of units committed and commitment cost) due to mixed-integer problem solving complexity and iteration within a timely and efficient solving process
  Some variation in results can occur within a convergence tolerance to meet objective function
Focus on savecase results illustrate ability of RUC to resolve AS shortages while meeting overall cost-minimization objective

## Slide 5: Previous Analysis Results
 | Hour 19 System Load (MW) | NSPIN AS Plan (MW) | NSPIN Shortage (MW) | Online NSPIN Award (MW) | Offline NSPIN Award (MW) | Commit Unit # | Commitment Unit HSL
Base Case 2 | 70302 | 3164 | 108.3 | 116.6 | 2939.1 | 40 | 3086.1
Base Case 2 with $10 Floor Price | 70302 | 3164 | 18.82 | 118.88 | 3026.3 | 40 | 3086.8
Base Case 2 with $15 Floor Price | 70302 | 3164 | 0.51 | 106.78 | 3056.7 | 40 | 3087.1
Base Case 2 with $20 Floor Price | 70302 | 3164 | 0 | 110.2 | 3053.8 | 40 | 3089.5
Results (all for Hour 19) indicate that the AS Shortage can be resolved with a ASDC floor ~$15*
*presented at Feb 19 RTC+B Task Force Meeting

## Slide 6: Additional Analysis
 | Hour 19 System Load (MW) | NSPIN AS Plan (MW) | Online NSPIN Award (MW) | Offline NSPIN Award (MW) | NSPIN shortage (MW) | Commit unit # | Commitment Unit HSL
Base Case 3 | 47702 | 3164 | 875.79 | 2218.73 | 69.52 | 66 | 6879.4
Base Case 3 with $10 Floor Price | 47702 | 3164 | 874.55 | 2226.26 | 63.2 | 64 | 6703.4
Base Case 3 with $15 Floor Price | 47702 | 3164 | 714.55 | 2449.45 | 0 | 55 | 6300.5
Floor price sensitivity using a different save case from February
Results indicate that the AS Shortage can be resolved with a ASDC floor ~$15

## Slide 7: Proposal
ASDC floor of $15 per MW per hour appears sufficient to help resolve Non-Spin shortages in RUC to meet AS plan based on save case studies
  Reflected in ERCOT comments on NPRR 1269
Floor increases the penalty cost of AS shortage which can require RUC optimization to make different commitment decisions as a result
Change in the units committed enables previous committed unit HSL to be considered for Off-Line Non-Spin award awards