## Slide 1
ERCOT Workshop to Address Requirements for REP and TDSP Data Submission in conjunction with PUCT Rule 25.186
Carl L Raish
Principal Load Profiling and Modeling
April 1, 2025

## Slide 2: Overview
  Background
  Data Submission
    Initial plan
    Long term plan
  Draft NPRR
    REP participation data
    REP event data
    TDSP participation data
  Stakeholder Feedback

## Slide 3: Background
  Public Utility Regulatory Act (PURA) §39.919, as enacted by Senate Bill (SB) 1699, Section 5 by the 88th Texas Legislature, Regular Session.
  16 Texas Administrative Code (TAC) §25.186, Goal for Average Total Residential Load Reduction.
  (a) Application. This section applies to the independent organization certified under PURA §39.151 for the Electric Reliability Council of Texas (ERCOT) region, a transmission and distribution utility (TDU), and a retail electric provider (REP) providing demand response using a responsive device program to residential customers.
  (b) Definition. When used in this section, the term “smart responsive appliance or device” has the following meaning unless the context indicates otherwise. An appliance or device that may be enabled to allow its electric usage or electric usage of connected appliances or devices to be adjusted remotely.
  REPS may contract with a DR Provider.
  Participating Customers may not include those participating in ERS or TDSP Load Management.

## Slide 4: Background (continued)
  REPs must submit data to ERCOT no later than 45 days after the end of each calendar quarter.
    ESIIDs of participants
    Events: date, start-time, stop-time, ESIIDs deployed
  ERCOT must publicly file results by March 31 for 12 months ending November 30 of the previous year. For each daily ERCOT peak demand period
    Date and time of the ERCOT hourly and 15-minute peak and net peak
    The aggregated hourly and 15-minute interval load of all ESIIDs with smart devices
    For deployment days, the estimated hourly and 15-minute interval load reduction during the peak period or EEA.(for all ESIIDs and for deployed ESIIDs)
    Data filed with PUCT must exclude ESI IDs participating in ERS or TDSP Load Management programs.
  PUCT staff will deal with assessing achievement of the goal … and possibly revising it for the future
  ERCOT must treat the REP submitted data as protected information.
  Rule provides for TDSP funding of the responsive devices under the Energy Efficiency Rules.

## Slide 5: Data Submission – Initial Plan
  REPs and TDSPs will submit the required data using the ERCOT Secure File Sharing application.
    Will need to send an email to ERCOT (DRSurvey@ercot.com) with a list of email addresses to be included in the Share.
    Notification to ERCOT is required when email addresses are changed.
  File formats will be described in an NPRR to be submitted by ERCOT.
    Separate file formats for REP participant files and event files.
    TDSP participant file.
  ERCOT will perform validations on submissions and return files via the Secure Share application in three business days or less.
  Deadline for a validated file will be 45 days after the end of each calendar quarter.
  REPs and TDSPs not offering responsive device programs are required to report that status by email (DRSurvey@ercot.com) to ERCOT on or before the required submission dates for each quarter.

## Slide 6: Quarterly Residential DR Data Collection - Timeline

## Slide 7: Data Submission – Long Term Plan
  Two data submission options will be available to REPs and TDSPs.
    Continue using the Secure File Sharing application.
    NAESB option available when NPRR is approved, and system changes are implemented.
    If the Secure File Sharing application is used, email address maintenance will be required (may want to set up generic email addresses).
    If NAESB option is used, REPs/TDSPs will be required to manage access to files within their own organizations.

## Slide 8: File Naming Convention
  File names for all files used in this reporting follow the same standard except for the ‘Report-Name’ field
  The ‘Report-Name’ field is used to designate the sender and receiver of the file as well as the purpose of the file.
Data Element | Comments | Format
DUNS | REP DUNS Number | Numeric (9 or 13)
Report-Name | Varies based on contents and sender | Alphanumeric (varies)
Date/Time | File transmission date/time stamp | Datetime format = ccyymmddhhmmss
counter | Counter (optional - may be used by REP for internal tracking) | Numeric (3)
.csv | Value of .csv mandatory in file name | 

## Slide 9: File Naming Convention (continued)
  The Report Name Filed is used to designate the sender and receiver of the file as well as the purpose of the file.
Report Name | File Content | Sender/Receiver
RDPParticipant | REP Participant file | REP-to-ERCOT
RDPParticipantERCOTResponse | First-level validation file | ERCOT-to-REP
RDPParticipantERCOTValidation | Second-level validation file | ERCOT-to-REP
RDPEvent | REP Event file | REP-to-ERCOT
RDPEventERCOTResponse | First-level validation file | ERCOT-to-REP
RDPEventERCOTValidation | Second-level validation file | ERCOT-to-REP
TDLMParticipant | TDSP Load Management Participant file | TDSP-to-ERCOT
TDLMParticipantERCOTResponse | First-level validation file | ERCOT-to-TDSP
TDLMParticipantERCOTValidation | Second-level validation file | ERCOT-to-TDSP

## Slide 10: REP Participation Files (Secure Share)
Data Element | Comments | Format
ESI ID | The ESI ID is the basic identifier assigned to each Service Delivery Point (SDP). | Alpha numeric (36)
Start Date | The date the ESI ID commenced participation in the Responsive Device program. | Numeric (8) yyyymmdd
Stop Date | The date the ESI ID ended participation in the Responsive Device program. If the ESI ID is still actively participating, enter the last date of the calendar quarter. | Numeric (8) yyyymmdd
Note: Use multiple rows for an ESIID when it has discontinuous participation during a quarter.
Example Participant file
Pipe ’|’ delimited.

## Slide 11: ERCOT Participant Response/Validation Files (ERCOT-to-REP)
Data Element | Comments | Format
Record Type | Hard Code “HDR” | Alpha numeric (3)
Report Name | Hard Code “RDPParticipantERCOTValidation” | Alpha numeric (29)
Orig Report ID | Report ID as sent in the RDPParticipant file. (blank if Secure Share) | Alpha numeric
REP Duns Number | REP of record DUNS Number receiving this response report information based on the original file submission. | Numeric (9 or 13)
Header Row
Sample Validation File Contents
  Three error message types:
    Response Errors: ER1, ER2
    Validation Errors: ER3
  Three row types: HDR, ER*, SUM

## Slide 12: ERCOT Participant Response/Validation Files (ERCOT-to-REP)
Data Element | Comments | Format
Record Type | Hard Code “ER1”,”ER2” or “ER3” | Alpha numeric (3)
Record Number | The unique sequential record number starting with “1” | Numeric (8)
ESI ID | The ESI ID is the basic identifier assigned to each SDP. | Alpha numeric (36)
Original Record Type | The type of record in error. Valid values are DET, HDR, and SUM. | Alpha numeric (3)
Original Record Number | Original DET Record Number sent from RDPParticipant file that is in error. Required if Original Record Type is DET. | Numeric (8)
Field Name | Field name of record that is in error. | Alpha numeric (80)
Error Description | Description of error. | Alpha numeric (80)
Error Row

## Slide 13: ERCOT Participant Response/Validation Files (ERCOT-to-REP)
Data Element | Comments | Format
Record Type | Hard Code “SUM” | Alpha numeric (3)
Total Number of DET Records | Total number of DET records in the original RDPParticipant file. | Numeric (8)
Total Number of processed DET Records | Total number of DET records processed without error from the RDPParticipant file. | Numeric (8)
Total Number of Error Records | Total number of DET records in error. | Numeric (8)
Sum Row

## Slide 14: ERCOT Participant Response/Validation Files (ERCOT-to-REP)
Error | Long Description | Common Fixes
Invalid-ESIID | ESI ID is not in ERCOT settlement system or has an Inactive or De-energized Status for one or more days in the date range provided. | Check that all significant digits of ESI ID were entered and none inadvertently set to zero with copying/pasting processes. Check that ESI ID is a valid ESI ID and is currently active.
Not-ROR | Reporting REP is not the REP of record for one or more days in the date range provided. | Check if the submitting REP was the REP of record for ESI ID from the participation start date to the stop date inclusive. If not the REP of record, remove row.
Invalid-Dates | No days in the date range provided are in the report quarter. | Check start and stop dates of program participation. Correct the start and/or stop dates of the program for the ESI ID.
Start-Date-After-Stop-Date | Start date for the ESI ID is after the stop date provided. | Check start and stop dates of program participation. Correct the start and/or stop dates of the program for the ESI ID.
Date-Overlap | Two or more rows for the same ESIID with overlapping periods of participation. | Check start and stop dates of program participation. Correct the start and/or stop dates of the program for the ESI ID.
Duplicate-Row | Row is identical to a previous record except for sequence number | Check ESI ID Profile Type, must be ‘RES’ for all days from the Start Date to the Stop Date.
ER3 Descriptions

## Slide 15: REP Event Files (Secure Share)
Data Element | Comments | Format
ESI ID | The ESI ID is the basic identifier assigned to each Service Delivery Point (SDP). | Alpha numeric (36)
Event Date | The date the ESI ID was deployed for the Responsive Device program. | Numeric (8) yyyymmdd
Start Time | The time the load reduction event started for the ESI ID. | Military Time format = hh:mm
Stop Time | The time the load reduction event ended for the ESI ID. | Military Time format = hh:mm
Device Type Code | Code for the type of appliance or device | Alpha numeric (3)
Pre-deploy | Y or N – yes/no - was pre-cooling/pre-heating initiated prior to the event. | Alpha numeric (1)
Opt-Out | Y, N or U – yes/no/unknown - did the participant opt-out at any time during the event. | Alpha numeric (1)
Note: Use multiple rows for an ESIID when it has been deployed more than once on a day.
Example Event file
Pipe ’|’ delimited.

## Slide 16: REP Event Files
Device Type Code | Description
TST | Smart Thermostat
WH | Electric Domestic Water Heater
PP | Pool Pump.
EV | Electric Vehicle Charging.
OTH | Other Device Type
Device Type Code Descriptions

## Slide 17: ERCOT Event Response/Validation Files (ERCOT-to-REP)
Data Element | Comments | Format
Record Type | Hard Code “HDR” | Alpha numeric (3)
Report Name | Hard Code “RDPEventERCOTValidation” | Alpha numeric (23)
Orig Report ID | Report ID as sent in the RDPEvent file. (blank if Secure Share) | Alpha numeric
REP Duns Number | REP of record DUNS Number receiving this response report information based on the original file submission. | Numeric (9 or 13)
Header Row
Sample Validation File Contents
  Three error message types:
    Response Errors: ER1, ER2
    Validation Errors: ER3
  Three row types: HDR, ER*, SUM

## Slide 18: ERCOT Event Response/Validation Files (ERCOT-to-REP)
Error | Long Description | Common Fixes
Invalid-Event-Date | Event date is outside the reporting quarter | Correct the event date or if the event date is in a different quarter delete the row
Invalid-ESIID | ESI ID is not found in RDDParticipant file on event date. | Check that all significant digits of ESI ID were entered and none inadvertently set to zero with copying/pasting processes. Check whether the ESI ID has been omitted from the RDPParticipant file.
Pre-Deploy-Invalid | Pre-deploy ‘Y’ for a device type other than ‘TST’. | Pre-cooling and pre-heating are only applicable to Smart thermostats. Other device types should have pre-event set to ‘N’
Start-Time-After-Stop-Time | Event start time is later than the stop time provided. | Check start and stop dates of the event. Correct the start and/or stop times of the event for the ESI ID.
Time-Overlap | Two or more rows for the same ESIID with overlapping event periods. | Check start and stop dates of the event. Correct the start and/or stop times of the event for the ESI ID.
Duplicate-Row | Row is identical to a previous row. | Remove duplicate row..
ER3 Descriptions

## Slide 19: TDSP LM Participation Files (Secure Share)
Data Element | Comments | Format
ESI ID | The ESI ID is the basic identifier assigned to each Service Delivery Point (SDP). | Alpha numeric (36)
Start Date | The date the ESI ID commenced participation in the TDSP’s Load Management program. | Numeric (8) yyyymmdd
Stop Date | The date the ESI ID ended participation in the TDSP’s Load Management program. If the ESI ID is still actively participating, enter the last date of the calendar quarter. | Numeric (8) yyyymmdd
Note: Use multiple rows for an ESIID when it has discontinuous participation during a quarter.
Example Participant file
Pipe ’|’ delimited.

## Slide 20: ERCOT Participant Response/Validation Files (ERCOT-to-TDSP)
Data Element | Comments | Format
Record Type | Hard Code “HDR” | Alpha numeric (3)
Report Name | Hard Code “TDLMParticipantERCOTValidation” | Alpha numeric (30)
Orig Report ID | Report ID as sent in the TDLMParticipant file. (blank if Secure Share) | Alpha numeric
TDSP Duns Number | TDSP DUNS Number receiving this response report information based on the original file submission. | Numeric (9 or 13)
Header Row
Sample Validation File Contents
  Three error message types:
    Response Errors: ER1, ER2
    Validation Errors: ER3
  Three row types: HDR, ER*, SUM

## Slide 21: ERCOT TDSP Response/Validation Files (ERCOT-to-TDSP)
Data Element | Comments | Format
Record Type | Hard Code “ER1”,”ER2” or “ER3” | Alpha numeric (3)
Record Number | The unique sequential record number starting with “1” | Numeric (8)
ESI ID | The ESI ID is the basic identifier assigned to each SDP. | Alpha numeric (36)
Original Record Type | The type of record in error. Valid values are DET, HDR, and SUM. | Alpha numeric (3)
Original Record Number | Original DET Record Number sent from RDPParticipant file that is in error. Required if Original Record Type is DET. | Numeric (8)
Field Name | Field name of record that is in error. | Alpha numeric (80)
Error Description | Description of error. | Alpha numeric (80)
Error Row

## Slide 22: ERCOT TDSP Response/Validation Files (ERCOT-to-TDSP)
Data Element | Comments | Format
Record Type | Hard Code “SUM” | Alpha numeric (3)
Total Number of DET Records | Total number of DET records in the original TDLMParticipant file. | Numeric (8)
Total Number of processed DET Records | Total number of DET records processed without error from the TDLMParticipant file. | Numeric (8)
Total Number of Error Records | Total number of DET records in error. | Numeric (8)
Sum Row

## Slide 23: ERCOT Participant Response/Validation Files (ERCOT-to-TDSP)
Error | Long Description | Common Fixes
Invalid-ESIID | ESI ID is not in ERCOT settlement system or has an Inactive or De-energized for one or more days in the date range provided. | Check that all significant digits of ESI ID were entered and none inadvertently set to zero with copying/pasting processes. Check that ESI ID is a valid ESI ID and is currently active.
Invalid-Dates | No days in the date range provided are in the report quarter. | Check start and stop dates of program participation. Correct the start and/or stop dates of the program for the ESI ID.
Start-Date-After-Stop-Date | Start date for the ESI ID is after the stop date provided. | Check start and stop dates of program participation. Correct the start and/or stop dates of the program for the ESI ID.
Date-Overlap | Two or more rows for the same ESIID with overlapping periods of participation. | Check start and stop dates of program participation. Correct the start and/or stop dates of the program for the ESI ID.
Duplicate-Row | Row is identical to a previous record except for sequence number | Check ESI ID Profile Type, must be ‘RES’ for all days from the Start Date to the Stop Date.
ER3 Descriptions

## Slide 24: REP and TDSP Feedback
  ERCOT could create a REP ESIID list file (similar to the one provided for the Annual DR Survey).
    Send to all REPs ~20 days after the end of a calendar quarter
    ESIID|Start-date|Stop-date.
    Active Residential ESI IDs the REP owns for one or more days during the calendar quarter.
    REPs could use the file to pre-screen their submissions to ERCOT.
  Other items?

## Slide 25: Next Steps
  ERCOT considers workshop feedback and officially submits NPRR.
  (If needed) ERCOT sends out updated initial data submission plan.
  REPs and TDSPs send email to drsurvey@ercot.com with email addresses of people who will be involved in the data exchange process!
  REPs and TDSPs submit data.
  ERCOT validates submissions and returns response and validation files within three business days.
  First submission deadline for validated files: May 15.

## Slide 26: Questions?
ON
OFF
craish@ercot.com