## Slide 1
Load Resource Changes Implemented
With the Real-Time Co-Optimization
ERCOT Staff
RTCBTF
March 25, 2025
ERCOT Public

## Slide 2: Introduction
Key changes implemented with the RTCB project affecting Load Resources (LRs), their Resource Entities, and Qualified Scheduling Entities (QSEs)
New Terms and Concepts
Day-Ahead Market (DAM) Changes
Telemetry Changes for NCLRs and CLRs
Real-Time Market (RTM) and Operational Changes
Deployment and Recall of Load Resources
Performance Analysis
Monthly Reports
This is not an all-encompassing review of changes – Focus is on LRs

## Slide 3: New Terms and Concepts
SCED is optimizing energy and AS in real-time
Energy and AS Awards in real-time are based on telemetered information
In real-time, NCLRs can Self-Provide RRS and ECRS subject to validation rules
LRs can also participate in real-time AS markets and their AS awards are based on a valid RTM offer for AS
The SASM has been eliminated
Telemetry changes (see RTC Telemetry Changes on RTC+B Training webpage)
Proxy offers will be used in the RTM for all Resources, including LRs, when the QSE-submitted AS offers don’t cover the telemetered AS capabilities
For CLRs, Resource-specific deployments replace the QSE-level deployments
AS Imbalance remains but the specific calculations are changing (see RTC+B Settlement Overview on RTC+B Training webpage)

## Slide 4: Day-Ahead Market (DAM) Changes
LRs can participate in DAM provided they are qualified to provide the AS (no change)
Existing qualification limits to provide AS will be retained for all LRs, but new Resources will be required to demonstrate their capability through a qualification test
  No additional testing for existing LRs
ASDCs will be added to the DAM optimization and will be used in the determination of the AS quantities procured and the MCPCs
QSEs then prepare COPs to show projected Resource availability and their AS capability coming out of DAM
No Changes Required
  AS Plan posted by 06:00 in the Day-Ahead for LSE QSEs
  After DAM runs, AS Awards are published based on the DAM AS procurement
  Participation of CLRs in DAM will be similar to Generation Resources

## Slide 5: Telemetry Changes for NCLRs and CLRs
Resource status for NCLRs or CLRs will either be ONL or OUTL.
Eliminated Statuses
  ONRGL, FRRSUP, FRRSDN, ONCLR, ONRL, ONECL, and ONFFRRRSL.
Resource specific AS Responsibility and AS Schedule will be eliminated
QSE telemeters current capability to provide RRS, ECRS and Non-Spin:
  Self-Provided capacity for RRS-UFR and ECRSM w/ UFR showing as Armed
  NCLR telemeters its ECRS capability in the form of a 10-minute blended ramp rate measured as MW/min
    i.e. 3.5 MW/min = 35 MW of capability
  NCLR telemeters its Non-Spin capability in the form of a blended 30-minute Ramp Rate
    i.e. 3.5 MW/min = 105 MW of capability
ERCOT sends AS Awards via ICCP every 5 min
For CLRs, the UDBP is replaced by the UDSP
See RTC Telemetry Changes on RTC+B Training webpage
ERCOT Nodal ICCP Communications Handbook RTC+B v4.03

## Slide 6: Real Time Market and Operation for CLR and NCLRs
Comparison of Load Resource Changes to ESRs and GRs
A/S Award Type | Gen | Comb Cycle | Quick Start | Sync Cond | ESR | CLR | NCLR |  | 
Regulation | UDSP-L | UDSP-L | X | X | UDSP-L | UDSP-L |  |  | Key:
Online NonSpin | UDSP-S | UDSP-S | UDSP-S |  | UDSP-S | UDSP-S | ASM |  | ASM: AS Manager XML Dispatch
Offline NonSpin | ASM | ASM |  |  |  |  |  |  | UDSP-L: LFC telemetry dispatch
ECRSS (SCED) | UDSP-S | UDSP-S |  | Freq | UDSP-S | UDSP-S |  |  | UDSP-S: SCED Dispatch and in telemtry
ECRSM (Manual) |  |  |  |  |  |  | ASM |  | Freq: Responds to frequency
Offline ECRS |  |  | UDSP-S |  |  |  |  |  | 
RRS-PFR (inc SyncCond) | UDSP-S | UDSP-S |  | Freq | UDSP-S | UDSP-S |  |  | Notes about NCLRs: ECRS and RRS-UFR will deploy together. Can register and qualify for RRS-UFR or RRS-FFR but not both. Notes about CLRs: CLRs participate like On-Line GRs
RRS-UFR |  |  |  |  |  |  | ASM |  | 
RRS-FFR | Freq | Freq |  |  | Freq |  | ASM |  | 

## Slide 7: RTM and Operational Changes for CLRs
CLRs offer in real-time and are awarded and deployed by SCED on a resource-specific basis
PFR required if seeking qualification of RRS and/or Regulation (no change)
Required to provide PFR if qualified for RRS and/or Regulation
Need to submit offers in real-time to cover telemetered AS capabilities if showing ONL status, otherwise MMS will use a proxy offer for energy and AS
Awards and deployments will respect operating limits including MPC, LPC and ramp rates
In general, participate like a conventional GR
No Deployment or Recall Changes for CLRs

## Slide 8: RTM and Operational Changes for NCLRs
Offers, Awards and Instructions are made in real-time and are resource specific
Awards for AS will be subject to limits/constraints for each service type; e.g. additional awards for RRS-UFR
If NCLR is qualified and showing ONL, SCED will award AS using ASDCs and Resource Offers
NCLRs may Self-Provided RRS and ECRS subject to validation rules
  Under-frequency relays must be armed
  RRS and ECRS self-provided capacity cannot exceed their net Ancillary Service position for the QSE (AS awards, self-arranged AS, and AS Trades at portfolio level)
  A Resource validation against telemetered AS capabilities
Very important to watch NPC, LPC, Status and Ramp Rates
Note that awards can be partial amounts of AS (e.g. 20 MW offer; 10 MW award)
QSEs have the ability to update AS offers in real-time
SCED will use a proxy offer for AS if NCLR is showing status of ONL, has headroom, and no offer submitted or offer does not cover the amount of AS available from the NCLR

## Slide 9: Deployment and Recall for NCLRs
Manual deployment for ECRS and RRS is done like today:
  Operator dials in a MW value, e.g. 500 MW, and then the AS Deployment manager issues resource specific instructions:
  ECRSM – No relay or relay not armed, then
  ECRSM – UFR armed, then
  ECRSM and RRS-UFR – both deployed at the same time when NCLR has an armed UFR, then
  RRS-UFR
Deployment of NCLRs providing Non-Spin will be like today; manual deployment by ERCOT Operator (no change)
No Group Assignments for deployment or recall
Deployment instructions are resource specific and done by XML instruction (no change)
NCLRs need to remain deployed until recalled (no change)
Once deployed, NCLRs are subject to an Imbalance charge similar to today (no change)
Once recalled, it’s important to cover AS financial position by returning to service or covering any shortage thru allowed substitution or market trades (no change)
The 3-hour return to service was a compliance metric that has been eliminated
  AS positions for future hour are financial, so this compliance metric is no longer applicable

## Slide 10: Performance Analysis for CLRs
CLR is evaluated against UDSP instead of UDBP
Performance is based on CLREDP methodology in Section 8 of the Protocols (no change)
Evaluated for PFR response to FMEs if qualified for RRS and/or Regulation (no change)
No change to compliance metrics

## Slide 11: Performance Analysis for NCLRs
Evaluate QSE level and Resource Specific event performance from time of deployment to recall instruction (no change)
Baseline capacity uses a 5 min average of NPC prior to instruction date/time stamp (no change)
Instructed capacity is part of the XML instruction (no change)
Resource deployment performance must be greater than 95% of instructed value (no change)
Evaluation also looks at over-performance and should be less than 150% of instructed value (no change)
Can be suspended if multiple failures in a 365-day period of time (no change)
Failures fall into the following categories (no change)
  Fail to deploy based on ramp time limit
  Fail to meet the 95% minimum requirement
  Exceed the 150% limit particularly for RRS and ECRS (excess UFR response)
  Fail to remain deployed/return to service prior to getting a recall instruction
Suspensions remain the same (2 failures with 365 days and the NCLR may be suspended (no change)

## Slide 12: Reports
NCLR Deployment Performance Report for AS (NSRS, ECRS and RRS) are done monthly
  QSE Level Report is done on a pass/fail basis for each event– secure report
    Individual report for all QSEs for RRS and ECRS and then a 2nd Report for Non-Spin
  Resource specific report done for each QSE on a pass/fail basis – certified report
    Individual report for each QSE for RRS and ECRS and then a 2nd report for each QSE showing all NCLRs providing Non-Spin
CLR Deployment Performance Report for AS (NSRS, ECRS and RRS) are done monthly
  Monthly report on CLREDP performance
  Event Performance for FMEs and PFR response from CLRs (if required)
Market Participation Report for all Load Resource
  Monthly report for LR Awards in RTM providing AS, broken down by type (NCLR and CLRs), CMZ and Delivery Hour

## Slide 13: Questions and for more info contacts
Demand Integration
ERCOTLRandSODG@ercot.com
Mark Patterson
Anthony Pataray
Donald House
Franky Wong

## Slide 14: Appendix - Acronyms
Ancillary Services (AS)
Ancillary Service Demand Curve (ASDC)
Controllable Load Resource (CLR)
Current Operating Plan (COP)
Day-Ahead Market (DAM)
ERCOT Contingency Reserve Service (ECRS)
High Sustained Limit (HSL)
Load Frequency Control (LFC)
Load Resource (LR)
Load Serving Entity (LSE)
Locational Marginal Price (LMP)
Low Power Consumption (LPC) = (LSL in EMS)
Low Sustained Limit (LSL)
Max Power Consumption (MPC) = (HSL in EMS)
Market Clearing Price for Capacity (MCPC)
Net Power Consumption (NPC)
Nodal Protocol Revision Request (NPRR)
Non-Spinning Reserve Service (Non-Spin)
Operating Reserve Demand Curve (ORDC)
Qualified Scheduling Entity (QSE)
Real-Time Co-optimization (RTC)
Real-Time Market (RTM)
Regulation Down (Reg-Down)
Regulation Up (Reg-Up)
Resource Limit Calculator (RLC)
Responsive Reserve Service (RRS)
Security-Constrained Economic Dispatch (SCED)
Supplemental Ancillary Service Market (SASM)
System-Wide Offer Cap (SWOC)
Under-Frequency Relay (UFR)
Value of Lost Load (VOLL)

## Slide 15: Examples
Scenario | MPC | LPC | Self-provided RRS UFR(MW) | Self-provided ECRS (MW) | Current Capability to provide UFR (MW) | ECRS (10min) Ramp Rate (MW/min) | Non-Spin (30min) Ramp Rate (MW/min) | Question | Answers
Resource is Self-providing 25MW RRS UFR and 10MW of ECRS. They have no additional room to provide more AS. | 35 | 0 | 25 | 10 | ? | ? | 0 | Should the Current Capability to provide RRSUF and the ECRS ramp rate reflect the NCLR's total availability to provide AS (35MW), or should it reflect the total availability to provide additional AS (0MW)? | The current capability to provide UFR should indicate the resources full availability (35 MW). The ECRS ramp rate should be telemetered as a MW/min value that can be achieved in 10 minutes, in this case 35/10 = 3.5 MW. SCED will assign awards based on both telemetered values.
Resource is Self-providing 25MW RRS UFR and 10MW of ECRS. They have 10MW of additional room to provide AS. | 45 | 0 | 25 | 10 | ? | ? | 0 | If the NCLR is also qualified to provide NSRS, would SCED know the NCLR cannot provide NSRS while also Self-providing RRS+ECRS? | Yes, SCED will know the NCLR cannot provide NSRS while self-providing due to the UFR telemetered status. Current capability to provide UFR will be at least 35 MW and could be as high as 45 MW depending on their qualified MW for RRSUF. Ramp rate for ECRS = Qualified MW for RRSUF/10.
Resource is Self-providing 25MW RRS UFR and 10MW of ECRS. They have 10MW of additional room to provide AS. | 45 | 0 | 25 | 10 | ? | ? | 0 | Can the NCLR be awarded additional ECRS capacity using the extra 10 MW of available capacity | Yes, the NCLR can be awarded additional ECRS capacity based on the validation rules that will be used; e.g. no more than 50% of ECRS can be awarded to NCLRs
 |  |  |  |  |  |  |  |  | The value shown in column F should show the amount the NCLR is qualified for RRSUF. The value shown in column G should equal the value in column F divided by 10. The value shown in column H should equal the amount of Non-Spin the NCLR is qualified for divided by 30.