## Slide 1
Monthly Review of Reliability Unit Commitment Market Impacts – February 2025
Wholesale Market Working Group
ERCOT Market Analysis

## Slide 2: RUC Resource-Hours
* The difference between “Instructed” and “Effective” values is a result of Resources starting up, shutting down, receiving partial hour instructions, or otherwise not being dispatchable by SCED.
February 2025 | Total | Capacity |  | Congestion | 
 |  | Opt-Out | Non-Opt-Out | Opt-Out | Non-Opt-Out
Instructed Resource-Hours |  |  |  |  | 
Total Count | 841.4 | 25 | 388.4 | 17 | 411
Effective Resource-Hours* |  |  |  |  | 
Total Count | 803.3 | 25 | 376.2 | 17 | 385.1
Average Megawatts (MW) for Effective Resource-Hours |  |  |  |  | 
Average LSL | 110.6 | 128.7 | 106.8 | 70.6 | 114.9
Average LDL | 120.3 | 129.5 | 119.1 | 73.3 | 122.9
Average BP | 123.2 | 158.1 | 120.6 | 78.5 | 125.5
Average HSL | 314 | 266.4 | 294.3 | 242.7 | 339.6

## Slide 3: RUC Instruction Reasons: Last 13 Months RUC effective hours in February 2025 were deployed about equally to resolve congestion and ensure sufficient capacity.

## Slide 4: RUC Instruction Reasons in February 2025
803.3 RUC effective Resource-hours.
  402.1 hours (50%) for congestion.

## Slide 5: Non-opt-out and Opt-out Totals: Last 13 Months February 2025 had a total of 761.3 non-opt-out effective Resource-hours (94.8%) and 42 opt-out effective Resource-hours (5.2%).

## Slide 6: Non-opt-out and Opt-out Totals: February 2025

## Slide 7: RUC Lead Time Margin: February 2025
Lead time refers to the length of time between a RUC instruction and the start of the commitment window.
Lead time margin is the difference between lead time and the Resource’s startup time.
  In cases where a Resource is committed for multiple back-to-back time blocks, lead time margin is calculated from the first instruction.
Most RUC commitment windows (83%) had a lead time margin of 2 hours or less.

## Slide 8: Average Resource Age: Last 13 Months In February 2025, the average age of RUC-committed Resources was 48.3 years for Non-opt-out Resource-hours and 37.4 years for Opt-out Resource-hours with DAM Commitments.
Note: For Resource configurations with multiple physical generators, the age of the oldest generator is used.

## Slide 9: Age Category: Last 13 Months In February 2025, most RUC Effective Resource-Hours (60%) were provided by resources that were more than 50 years old.
Non-opt-out
Opt-out

## Slide 10: RUC-Instructed Resource Dispatch above LDL
February 2025
There were 59.5 effective Resource-hours in which Resources that did not successfully opt out were dispatched above their LDL.
  For 34.2 of these Resource-hours, the LMP for the RUC-instructed Resource was above the RUC offer floor.
  For 25.3 of these Resource-hours, the LMP for the RUC-instructed Resource was below the RUC offer floor.
    For all of these 25.3 Resource-hours, the RUC-instructed Resource was mitigated.
There were no Exceptional Fuel Cost submissions for any RUC-committed Resources.

## Slide 11: Reliability Deployment Price Adder: Last 13 Months February 2025 had a total of 213.57 RTORDPA hours with an average value of $3.90/MWh.
These graphs show RTORDPA instances by reliability action: 'RUC Only' for instances triggered solely by Reliability Unit Commitment, 'RUC and other triggers' for instances with RUC and additional triggers, and 'Other triggers only' for instances with non-RUC triggers. The daily average RTORDPA is calculated using the total duration across all categories. See ERCOT protocol section 6.5.7.3.1 for details.

## Slide 12: Reliability Deployment Price Adder: February 2025 OD 02/21 had the highest daily time-weighted average RTORDPA of $9.96/MWh.
These graphs show RTORDPA instances by reliability action: 'RUC Only' for instances triggered solely by Reliability Unit Commitment, 'RUC and other triggers' for instances with RUC and additional triggers, and 'Other triggers only' for instances with non-RUC triggers. The daily average RTORDPA is calculated using the total duration across all categories. See ERCOT protocol section 6.5.7.3.1 for more details.

## Slide 13: RUC Clawback, Make-Whole, and Shortfall For February 2025, the total Clawback Charge was $3,272,312. The total Make-Whole Payment was $1,198,579.
Of the $1,198,579 in Make-Whole Payments made in February 2025, $1.51 was uplifted to load due to rounding.
The remaining amount was collected through Capacity-Short Charges.
Data as of February 18th, 2025

## Slide 14: RUC Clawback by Settlement Type
Negative dollars represent a payment from ERCOT to a market participant
“-” indicates settlement has yet to be completed.
Net figures may differ slightly due to rounding.
Month | Initial Settlement ($) | Final Settlement Change ($) | True-up Settlement Change ($) | Net as of March 10, 2025 ($)
Feb ‘24 | 88,220 | 0 | 0 | 88,220
Mar ‘24 | 487,193 | 0 | 0 | 487193
Apr ‘24 | 2,092,224 | 0 | -11,819 | 2,080,405
May ‘24 | 2,084,416 | 0 | 0 | 2,084,416
Jun ’24 | 58 | 0 | 0 | 58
Jul ‘24 | 47,627 | 0 | -47,627 | 0
Aug ‘24 | 73,690 | 0 | 0 | 73,690
Sep ‘24 | 140,239 | 0 | 0 | 140,239
Oct ‘24 | 179,331 | 0 | - | -
Nov ‘24 | 2,022,874 | 0 | - | -
Dec ‘24 | 147,389 | -3 | - | -
Jan ‘25 | 1,037,717 | 0 | - | -
Feb ‘25 | 3,272,312 | - | - | -

## Slide 15: RUC Make-Whole by Settlement Type
Negative dollars represent a payment from ERCOT to a market participant
“-” indicates settlement has yet to be completed.
Net figures may differ slightly due to rounding.
Month | Initial Settlement ($) | Final Settlement Change ($) | True-up Settlement Change ($) | Net as of March 10, 2025 ($)
Feb ‘24 | -19,673 | 0 | -9,004 | -28,678
Mar ‘24 | -353,562 | 0 | 0 | -353,562
Apr ‘24 | -443,178 | 0 | -35,271 | -478,449
May ‘24 | -2,957 | 0 | 0 | -2,957
Jun ’24 | -76,670 | 0 | -57,341 | -134,011
Jul ‘24 | -4,297 | 0 | -109,781 | -114,078
Aug ‘24 | -305,171 | 0 | 0 | -305,171
Sep ‘24 | -239,681 | 0 | 0 | -239,681
Oct ‘24 | -364,395 | 0 | - | -
Nov ‘24 | -164,191 | 0 | - | -
Dec ‘24 | -179,587 | 0 | - | -
Jan ‘25 | -834,867 | -26,923 | - | -
Feb ‘25 | -1,198,579 | - | - | -