## Slide 1
NCLRs in Real-Time Energy and AS Imbalance
Ryan King
Manager, Market Design
WMS
April 2, 2025

## Slide 2: Agenda
During ADER Pilot discussion at the March 5, 2025 WMS, stakeholders asked for additional information on the settlement treatment of Non-Controllable Load Resources (NCLRs)
Next slides provide a high-level overview of how NCLRs carrying AS are assessed in real-time Energy and Ancillary Service imbalance

## Slide 3: NCLR Overview
Non-Controllable Load Resources – Blocky loads with both a 10-minute ramp capability for manual deployments and automatic deployment through Under Frequency Relay
NCLRs are able to offer and get awarded Ancillary Services (AS) in the DAM (QSEs can self-arrange AS on NCLRs subject to certain % limits)
  QSEs can also assign AS responsibility to NCLRs in real-time subject to certain requirements (e.g., cannot carry both RRS and NSRS on the same resource)
  NCLRs are considered to provide a reserve supply in Real-Time only when carrying an Ancillary Service
Not in SCED: no energy bids to buy, no base point instructions (settled as real-time adjusted metered load)
NCLRs are settled in Real-Time Energy and AS imbalance
  Slides (6-8) will illustrate settlement treatment under different scenarios

## Slide 4: Real-Time Ancillary Service Imbalance
[(On-Line Reserve Supplies – On-Line Reserve Obligations)*On-Line Reserve Price
+
(Off-Line Reserve Supplies – Off-Line Reserve Obligations)*Off-Line Reserve Price]
Concept
  RT AS imbalance is a charge or payment based on the imbalance between available capacity and Ancillary Service Reserves
  Applies to all QSEs that have Resource Capacity available to ERCOT during Real-Time

## Slide 5: Examples
Next slides will use examples to illustrate settlement treatment of NCLRs under different scenarios
Purpose is to clarify how NCLRs are settled today in real-time energy and AS imbalance and to make clear there is no extra ‘energy payment’ when a NCLR is deployed for AS

## Slide 6: Real-Time Ancillary Service Imbalance
Energy Consumed
AS Capacity
LSL
Charged in Real-Time Energy Imbalance
Price: RTSPP
Paid in DAM or SASM
Price: MCPC
Case 1: QSE with AS Responsibility from DAM award
NCLR QSE will be charged real-time energy imbalance for all energy consumed
QSE was already paid for AS capacity in DAM (or SASM)
HSL

## Slide 7: Real-Time Ancillary Service Imbalance
Energy Consumed
AS Deployed
LSL
Charged in Real-Time Energy Imbalance
Price: RTSPP
Charged in Real-Time AS Imbalance
Price: On-Line Reserve Price
Case 2: AS Deployed
QSE will be charged for the deployed AS capacity through Real-Time Ancillary Service imbalance
Will effectively buy back their reserve obligation at the On-Line Reserve Price
When AS is deployed on NCLR, they will be avoiding the energy costs associated with servicing the load (no extra energy payment for deployed MW)
By charging the QSE the On-Line Reserve Price for deployed capacity, QSE is only allowed to avoid LMP component of energy costs
HSL

## Slide 8: Real-Time Ancillary Service Imbalance
Energy Consumed
AS Deployed
LSL
Charged in Real-Time Energy Imbalance
Price: RTSPP
Charged in Real-Time AS Imbalance
Price: On-Line Reserve Price
Case 3: AS Deployed but Energy purchased in DAM
QSE will be charged for the deployed AS capacity through Real-Time Ancillary Service imbalance
Will effectively buy back their reserve obligation at the On-Line Reserve Price but will also be paid in Real-Time Energy Imbalance for MWs purchased in DAM
HSL
Paid in Real-Time Energy Imbalance (if purchased in the DAM)

## Slide 9: Summary
For NCLR Resources
QSE will be charged in real-time energy imbalance for all MWs consumed
QSE paid in the DAM/SASM for any AS awards
QSE charged in RT AS imbalance for deployed AS capacity
When AS is deployed on NCLR, they will be avoiding the energy costs associated with servicing the load (no extra energy payment for deployed MW even if QSE for NCLR is a third party)
  By charging the QSE the On-Line Reserve Price for deployed capacity, QSE is only allowed to avoid LMP component of energy costs