## Slide 1
Long-term Load Forecast Update
for 2025
Sam Morris
Manager, Load Forecasting and Analysis
TAC 04/23/25

## Slide 2: Overview
Waterfall Methodology
Annual Energy and Peak Relationship
TSP Provided Loads
ERCOT Methodology for Adjustments
Outage Planning Forecast

## Slide 3
TSP-Provided Load Forecasting Process
Potential
ERCOT LOAD FORECAST
Base Economic Forecast
Electric Vehicle forecast plus existing Crypto Site Load growth minus Rooftop Photovoltaic
Executed Customer Agreements
Credible 3rd Party Forecasts (e.g., S&P Global oil and gas)
TSP Officer Attested Letters New
Key Takeaways:
Most impactful difference between the HB5066 process and ERCOT’s previous Load forecasting process is that ERCOT must accept TSP Officer Attested Letters as reasonable.
ERCOT is beginning to have actual Load to verify forecasts provided in TSP officer attested Load category.
EXISTING LOAD
Transmission
Service Providers
(TSPs)
Notes: SME: Woody Rickerson
Created: February 2025

## Slide 4: Waterfall Methodology
Base Forecast = Base Economic Forecast + EV Forecast + LFL Forecast – PV Forecast
TSP Provided and ERCOT Adjusted then add Contracts and Officer Letter Load Projection

## Slide 5: Annual Energy and Peak Relationship
*Summer Peak 2024 was 85,199 MW
Chart: Annual Energy and Summer Peak Comparison
| 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035
Historical Annual Energy | 279859.6871 | 284353.9065 | 288361.9987 | 298432.4753 | 304957.9249 | 306569.309 | 310833.7322 | 307366.3563 | 318268.5325 | 333968.6178 | 324986.4682 | 331715.6797 | 340115.3201 | 347470.2521 | 351344.2118 | 357227.0858 | 376506.7889 | 384318.668 | 382572.9108 | 396848.4302 | 431665.1289 | 444548.9592 | 461491.6918
Forecast Annual Energy | 485897 | 558121 | 648140 | 794921 | 889465 | 983796 | 1037742 | 1080964 | 1098875 | 1118552 | 1136971
Historical Peak | 56068.0162 | 60029.6626 | 58483.7006 | 60212.6796 | 62202.8028 | 62114.7508 | 62102.9637 | 63407.1899 | 65713.4485 | 68317.6698 | 66557.7818 | 67252.9949 | 66464.0643 | 69620.4076 | 71092.6092 | 69496.2398 | 73308.1534 | 74665.5795 | 74327.8368 | 73650.5735 | 80037.836 | 85464.1164 | 85198.85
Forecast Peak | 85758.65 | 94650.257 | 104294.638 | 121543.449 | 128850.719 | 138944.358 | 144521.884 | 148566.875 | 149845.644 | 152229.85 | 154077.121

## Slide 6: TSP Provided Load Forecast Comparison of Demand (2024 to 2025)

## Slide 7: 2025 TSP-Provided Load Forecast Breakdown by Type
Key Takeaway: New Data Centers continue to be the major area of new growth in the 2025 TSP-Provided Load forecast.
208 GW
218 GW
197 GW
173 GW
138 GW
109 GW
94GW

## Slide 8: Forecast Methodologies
Key Takeaway: ERCOT will begin incorporating an adjusted Load Forecast in analysis that uses historic trends to adjust the TSP-Provided Load Forecast. (All displayed peaks use the 90th percentile base forecast)
TSP-Provided Load Forecast
All contracts and Officer Letter Loads based on the in-service dates and MWs that the TSPs provided
ERCOT Adjusted Load Forecast –
180 Day delay for all contract and Officer Letter Load
All new Data Center Load reduced to 49.8% of request
Then Officer Letter Load reduced to 55.4% of request
Pre-2024 Load Forecast Method
Contracts only on the ramp schedule provided by the TSPs

## Slide 9: 2025 ERCOT Adjusted Load Forecast Breakdown by Type
Key Takeaway: After adjustments, Data Center Load remains the largest growth by type.
2025 TSP-Provided LTLF
109 GW
138GW
173 GW
197 GW
208 GW
218 GW
94 GW
130 GW to 148 GW range used in 2024 Regional Transmission Plan for forecast year 2030
130 GW
148 GW

## Slide 10: Use of ERCOT Adjusted Load Forecast
The ERCOT Adjusted Load Forecast will be utilized in the following areas:
Capacity Demand and Reserves (CDR) Report – Beginning with the May 2025 CDR, ERCOT will utilize the ERCOT Adjusted Load Forecast for developing the Planning Reserve Margin. Additional scenarios will capture the TSP-Provided Load Forecast for comparison purposes.
Regional Transmission Plan (RTP) – To develop the annual regional transmission roadmap and support NERC transmission planning obligations, ERCOT will utilize the ERCOT Adjusted Load Forecast. ERCOT is beginning discussions with Market Participants on how to incorporate the TSP-Provided Load Forecast into longer term transmission planning analysis.
Regional Planning Group (RPG) Projects – ERCOT analysis will begin with the Adjusted Load Forecast; however, the TSP-Provided Load Forecast will be accepted in the RPG review process.
Resource Outage Scheduling – ERCOT has initiated changes to how the Maximum Daily Resource Planned Outage Capacity (MDRPOC) is calculated. Once those changes are approved, the MDRPOC would be updated based on the ERCOT Adjusted Load Forecast.

## Slide 11: 90th Percentile Forecast for Outage Studies
A forecast of the weekly 90th peak going out 24 months.
Starting with the 90th Percentile ERCOT Forecast. (Base + EV + LFL – PV)
For the first 180 days the large load additions are from the Large Load Interconnection Que are used in place of the contracts and officer letters provided by the TSP’s.
After the first 180 Days the forecast reverts to the ERCOT Adjusted Forecast.
Begin_Date | End_Date | Peak_Date | Peak_Hour | COAST | EAST | FWEST | NCENT | NORTH | SCENT | SOUTH | WEST | ERCOT
4-May-25 | 10-May-25 | 9-May-25 | 17 | 19575.80 | 2604.56 | 7696.41 | 22292.66 | 2175.39 | 13878.67 | 6514.12 | 1881.46 | 76619.08
11-May-25 | 17-May-25 | 16-May-25 | 18 | 20126.51 | 2490.98 | 7877.37 | 20662.85 | 2037.11 | 13928.77 | 6567.19 | 1882.11 | 75572.89
18-May-25 | 24-May-25 | 18-May-25 | 18 | 19980.59 | 2560.84 | 7908.00 | 23057.20 | 2235.36 | 14434.96 | 6423.73 | 1958.74 | 78559.42
25-May-25 | 31-May-25 | 27-May-25 | 18 | 20580.94 | 2558.23 | 8001.28 | 23093.48 | 2284.12 | 14442.29 | 6770.29 | 1945.05 | 79675.68
1-Jun-25 | 7-Jun-25 | 6-Jun-25 | 17 | 20436.77 | 2725.35 | 7020.18 | 24391.00 | 1962.00 | 14241.61 | 6786.77 | 1971.07 | 79534.76
8-Jun-25 | 14-Jun-25 | 13-Jun-25 | 17 | 20760.57 | 2825.28 | 7061.65 | 25848.90 | 2047.41 | 14074.81 | 6708.41 | 1987.21 | 81314.23
15-Jun-25 | 21-Jun-25 | 20-Jun-25 | 17 | 20710.48 | 2839.48 | 7093.55 | 26012.74 | 2010.90 | 14020.44 | 6785.01 | 1976.29 | 81448.89
22-Jun-25 | 28-Jun-25 | 26-Jun-25 | 16 | 21135.80 | 2832.48 | 7054.87 | 26027.15 | 2100.31 | 14717.33 | 6924.98 | 1970.64 | 82763.58
29-Jun-25 | 5-Jul-25 | 3-Jul-25 | 17 | 20948.85 | 2870.23 | 7437.04 | 25387.11 | 1994.94 | 14212.06 | 6667.88 | 1976.10 | 81494.22
6-Jul-25 | 12-Jul-25 | 8-Jul-25 | 17 | 20933.48 | 2856.33 | 7490.45 | 26018.82 | 2055.31 | 14341.16 | 6807.06 | 2053.62 | 82556.23
13-Jul-25 | 19-Jul-25 | 13-Jul-25 | 18 | 21231.93 | 2920.13 | 7490.63 | 26563.26 | 2102.56 | 14798.22 | 6850.14 | 2057.98 | 84014.85
20-Jul-25 | 26-Jul-25 | 20-Jul-25 | 18 | 20940.76 | 2869.58 | 7501.46 | 26845.28 | 2084.62 | 14438.96 | 6739.93 | 2092.72 | 83513.31
27-Jul-25 | 2-Aug-25 | 1-Aug-25 | 17 | 21361.21 | 2965.27 | 7530.62 | 27542.47 | 2154.71 | 14799.40 | 7000.92 | 2037.39 | 85391.99
3-Aug-25 | 9-Aug-25 | 3-Aug-25 | 18 | 21511.02 | 2960.95 | 7633.23 | 27536.33 | 2151.25 | 14745.13 | 6903.96 | 2090.28 | 85532.15
10-Aug-25 | 16-Aug-25 | 10-Aug-25 | 17 | 21649.61 | 3000.82 | 7588.40 | 27658.64 | 2105.37 | 14604.74 | 6988.19 | 2078.90 | 85674.66
17-Aug-25 | 23-Aug-25 | 19-Aug-25 | 17 | 21866.68 | 2914.33 | 7583.94 | 26289.99 | 2055.72 | 14770.54 | 7041.42 | 2029.69 | 84552.31
24-Aug-25 | 30-Aug-25 | 29-Aug-25 | 17 | 22132.93 | 2902.54 | 8738.67 | 26078.10 | 4595.26 | 15659.73 | 8054.81 | 2918.13 | 91080.18
31-Aug-25 | 6-Sep-25 | 31-Aug-25 | 17 | 21822.20 | 2928.26 | 8772.68 | 26260.32 | 4674.18 | 15421.47 | 7774.95 | 2939.75 | 90593.82
7-Sep-25 | 13-Sep-25 | 7-Sep-25 | 17 | 20424.88 | 2729.11 | 8719.60 | 25379.96 | 4628.18 | 14946.19 | 7540.24 | 2911.22 | 87279.38
14-Sep-25 | 20-Sep-25 | 14-Sep-25 | 17 | 20468.15 | 2740.86 | 8710.91 | 23421.40 | 4467.49 | 14820.76 | 7301.94 | 2868.67 | 84800.18
21-Sep-25 | 27-Sep-25 | 25-Sep-25 | 17 | 20060.44 | 2598.99 | 8655.37 | 23297.58 | 4477.96 | 14788.07 | 7385.42 | 2798.02 | 84061.83
28-Sep-25 | 4-Oct-25 | 1-Oct-25 | 17 | 19167.94 | 2488.06 | 9849.35 | 22224.75 | 4702.21 | 15048.95 | 7111.75 | 2723.29 | 83316.30
5-Oct-25 | 11-Oct-25 | 7-Oct-25 | 17 | 19038.86 | 2421.24 | 9827.91 | 21832.71 | 4701.91 | 14727.73 | 7121.33 | 2784.01 | 82455.71

## Slide 12: Forecast Postings
https://www.ercot.com/gridinfo/load/forecast/