## Slide 1
NDCRC – RTC+B Changes
Nick Barbas
April 24, 2025

## Slide 2: NDCRC – RTC+B
Timeline Update
  NDCRC RTC+B release planned for production in December 2025 to incorporate changes supporting the submission of test data for single model ESRs
  Project is in execution phase with a release candidate currently deployed to test environment at ERCOT

## Slide 3: NDCRC – RTC+B
Reactive Test Changes
  Launching a new ESR specific version of the reactive test that’s similar to existing MVAR/IRR versions of the form with the following notable changes
  Only allows selection of single model ESR units
  Displays two separate sets of CURL points for discharging and charging rather than a single set like existing reactive tests
  “CURL Points (Charge)” section expects negative “Megawatt” values
  The 3 separate tests to gather metrics on are now classified as “Test 1a (15 min)”, “Test 1b (15 min)”, and “Lagging Test 2 (1 hr)”
  VSS Validation section of form adds “Max Net Discharge Power” and “Max Net Charge Power” fields

## Slide 4: NDCRC – RTC+B

## Slide 5: NDCRC – RTC+B

## Slide 6: NDCRC – RTC+B

## Slide 7: NDCRC – RTC+B
AVR Test Changes
  Users are expected to use the existing version of the form to submit single model AVR tests, unlike the reactive test
  New field added to form called “AVR Test Category” with values “ESR Charging”, “ESR Discharging”, and “Normal”

## Slide 8: NDCRC – RTC+B

## Slide 9: NDCRC – RTC+B
Unit Changes - Database
  Units with the designation “PWRSTR” (power storage) representing the generation side of a combo model ESR will be removed
  Units with the designation “CLR” (controllable load resource) representing the load side of a combo model ESR will be removed, but other CLRs outside of combo model ESRs will remain in the database
  New units with the designation “ESR” (energy storage resource) will be added to the database to replace the removed “PWRSTR”/”CLR” combo model units
  Naming convention for “ESR” units are “STATION_ESR1”, “STATION_ESR2”…

## Slide 10: NDCRC – RTC+B
Unit Changes – Existing NDCRC Forms
  CT Freq. Resp. – exclude single model ESRs from unit list
  ESR Freq. Resp. – only show single model ESRs in unit list
  CLR Freq. Resp. – only show CLRs that aren’t part of a combo model ESR
  Turbine Mech-Hydr. – exclude single model ESRs from unit list
  Turbine Electro-Hydr. – exclude single model ESRs from unit list
  Historical Freq. Resp. – exclude single model ESRs from unit list
  ESR Historical Freq. Resp. – only show single model ESRs in unit list
  Unannounced Seasonal HSL – exclude single model ESRs from unit list