## Slide 1
Self-Provisioning for Load Resources with
Under-Frequency Relays (UFRs)
ERCOT Staff
DSWG
May 12, 2025
ERCOT Public

## Slide 2: Introduction to Self-Provision
What is self provision?
  Self-provision is a new concept in RTC+B where QSEs have the option to cover their Ancillary Service (AS) position with load resources that operate with an Under Frequency Relay (UFR)
    If the QSE has a responsibility at the end of the adjustment period, the QSE can telemeter self-provision amount to ensure AS responsibility are awarded/met in real time
    (Day Ahead AS Awards + Day Ahead Self Arranged AS + net of AS Trades Sold – AS Trades Purchased)
  *Different than self-arrangement*
Who does self-provision apply to?
  NCLRs that are qualified for AS that operate utilizing an armed UFR:
    RRS UFR
    RRS FFR
    ECRS resources with a UFR
When can a Load Resource that is not a Controllable Load Resource (CLR) self-provide AS?
  Self-provision is resource-specific and managed in real time through telemetry, which is set by the QSE.
Why was self-provision created?
  Self-provision was introduced in response to Market Participant concerns about frequent AS reassignments during real-time operations. It was developed to prevent the constant arming and disarming of UFRs

## Slide 3: Self-Arrangement vs Self-Provision
Self-Arrangement
  Applies to the Day-Ahead Market (DAM)
  Allows QSEs with Ancillary Service (AS) obligations to procure AS on their own
  Prevents ERCOT from purchasing AS on their behalf in DAM
  Process remains unchanged under Real-Time Co-Optimization (RTC)
Self-provision
  Self-provision in the Real-Time Market (RTM) applies to AS suppliers using under-frequency relays
  Intended to reduce AS reassignments during real-time operations
  Helps avoid the need to frequently arm or disarm relays
  New concept under Real-Time Co-optimization (RTC)

## Slide 4: Self-Provision Achieved via Telemetry Points
QSEs will be able to self-provide in real-time via telemetered ICCP points
LEGEND
ICCP Change Request Example RTC+B V1.4 on RTC ERCOT webpage

## Slide 5: Validation Rules of Self-Provision
NCLRs may self-provide high-set under-frequency relay-controlled RRS and ECRS subject to the following validation rules:
  Under-frequency relays must be armed
  Load Resources are validated against telemetered AS capabilities
  The amount of RRS and ECRS a QSE self-provides must not be more than the QSEs total Ancillary Service position (including awards, self-arranged amounts, and trades)

## Slide 6: Self-Provision Scenarios
For the next few example scenarios, please assume the following:
  All load resources are fully qualified for RRS UFR, RRS FFR and ECRS operating with a UFR
  All load resources have standard/acceptable offers submitted to SCED in real time
  All ECRS Awards in this set of scenarios are for ECRS operating with a UFR

## Slide 7: Scenario 1
Scenario ** Assume AS qualified for All Headroom (NPF-LPC) | MPC | NPF | LPC | RST | UFR | Self-provided RRS UFR(MW) | Self-provided ECRS (MW) | Current Capability to provide UFR (MW) | ECRS (10min) Ramp Rate (MW/min) | RRS UFR AS Award | ECRS AS Award | Notes
NCLR_1 is qualified to provide 15 MW. DAM awards NCLR_1 with 10MW RRS. QSE also has additional 5MW RRS Position via RRS Trades. | 15 | 15 | 0 | ONL | Arm | 15 | 0 | 15 | 0 | 15 | 0 | NCLR_1 Telemetry needs to show: Status = ONL, MPC >= NPF >= 15 MW, NPF-LPC >= 15 MW, RRS capability >= 15 MW, RRS self-provided telemetry = 15 MW SCED will respect the 15 MW self-provided RRS and award the resource 15 MW RRS UFR.
QSE to ERCOT Telemetry
ERCOT to QSE ICCP
NCLR_1 has a 15 MW RRS AS Position, 10 MW from DAM award and 5 MW from RRS Trade

## Slide 8: Scenario 2 and 3
Scenario ** Assume AS qualified for All Headroom (NPF-LPC) | MPC | NPF | LPC | RST | UFR | Self-provided RRS UFR(MW) | Self-provided ECRS (MW) | Current Capability to provide UFR (MW) | ECRS (10min) Ramp Rate (MW/min) | RRS UFR AS Award | ECRS AS Award | Notes
NCLR_2 has NO HEADROOM and the following AS positions: 25 MW of RRS 10 MW of ECRS | 35 | 35 | 0 | ONL | Arm | 25 | 10 | 25 | 1 | 25 | 10 | NCLR_2 is telemetering enough capability (NPF-LPC) to cover its self-provided amounts, and enough capability to meet its self-provided telemetered amounts. The resource is awarded 25 MW of RRS and 10 MW of ECRS.
NCLR_3 HAS headroom and the following AS positions: 10 MW of RRS 25 MW of ECRS | 50 | 50 | 0 | ONL | Arm | 10 | 25 | 25 | 2.5 | 10~25 | 25 | NCLR_3 has 15 additional MW of capacity. The resource will be awarded at least 10 MW of RRS as it is self-providing 10 MW. In this scenario the resource is awarded 10-25 MW of RRS due to additional capacity telemetered. NCLR_3 is awarded 25 MW of ECRS as it is telemetering 25 MW of capability and self-providing 25 MW of ECRS.
QSE to ERCOT Telemetry
ERCOT to QSE ICCP
NCLR_2 has AS Positions of 25 MW RRS and 10 MW of ECRS with no additional room to provide AS.
NCLR_3 has AS Positions of 10 MW RRS and 25 MW of ECRS with additional headroom to provide AS.

## Slide 9: Scenario 4
Scenario ** Assume AS qualified for All Headroom (NPF-LPC) | MPC | NPF | LPC | RST | UFR | Self-provided RRS UFR(MW) | Self-provided ECRS (MW) | Current Capability to provide UFR (MW) | ECRS (10min) Ramp Rate (MW/min) | RRS UFR AS Award | ECRS AS Award | Notes
NCLR_4 carries 30 MW of self-provision | 45 | 45 | 5 | ONL | Arm | 30 | 0 | 30 | 0 | 30 | 0 | NCLR_4 was awarded 30 MW of RRS while self-providing 30 MW. The resource has additional headroom, but the capability to provide RRS UFR is set to 30 MW. The resource will be awarded 30 MW.
NCLR_5 does not self-provide RRS | 15 | 15 | 0 | ONL | Dis-Arm | 0 | 0 | 15 | 0 | 0 | 0 | Despite telemetering 15 MW RRS capability, NCLR_5 is not awarded RRS due to UFR status set to dis-armed.
NCLR_6 carries 20 MW of self-provision | 40 | 40 | 10 | ONL | Arm | 20 | 0 | 30 | 0 | 20~30 | 0 | NCLR_6 telemetered a RRS capability of 30MW and self-provided 20MW of RRS. The resource will be awarded at least 20 MW, due to self-provided telemetry of 20 MW, and up to 30 MW as its capability to provide RRS UFR is set to 30 MW and has ample capacity.
QSE to ERCOT Telemetry
ERCOT to QSE ICCP
QSE 1 is awarded 50 MW of RRS UFR in the Day Ahead. QSE 1 has 3 Load Resources with 100 MW of capability in its portfolio to spread the 50 MW obligation across.

## Slide 10: Additional Points
Self-provision for ECRS is specific for UFR enabled resources, however ECRS can still be provided by load resources that are not controlled by UFRs
ERCOT is currently considering potential changes that would allow NCLRs to self-provide for non-UFR-enabled ECRS and Non-Spin.
Any related implementation would not occur with the initial RTC+B go-live in December and would likely be explored as part of a future post-implementation update.

## Slide 11: Questions and for more info contacts
Demand Integration
ERCOTLRandSODG@ercot.com
Mark Patterson
Anthony Pataray
Donald House
Franky Wong

## Slide 12: RTC+B Training videos
See RTC Training Webpage