## Slide 1: Capping System Lambda under RTC
Shams Siddiqi, Ph.D.
Hunt Energy Network (HEN)
(512) 619-3532
shams@crescentpower.net
RTCBTF Meeting
May 21, 2025

## Slide 2: Background: Why is System Lambda capped under RTC?
6.5.7.3 Security Constrained Economic Dispatch (15)(d) “The System Lambda used to determine LMPs from SCED Step 2 shall be capped at the effective VOLL.”
PUCT didn’t Order price cap (only offer cap)–why cap System Lambda under RTC?
  Current Protocols reduce ORDC Adder such that System Lambda (SL) plus ORDC Adder does not exceed VOLL (current VOLL is $5,000/MWh).
  Even though PUCT does not impose any price cap (e.g., on 2/19/25 LMPs were as high as $28,000/MWh), due to the ORDC Adder formulation, current SL does not exceed VOLL.
  ORDC Adder formulation is a “poor man’s approximation” of AS Opportunity Cost under RTC
  However, actual RTC AS Opportunity Cost can be as high as $5,000/MWh (pre-NPRR1268)
  Thus, System Lambda under RTC can be as high as $7,000/MWh.
  Capping prices (SL) creates serious price distortion, inconsistent congestion pricing and uplift issues that are not currently present and should be avoided at all costs under RTC
  Since the RTC Protocols had been originally approved:
    VOLL study determined actual VOLL to be closer to $35,000/MWh; however,
    HCAP has been reduced to $5,000/MWh from $9,000/MWh (original SL cap); and
    Emergency Pricing Program (EPP) has been implemented that reduces HCAP to ECAP of $2,000/MWh for the greater of 24 hours or the entire EEA period when prices for 12 of the 24 hours are at HCAP. This greatly reduces the likelihood of prolonged scarcity prices.

## Slide 3: Simple Example to Illustrate Impacts of Capping
The following simple example shows the bad price signals, inconsistent congestion pricing and uplift created by ERCOT’s proposed implementation of capping:
  Say, for an interval, System Lambda (SL)=$6,000/MWh, LMP1=$200/MWh, LMP2=$4000/MWh
  Capping SL to $5,000/MWh implies LMP1=-$250/MWh (due to floor) and LMP2=$3000/MWh
  Terrible Price Signal: instead of $200/MWh (which is a relative strong price), setting the price at -$250/MWh sends a bad price signal for operations and future resource investment and flexible load consumption decision.
  Inconsistent Congestion Pricing: Congestion (basis) between 1 and 2 is $3000-(-$250)=$3250 instead of the actual $4000-$200=$3800 without capping
  Unnecessary Uplift: If 10,000MW of Resources offered at $200/MWh at location 1, then ERCOT must pay a dispute-based emergency settlement of 10,000*(200-(-250))=$4,500,000 – an unhedgeable huge uplift to Load in one hour that can be avoided
Although SL exceeding VOLL happens infrequently, appropriate pricing during such scarcity events is critically important to the success of the Energy-Only Market
As a general rule, any Price Capping reflects bad market design – which is why the PUCT never Ordered price caps and why this SL price cap needs to be removed

## Slide 4: Solution: Delete Protocol Language related to Capping
PUCT didn’t explicitly Order capping prices – no-impact Urgent NPRR deleting capping language would require PUCT approval (allowing PUCT to decide if explicit price capping is desirable)
VOLL when RTC Protocols were approved was $9,000/MWh – so, SL would’ve been capped at $9,000/MWh – eliminating the SL cap implies SL could reach $7,000/MWh in the unlikely scenario where the marginal Resource offers AS at $0/MW during scarcity
Post-NPRR1268, since ERCOT sheds firm Load to maintain PRC of 1,500MW, RRS ASDC may set AS Opportunity Cost. In unlikely scenario of $0/MW RRS offer, the highest SL would be about $9,000/MWh – the VOLL cap when RTC was approved
Scarcity prices limited to short duration since EPP kicks in reducing HCAP to $2,000/MWh
Thus, average annual energy price impact of eliminating cap would likely be small
With a more accurate VOLL being closer to $35,000/MWh and all the significant changes since RTC approval (HCAP reduction from $9,000/MWh to $5,000/MWh [$2,000/MWh for SCED under RTC] and EPP implementation), eliminating SL capping would ensure:
  Appropriate scarcity price signals essential for an Energy-Only Market
  Un-distorted Energy and Congestion price signals
  Avoidance of unnecessary and potentially large Uplift to Load