## Slide 1: Impact of Duration Constraints for NSPIN on SCED Awards
Presented to:
RTCBTF
Andrew Reimers, Ph.D.
Potomac Economics
May 21, 2025

## Slide 2: Higher Duration Constraints on NSPIN Lead to Greater Energy Awards for ESRs
The expressed intention of the higher duration constraint for NSPIN is to ensure that reserves are able to last longer through a reliability event such as prolonged forecast error
In practice, this constraint will lead to more base points being awarded to ESRs, which will then exhaust their SOC and make them unavailable to provide either energy or reserves as the event persists
As SOC declines, SCED increasingly favors ESRs for energy instead of AS
This dynamic does not depend on high-priced offers for AS
Lower duration requirements allow ESRs to monetize more of their capacity providing AS for longer and to preserve SOC until it is needed

## Slide 3: A Simplified SCED Simulation Tool Was Used to Demonstrate this Dynamic
No Transmission Constraints
Resources
  Thermal generator
    HSL = 40,000 MW
    AS Qty = 10,000
    Energy Offer = $29/MWh
  ESR
    HSL 10,000 MW
    AS Qty = 10,000 MW
    Energy Offer = $1000/MWh
    Max SOC = 10,000 MWh
  Both resources offer RegUp at $6 and all other AS at $0
Demand = 40,000 MW
AS Plan
  RegUp = 900MW
  RRS = 2300 MW
  ECRS = 2300 MW
  NSPIN = 4,000 MW
  Total = 9,500 MW

## Slide 4: Simplified Demand Curves Based on NPRR 1268
Chart: AS Demand Curves
| 0 | 810 | 810 | 832.5 | 832.5 | 855 | 855 | 877.5 | 877.5 | 900
REGUP | 9052 | 9052 | 3250 | 3250 | 2250 | 2250 | 1250 | 1250 | 250 | 250
RRS | 7051 | 7051 | 3100 | 3100 | 2100 | 2100 | 1100 | 1100 | 100 | 100
ECRS | 5050 | 5050 | 3040 | 3040 | 2030 | 2030 | 1020 | 1020 | 15 | 15
NSPIN | 5000 | 5000 | 1000 | 1000 | 100 | 100 | 55 | 55 | 15 | 15 | 0.1 | 0.1 | 0.01 | 0.01

## Slide 5: Impact of NSPIN Duration Requirement on Awards
Chart: 4-Hour NSPIN Duration
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
Energy | 0 | 0 | 0 | 99.5745 | 354.8936 | 610.2128 | 865.5319 | 10 | 964.0909 | 2733 | 0
NSPIN | 1643 | 1393.75 | 1143.75 | 907.9255 | 652.6064 | 397.2872 | 141.9681 | 0 | 0 | 0 | 0
Chart: 1-Hour NSPIN Duration
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
Energy | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 964.0909 | 2733 | 0
NSPIN | 4500 | 4500 | 4100 | 3100 | 2575 | 1575 | 651.25 | 10 | 0 | 0 | 0

## Slide 6: Impact of NSPIN Duration on Prices
Chart: 4-Hour NSPIN Duration
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
Energy | 1002.08 | 1002.08 | 1002.08 | 1020.6596 | 1020.6596 | 1020.6596 | 1020.6596 | 1085 | 1088.2727 | 1194.2 | 11053
REGUP | 18.5 | 18.5 | 18.5 | 129.9574 | 129.9574 | 129.9574 | 129.9574 | 516 | 535.6364 | 1171.2 | 9052
RRS | 12.5 | 12.5 | 12.5 | 123.9574 | 123.9574 | 123.9574 | 123.9574 | 510 | 529.6364 | 1165.2 | 7051
ECRS | 25 | 25 | 25 | 247.9149 | 247.9149 | 247.9149 | 247.9149 | 1020 | 1059.2727 | 1165.2 | 5050
NSPIN | 100 | 100 | 100 | 991.6596 | 991.6596 | 991.6596 | 991.6596 | 1056 | 1059.2727 | 1165.2 | 5000
Chart: 1-Hour NSPIN Duration
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
Energy | 1000.01 | 1000.01 | 1000.01 | 1001.25 | 1004.58 | 1008.3 | 1083.3 | 1085 | 1088.2727 | 1194.2 | 11053
REGUP | 6.05 | 6.05 | 6.05 | 13.5 | 33.5 | 56 | 506 | 516 | 535.6364 | 1171.2 | 9052
RRS | 0.05 | 0.05 | 0.05 | 7.5 | 27.5 | 50 | 500 | 510 | 529.6364 | 1165.2 | 7051
ECRS | 0.1 | 0.1 | 0.1 | 15 | 55 | 100 | 1000 | 1020 | 1059.2727 | 1165.2 | 5050
NSPIN | 0.1 | 0.1 | 0.1 | 15 | 55 | 100 | 1000 | 1020 | 1059.2727 | 1165.2 | 5000

## Slide 7: Summary and Recommendation
Imposing a four-hour duration constraint on NSPIN results in SCED awarding base points to ESRs, thus depleting rather than preserving SOC
This outcome runs counter to the stated objective of preserving reserve capacity through a prolonged reliability event
We recommend that ERCOT set the duration requirement for NSPIN to no more than one hour