## Slide 1
Monthly Review of Reliability Unit Commitment Market Impacts – May 2025
Wholesale Market Working Group
ERCOT Market Analysis

## Slide 2: RUC Resource-Hours
* The difference between “Instructed” and “Effective” values is a result of Resources starting up, shutting down, receiving partial hour instructions, or otherwise not being dispatchable by SCED.
May 2025 | Total | Capacity |  | Congestion | 
 |  | Opt-Out | Non-Opt-Out | Opt-Out | Non-Opt-Out
Instructed Resource-Hours |  |  |  |  | 
Total Count | 230.8 | 0.0 | 14.8 | 11.0 | 205.0
Effective Resource-Hours* |  |  |  |  | 
Total Count | 224.0 | 0.0 | 14.5 | 10.2 | 199.3
Average Megawatts (MW) for Effective Resource-Hours |  |  |  |  | 
Average LSL | 63.8 | 0.0 | 47.9 | 179.7 | 59.2
Average LDL | 76.3 | 0.0 | 48.6 | 242.0 | 70.0
Average BP | 83.3 | 0.0 | 53.3 | 319.7 | 73.7
Average HSL | 236.9 | 0.0 | 261.1 | 331.4 | 230.3

## Slide 3: RUC Instruction Reasons: Last 13 Months Most RUC effective hours in May 2025 were nominally attributed to congestion.

## Slide 4: RUC Instruction Reasons in May 2025
224.0 RUC effective Resource-hours:
  209.5 hours (94%) for congestion
  14.5 hours (6%) for capacity

## Slide 5: Non-opt-out and Opt-out Totals: Last 13 Months May 2025 had a total of 213.8 non-opt-out effective Resource-hours (95%) and 10.2 opt-out effective Resource-hours (5%).

## Slide 6: Non-opt-out and Opt-out Totals: May 2025

## Slide 7: RUC Lead Time Margin: May 2025
Lead time refers to the length of time between a RUC instruction and the start of the commitment window.
Lead time margin is the difference between lead time and the Resource’s startup time.
  In cases where a Resource is committed for multiple back-to-back time blocks, lead time margin is calculated from the first instruction.
Most RUC commitment windows (74%) had a lead time margin of 2 hours or less.

## Slide 8: Average Resource Age: Last 13 Months In May 2025, the average age of RUC-committed Resources was 52.0 years for Non-opt-out Resource-hours.
Note: For Resource configurations with multiple physical generators, the age of the oldest generator is used.

## Slide 9: Age Category: Last 13 Months In May 2025, most RUC Effective Resource-Hours (68%) were provided by resources that were more than 50 years old.
Non-opt-out
Opt-out

## Slide 10: RUC-Instructed Resource Dispatch above LDL
May 2025
There were 18.3 effective Resource-hours in which Resources that did not successfully opt out were dispatched above their LDL.
  For 7.8 of these Resource-hours, the LMP for the RUC-instructed Resource was above the RUC offer floor.
  For 10.5 of these Resource-hours, the LMP for the RUC-instructed Resource was below the RUC offer floor.
    For all of these 10.5 Resource-hours, the RUC-instructed Resource was mitigated.
There were no Exceptional Fuel Cost submissions for any RUC-committed Resources.

## Slide 11: Reliability Deployment Price Adder: Last 13 Months May 2025 had a total of 97.75 RTORDPA hours with a time-weighted average value of $1.95/MWh.
These graphs show RTORDPA instances by reliability action: 'RUC Only' for instances triggered solely by Reliability Unit Commitment, 'RUC and other triggers' for instances with RUC and additional triggers, and 'Other triggers only' for instances with non-RUC triggers. The daily average RTORDPA is calculated using the total duration across all categories. See ERCOT protocol section 6.5.7.3.1 for details.

## Slide 12: Reliability Deployment Price Adder: May 2025 OD 05/08 had the highest daily time-weighted average RTORDPA of $6.30/MWh.
These graphs show RTORDPA instances by reliability action: 'RUC Only' for instances triggered solely by Reliability Unit Commitment, 'RUC and other triggers' for instances with RUC and additional triggers, and 'Other triggers only' for instances with non-RUC triggers. The daily average RTORDPA is calculated using the total duration across all categories. See ERCOT protocol section 6.5.7.3.1 for more details.

## Slide 13: RUC Clawback, Make-Whole, and Shortfall For May 2025, the total Clawback Charge was $574,643. The total Make-Whole Payment was $493,728.
Of the $493,728 in Make-Whole Payments made in May 2025, $2.84 was uplifted to load due to rounding.
The remaining amount was collected through Capacity-Short Charges.
Data as of June 6th, 2025

## Slide 14: RUC Clawback by Settlement Type
Negative dollars represent a payment from ERCOT to a market participant
“-” indicates settlement has yet to be completed.
Net figures may differ slightly due to rounding.
Month | Initial Settlement ($) | Final Settlement Change ($) | True-up Settlement Change ($) | Net as of June 06, 2025 ($)
May ‘24 | 2,084,416 | 0 | 0 | 2,084,416
Jun ’24 | 58 | 0 | 0 | 58
Jul ‘24 | 47,627 | 0 | -47,627 | 0
Aug ‘24 | 73,690 | 0 | 0 | 73,690
Sep ‘24 | 140,239 | 0 | -7,864 | 132,375
Oct ‘24 | 179,331 | 0 | 0 | 179,331
Nov ‘24 | 2,022,874 | 0 | -259,986 | 1,762,888
Dec ‘24 | 147,389 | -3 | 0 | 147,386
Jan ‘25 | 1,037,717 | 0 | - | -
Feb ‘25 | 3,272,312 | 0 | - | -
Mar ‘25 | 545,642 | 0 | - | -
Apr ‘25 | 993,341 | 119 | - | -
May ‘25 | 574,643 | - | - | -

## Slide 15: RUC Make-Whole by Settlement Type
Negative dollars represent a payment from ERCOT to a market participant
“-” indicates settlement has yet to be completed.
Net figures may differ slightly due to rounding.
Month | Initial Settlement ($) | Final Settlement Change ($) | True-up Settlement Change ($) | Net as of June 06, 2025 ($)
May ‘24 | -2,957 | 0 | 0 | -2,957
Jun ’24 | -76,670 | 0 | -57,341 | -134,011
Jul ‘24 | -4,297 | 0 | -109,781 | -114,078
Aug ‘24 | -305,171 | 0 | -46,445 | -352,679
Sep ‘24 | -239,681 | 0 | -192,317 | -431,804
Oct ‘24 | -364,395 | 0 | -26,567 | -436,776
Nov ‘24 | -164,191 | 0 | -317,703 | -481,894
Dec ‘24 | -179,587 | 0 | 0 | -179,587
Jan ‘25 | -834,867 | -80,530 | - | -
Feb ‘25 | -1,198,579 | -17,762 | - | -
Mar ‘25 | -1,701,707 | 0 | - | -
Apr ‘25 | -594,864 | -3,693 | - | -
May ‘25 | -493,728 | - | - | -