## Slide 1
NPRR1290 Updates and Discussion: Potential ERCOT Modifications/Additions
David Maggio
Principal, Market Design & Analytics
June 18, 2025
Real-Time Co-optimization plus Batteries Task Force (RTCBTF)
ERCOT Public

## Slide 2: Modification/Additions Included in the Draft Comments
Addressing lingering uses of the term “System-Wide Offer Cap (SWCAP).”
Clarifications regarding default Responsive Reserve Service-Primary Frequency Response (RRS-PFR) amounts for newly qualified Resources and corrections for Physical Responsive Capability (PRC) calculations.
Proposed changes to the emergency operations settlement approach for compensating Qualified Scheduling Entities (QSEs) when their Resource(s) have been financially harmed by the existing System Lambda capping process.
  This is a modification to the proposal in the May presentation.

## Slide 3: Addressing lingering uses of “SWCAP”
We identified uses of the term “SWCAP” which were either missed during the development of RTC+B Protocol language or added after the current RTC+B Protocol language was approved.
As that term is being replaced after RTC+B implementation, there is proposed language in the draft comments to use the correct term, as applicable.
  Under RTC+B, there is a distinction between Day-Ahead and Real-Time SWCAP (DASWCAP and RTSWCAP).
This impacted language in Protocol sections 2.1, 4.4.9.8, 4.4.9.8.1, 6.5.7.3, 6.6.9.1, 16.11.4.1, and 22 Attachment P

## Slide 4: Clarifications regarding default RRS-PFR qualified amounts and PRC calculations
Current Protocols define the default RRS-PFR qualified amount for all Resources as 20% of its High Sustained Limit (HSL). Under RTC+B, the default RRS-PFR qualified amount for an Energy Storage Resource (ESR) is expected to be 20% of its full operating range between HSL and Low Sustained Limit (LSL)
  I.e., the droop characteristic for an ESR is based on this full operating range.
The draft comments propose defining “Total Governor Control Capability (TGCC),” which will represent the total capability of a Generation Resource, ESR or Controllable Load Resource (CLR) to respond to system frequency deviations based on droop characteristics.
  The proposed language includes changes to Protocol sections 3.18 and 8.1.1.2.1.2, where “TGCC” is used to determine the default RRS-PFR qualified amount.
Additionally, there are proposed language changes for section 6.5.7.5 which correct the PRC8 and PRC9 calculations to use the new “TGCC” term.
ERCOT will also present related Nodal Operating Guide draft changes for discussion at the June 20, 2025, PDCWG meeting.

## Slide 5: Compensating QSEs financially harmed by the existing System Lambda capping process
In May, ERCOT had proposed utilizing existing emergency operations settlement logic, equivalent to what is used in the case of a Real-Time Market price correction.
  These calculations are codified in paragraph (2) of Protocol 6.6.9.1.
  This approach is designed to take into account both energy and Ancillary Services for a Resource when considering harm to its QSE, where Ancillary Service revenues may offset otherwise deficient energy revenues.
Both during and following the last RTCBTF meeting, we received questions and feedback regarding the use of Ancillary Service revenues in these calculations for the capping scenario. ERCOT is proposing an alternative solution based on the feedback received.

## Slide 6: Compensating QSEs financially harmed by the existing System Lambda capping process cont.
While there are scenarios in which consideration of both energy and Ancillary Services continues to seem appropriate (e.g., price corrections), the System Lambda capping process is specific to energy pricing and dispatch.
Also, the current RTC+B Protocol language already recognizes a distinction in scenarios and has formulas that focus on only energy when evaluating the need for QSE compensation, specifically paragraph (1) of Protocol 6.6.9.1.
As such, ERCOT’s draft comments propose to reference paragraph (1) instead of paragraph (2) of Protocol 6.6.9.1 when evaluating compensation for the System Lambda capping scenario.

## Slide 7: Compensating QSEs financially harmed by the existing System Lambda capping process cont.
Language is also proposed to describe what to do in the scenario in which multiple emergency operations settlement scenarios could apply.
  E.g., System Lambda is lowered through the capping process and there is a price correction for the same Settlement Interval.
As this alternative approach continues to make use of existing RTC+B Protocols and processes, there is no impact to ERCOT’s systems and risk to the RTC+B program is avoided.

## Slide 8: Next steps
ERCOT wanted to discuss these draft comments to NPRR1290 before formally filing them.
Pending feedback from the task force, we expect to file these comments no later than the end of the month.