## Slide 1: NPRR1290 HEN Comments: Method for Determining LMPs when System Lambda is Capped that Avoids Uplift, Bad Price Signals, and Uncompensated Losses
Shams Siddiqi, Ph.D.
Hunt Energy Network (HEN)
(512) 619-3532
shams@crescentpower.net
RTCBTF Meeting
June 18, 2025

## Slide 2: Problems with LMP-setting method implied in NPRR1290
Even though not explicitly described in NPRR1290, the make-whole and uplift provisions imply that all LMPs are set by subtracting (System Lambda-VOLL) from the original actual LMPs
The following simple example shows the bad price signals, inconsistent congestion pricing, uplift, and losses created by the implied method of setting LMPs when System Lambda is capped in NPRR1290 as submitted:
  Say, for an interval, System Lambda (SL)=$6,000/MWh, LMP1=$200/MWh, LMP2=$4000/MWh
  Capping SL to $5,000/MWh implies LMP1=-$250/MWh (due to floor) and LMP2=$3000/MWh
  Terrible Price Signal: instead of $200/MWh (which is a relative strong price), setting the price at -$250/MWh sends a bad price signal for operations and future resource investment and flexible load consumption decision.
  Unnecessary Uplift: If 10,000MW of Resources offered at $200/MWh at location 1, then ERCOT must pay a dispute-based emergency settlement of 10,000*(200-(-250)) = $4,500,000 – an unhedgeable huge uplift to Load in one hour that can be avoided
  Uncompensated Losses: If a Resource has 100MW LSL or a QSE purchased 100MW at location 1 (in DAM or Bilaterally), that Resource/QSE is charged $25,000 for this hour instead of receiving an expected payment of $20,000 – a large uncompensated loss
  Inconsistent Congestion Pricing: Congestion (basis) between 1 and 2 is $3000-(-$250)=$3250 instead of the actual $4000-$200=$3800 without capping
  Burden on ERCOT Staff processing potentially large number of disputes every time SL exceeds VOLL.
Although SL exceeding VOLL happens infrequently, appropriate pricing during such scarcity events is critically important to the success of the Energy-Only Market

## Slide 3: HEN Method of Determining LMPs when System Lambda capped
PUCT didn’t Order and Substantive Rules don’t require price cap (only offer cap)
Capping prices creates serious price distortion, uplift costs to Load, and potential uncompensated losses from DAM and Bilateral positions, that are not currently present and should be avoided at all costs under RTC
HEN prefers not capping prices at all – but that will require some discussion
To mitigate the significant adverse impacts of the implied method of setting LMPs in NPRR1290 when SL is capped, HEN provides the following method of determining LMPs:
  Cap System Lambda (SL) at $5,000/MWh (as specified in the Protocols)
    E.g., if initial SL is $5,500/MWh prior to capping, final SL is reduced by $500/MWh
  For all Initial LMP>$5,000/MWh, Final LMP=Max($5,000, Initial LMP – SL Reduction)
    E.g., if initial LMP=$6,000/MWh, final LMP=$5,500/MWh; if initial LMP=$5,400/MWh, then final LMP=$5,000/MWh
  For all Initial LMP<=$5,000/MWh, Final LMP=Initial LMP (i.e., these LMPs are unaltered)
    Generalized formula for all LMP = Min(Initial LMP, Max(VOLL, Initial LMP-Max(0,(SL-VOLL))))
  No make whole payment needed; thus, no unhedgeable uplifted cost to Load

## Slide 4: Benefits of HEN Changes to NPRR1290
Maintains critically important price signals throughout the system and only reduces LMPs above VOLL by the same amount as System Lambda is reduced to not exceed VOLL.
Since no offer or bid can be greater than VOLL in RTM and DAM, there are no QSEs/Resources that are harmed (i.e., incurring actual losses) by this method of LMP determination
Of course, RTM sales and Point-to-Point Obligations that sink at Settlement Points with LMPs lowered to VOLL or higher make less than unaltered prices (true with any price capping) – but likely still realize substantial profits.
Eliminates the ability to submit disputes to recover costs related to SL capping
Eliminates any uplift cost to Load due to SL capping.
Eliminates uncompensated losses to Resources and QSEs with DAM and Bilateral positions that are adversely impacted by the method of setting of LMPs under NPRR1290 as submitted.
Eliminates burden on ERCOT Staff processing potentially large number of disputes every time System Lambda exceeds VOLL.