## Slide 1: Design Concepts for DRRS
Andrew Reimers, Ph.D.
Deputy Director
Potomac Economics | ERCOT IMM
DRRS Workshop V
June 26, 2025

## Slide 2: Shoulds and Should Nots of DRRS Design
DRRS should be able to be provided by both online and offline units and co-optimized in real-time so that any shortages in the supply of DRRS are factored into price formation
  Eligibility to provide offline DRRS in real-time should not be limited to resources that were awarded DRRS in DAM. ERCOT is still working through this issue
  Eligibility to provide offline DRRS in real-time could be checked against COP so that resources already planning to turn on in the next two hours are not eligible to receive DRRS awards
DRRS should be designed strictly as an operating reserve and not as a resource adequacy product
  DRRS was originally conceived as an “uncertainty product” to provide operating reserves in the event of prolonged forecast errors that result in under-commitment from thermal generators
  ERCOT’s “Release Factor” concept is meant to allow DRRS to function as both an operating reserve (i.e., “non-overlapping DRRS”) and as a source of revenue for achieving a resource adequacy target
  How do you reflect a future RA target in current procurement volumes for DRRS? How do the current revenues for DRRS correspond to future investment decisions?

## Slide 3: Resolving the Handoff between SCED and RUC
One of the challenges with procuring offline-DRRS in real-time is how these awards are handled by RUC. What is SCED actually buying each interval if the resource has to be committed by RUC, which only runs at the beginning of each hour and takes 15-30 mins to run?
Solution: implement a version of RUC with a shorter study period that can execute more quickly (appx 5 mins) on a more frequent (e.g., every 15 minutes) or on an as needed basis

## Slide 4: How Would this Faster Version of RUC Work?
This new version of RUC would incorporate the most recent SCED awards for offline DRRS into its commitment logic just like in ERCOT’s proposed concepts
The study period would be reduced to 4-5 hours to account for the full range of time DRRS units are required to be online per statute
The first interval of the study period would be an hour after the time at which this RUC process was initiated

## Slide 5: Benefits of a Faster, More Frequent RUC Process
Reducing the study period would reduce the solve time both by reducing the number of hourly decision variables and by implicitly ruling out commitment of resources with longer start times
This RUC process could utilize the same demand curves as SCED and remove the scaling factors used in the HRUC/DRUC processes such that commitment decisions are made on an economic basis
A more frequent RUC process closer to real-time could approximate the benefits of a multi-interval RTM
  More effective accounting for ESR SOC
  More effective deployment of offline NSPIN

## Slide 6: Summary of IMM Recommendations for DRRS Design Criteria
DRRS should be able to be provided by both online and offline units, regardless of DAM awards, and co-optimized in real-time so that any shortages in the supply of DRRS are factored into price formation
DRRS should be designed strictly as an operating reserve and not as a resource adequacy product, unlike ERCOT’s current “release factor” concept
A faster-running version of RUC with a shorter study period resolves handoff between SCED and RUC and allows for more efficient deployment of offline reserves