## Slide 1
Annual Distributed Generation Estimate
Supply Analysis Working Group
Thinesh Devadhas Mohanadhas
Principal Engineer, Emerging Technologies
ERCOT
June 27, 2025

## Slide 2: ERCOT Estimated Total DG Growth 2015-2024 (MW)
Chart: ERCOT Estimated DG Growth (MW) 2015-2024
| Nat Gas MW > 1 MW | Diesel/IC MW > 1 MW | Solar MW >1MW | Battery MW >1MW | Other Renewable MW >1MW | Nat Gas MW < 1 MW | Diesel/IC MW < 1 MW | Solar MW <1MW | Battery MW < 1 MW | Other Renewable MW < 1 MW
2015 TOTALS | 93.31 | 242.8956 | 64.189 | 0 | 90.328 | 2.0787 | 1.6325 | 132.4419 | 0 | 4.5842
2016 Totals | 103.155 | 265.2456 | 78.199 | 0 | 108.408 | 2.2787 | 4.1875 | 235.2925 | 0 | 4.3834
2017 Totals | 160 | 280 | 90 | 2 | 120 | 10 | 10 | 360 | 0 | 20
2018 Totals | 230 | 280 | 220 | 2 | 130 | 10 | 10 | 500 | 0 | 20
2019 Totals | 260 | 350 | 260 | 2 | 120 | 10 | 10 | 710 | 0 | 20
2020 totals | 310 | 280 | 270 | 130 | 130 | 30 | 20 | 990 | 10 | 20
2021 totals | 410 | 290 | 290 | 260 | 130 | 30 | 20 | 1440 | 60 | 20
2022 totals | 460 | 290 | 290 | 390 | 130 | 30 | 20 | 2100 | 130 | 20
2023 totals | 480 | 310 | 300 | 540 | 130 | 39 | 20 | 2750 | 190 | 20
2024 totals | 560 | 310 | 320 | 1250 | 130 | 70 | 30 | 3110 | 290 | 20
Annual Estimates (MW) | 
2015 | 650
2016 | 800
2017 | 1050
2018 | 1400
2019 | 1710
2020 | 2180
2021 | 2920
2022 | 3850
2023 | 4770
2024 | 6050
Notes: Major areas of DG growth in ERCOT
Solar PV <1 MW
DGR Energy Storage> 1 MW
Natural gas > 1 MW
Detail for Systems > 1 MW
New applications for Energy Storage/Increased Growth in Distribution connected batteries
Continuation of upward trend for Nat Gas
Limited growth for solar > 1 MW
Declining Landfill Gas, Hydro, Wind
Detail for Systems < 1 MW
Steady Solar PV trend in line with projections
Increased Growth in Distribution connected batteries
ERCOT proposed NPRR 1265 to align with House Bill 3390 (HB 3390) to address DG reporting of Unregistered DG. This NPRR establishes procedures for UDG reporting to ERCOT and UDG reporting requirements from ERCOT. This will help with tracking and reporting UDG in the region and aligns to allow the utilities to share information with ERCOT.

## Slide 3: Settlement-Only Distributed Generation in ERCOT 2010-2024
SODGs are:
<10 MW
If >1 MW and inject to grid, must register with ERCOT
If <1 MW, registration optional
SODGs | # Units | MW
Non-Renewable | 356 | 742
Renewable + Storage | 63 | 350
TOTALS | 419 | 1092
Chart: SODG 2010-2024
| 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
Renewable MW | 67.66 | 87.32 | 93.72 | 133.08 | 133.08 | 143.07 | 156.15 | 170.72 | 216.56 | 290.64 | 328.14 | 338.14 | 348.04 | 348.04 | 355.9 | 349.85
Accumulated MW | 79.36 | 107.22 | 121.22 | 160.58 | 332.31 | 373.34 | 427.05 | 459.1 | 593.59 | 742.73 | 808.93 | 890.93 | 946.58 | 1004.33 | 1045.14 | 1091.47
Accumulated Count | 13 | 17 | 20 | 29 | 44 | 52 | 61 | 74 | 133 | 208 | 236 | 298 | 327 | 374 | 394 | 419

## Slide 4: ERCOT Solar PV Rooftop Projections vs Actual 2024
Chart: MW
| 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035
Conservative | 235 | 360 | 500 | 710 | 990 | 1302.2562 | 1922.6849 | 2470.1512 | 2755.2076 | 2973.3434 | 3187.7197 | 3383.55 | 3559.0638 | 3713.7038 | 3847.9145 | 3962.8798 | 4060.26 | 4141.9637 | 4209.969 | 4266.1971
Moderate | 235 | 360 | 500 | 710 | 990 | 1302.2562 | 1922.6849 | 2470.1512 | 2755.2076 | 3007.6 | 3309.1178 | 3604.6352 | 3888.6199 | 4156.401 | 4404.4302 | 4630.3903 | 4833.1595 | 5012.6667 | 5169.6825 | 5305.5879
Aggressive | 235 | 360 | 500 | 710 | 990 | 1302.2562 | 1922.6849 | 2470.1512 | 2755.2076 | 3114.4718 | 3759.5 | 4404.5282 | 5012.6667 | 5555.0081 | 6015.2 | 6389.4875 | 6683.5556 | 6908.3797 | 7076.7059 | 7200.768
Notes: Total of ~3110 MW for NOIEs plus Competitive Choice areas
Scenarios :
Conservative reaches ~3100 by 2026 and ~4000 MW by 2032
Moderate reaches ~3300 MW by 2026 and ~4800 MW by 2032
Aggressive reaches ~3800 MW by 2026 and ~6700 MW by 2032
2016-2024 Data matches the “Moderate” profile best (so far).