## Slide 1: DWG Report to ROS
Aditi Upadhyay – DWG Vice Chair
July 10th, 2025

## Slide 2: DWG Update
DWG Webex meeting held on 6/26/2025
Large Power Electronics Load Ride Through
  A ride through requirement proposal for large power electronic load (focus on datacenters and crypto loads) was provided by ERCOT
  Currently engaged with Texas A&M to develop PSCAD models and EPRI to develop PSSE models
  Action item: DWG to provide feedback on ride through proposal by July 3rd
  Next step: Present a draft to Large Load Working Group and get industry feedback

## Slide 3: DWG Update, continued
PSSE error with the node breaker cases
  Oncor has observed some errors while running dynamic simulations using the node breaker cases
  Error is not consistent, Oncor presented a workaround while awaiting resolution from Siemens PTI
Large Load stability study guideline/screening technique
  Recap discussion held with TSPs on the large load stability whitepaper
  Provided guidance on selecting nearby large loads for stability studies
  Discussed an updated proposed stability screening criteria based on TSP feedback, discussion to continue in future meetings

## Slide 4: DWG Update, continued
Flat Start Update 2025/2026 Tentative Schedule
  Updated Stability Book was posted June 4 including dynamic load models
  Reviewed feedback received on including large load dynamic models in the flat start cases
  Discussed the tentative schedule for the 2025/2026 case build
  Action item: TSP to review seed case (Pass 0) and provide feedback after SSWG posts final case set
NERC TPL-008-1 and DWG TSP support
  ERCOT shared tentative plan to perform Extreme Temperature Events Stability Study to identify performance deficiencies and develop Corrective Actions Plans
  Study will be performed by ERCOT every 5 years with support from DWG TSPs
  Contingency events will be limited to NERC Category P0, P1, and P7

## Slide 5: Questions or Feedback?