## Slide 1
4CP Calculation Overview
September 2025 DSWG

## Slide 2: 4 Co-incident Peak Overview
4CP is the four peak intervals from the summer months of June through September. One peak per month.
  ERCOT average 4CP is defined as the average of the peaks from each of the four summer months.
ERCOT calculates the four co-incident peaks for each year based on final settlement data.
  Uses:
    Reported to PUCT (Transmission Service Charges)
    Demand Response
    Load shedding obligations
ERCOT calculates and posts 4CP by December 1st of every year based on Protocol 9.17 and 9.17.1.

## Slide 3: How is 4CP Calculated
First calculation step is determining the peak interval for the month.
Peak interval is defined as the highest 15-minute final settlement interval for the entire ERCOT system per the formula below:
  Sum of:
  Generation Resources + Settlement Only Generators(SOGs)
  + Block Load Transfers(BLT) out of ERCOT + DC Tie Imports
  – BLT into ERCOT – DC Tie exports – Wholesale Storage Load(WSL)
Any difference between the determined coincidental peak is allocated to all DSPs and ELSEs that are listed in the 4CP report. (9.17.1(4))
  Adjustment to each load is based on Load Ratio Share (LRS) for each DSP and ELSE prior to adjusting for load/gen mismatch.
  For 2025 seeing between approximately -1 MWH to -21 MWH of adjustment.

## Slide 4: Deviation from Operation Load
Official 4CP is based on final settlement data.
  Settlement interval data may differ from operational data due to difference in accuracy from metering and telemetry.
    These differences could impact which interval is determined as a co-incident peak.
  Changes to generation site or WSL EPS meter data can change between initial and final.

## Slide 5: Comparison of June 2025 Initial and Final Peaks
 | 06/19/2025 @ 17:00 | 06/23/2025 @ 14:30 | 06/20/2025 @ 16:30 | 06/24/2025 @14:15 | 06/28/2025 @ 16:30
Initial | 77453 | 77253 | 77173 | 77001 | 76854
Final | 77486 | 77258 | 77205 | 77005 | 76856
Noted issues changing data between Initial and Final
  Error in meter time
  Current Transformer ratio error

## Slide 6: QUESTIONS?

## Slide 7
NCLR Telemetry in RTC+B
September 2025 DSWG

## Slide 8: NCLR Resource Status Codes
Pre-RTC
  Resource Status Codes (RST)
  OUTL = 260
  ONRL = 259
  ONECL = 264
RTC+B
  Updated Resource Status Codes (RSTR)
  OUTL = 258
  ONL = 257

## Slide 9: Ramp Rates and Capabilities
Pre-RTC
  AS Responsibility and Schedule
  RRRS
  RRSC
  ECRS
  ECSC
  NSRS
  NSSC
RTC+B
  Ramp Rates & Awards
  UFRC (UFR Capability)
  UFRA (UFR Award)
  ECRR (ECRS RR Capability *10 Min)
  ECRA (ECRS Award)
  NSRR (NSPIN RR Capability *30 Min)
  NSRA (NSPIN Award)
QSE to ERCOT Telemetry
ERCOT to QSE ICCP

## Slide 10: Self-Provision Achieved via Telemetry Points for NCLRs
QSEs will be able to self-provide in real-time via telemetered ICCP points
LEGEND
ICCP Change Request Example RTC+B V1.4 on RTC ERCOT webpage

## Slide 11: The Self-Provision Checklist
Scenario: My Load Resource was awarded 15 MW in the DAM, and I purchased 5 MW via a trade.
My total RRS AS Position is 20 MW.
How to correctly self-provide 20 MW:
    Is my resource qualified?
    Telemetry Points
      RST set to ONL (257)
      UFR must be Armed
      Can I cover my obligation?
        Qualified MW Amount ≥ Self-provided amount
        NPF - LPC ≥ Self-provided amount
        Capability to Provide AS ≥ Self-provided amount
      Telemeter Self-provision
      “your offers explain your extra”

## Slide 12: Scenario 1
Scenario ** Assume AS qualified for All Headroom (NPF-LPC) | Max Power Cons. | Net Power Flow | Low Power Cons. | Resource Status | Under Freq. Relay | Self-provided RRS UFR (MW) | Self-provided ECRS (MW) | Current Capability to provide UFR (MW) | ECRS (10min) Ramp Rate (MW/min) | RRS UFR AS Award | ECRS AS Award | Notes
 | MPC | NPF | LPC | RST | UFR | SPUF | SPEC | UFRC | ECRR | UFRA | ECRA | 
NCLR_1 is qualified to provide 20 MW. DAM awards NCLR_1 with 15MW RRS. QSE also has additional 5MW RRS Position via RRS Trades. | 20 | 20 | 0 | ONL | Arm | 20 | 0 | 20 | 0 | 20 | 0 | NCLR_1 Telemetry needs to show: Status = ONL, MPC >= NPF >= 20 MW, NPF-LPC >= 20 MW, RRS capability >= 20 MW, RRS self-provided telemetry = 20 MW SCED will respect the 20 MW self-provided RRS and award the resource 20 MW RRS UFR.
QSE to ERCOT Telemetry
ERCOT to QSE ICCP
NCLR_1 has a 20 MW RRS AS Position, 15 MW from DAM award and 5 MW from RRS Trade