## Slide 1
RTCBTF
October 15, 2025
Balancing Operations Planning Staff
RTC-RUC AS Deployment Factors for Go Live

## Slide 2: Introduction
ERCOT has been actively working on analysis to formulate a strategy for setting Ancillary Service (AS) Deployment Factors (DFs) in Reliability Unit Commitment (RUC) studies in RTC.
Note the ASDFs shared in this deck are for immediate use along with RTC Go-Live. These values have been selected based on functionality that is expected to be available at Go-Live and expected submission behavior.
  Specifically, upon RTC Go-Live changing ASDFs will require manual operator action. To reduce the risk of human input errors, ERCOT intends to set ASDFs in a manner that minimizes manual operator action to change these.
Post-RTC Go-Live, as more operational experience with RTC is gained, ERCOT intends to transition to setting ASDFs a day or two days prior to the Operating Day informed by forecasted uncertainty or other relevant data.
  This approach will require system changes both to determine the appropriate ASDFs and establish a workflow that updates the ERCOT systems with these.

## Slide 3: Introduction, Contd.
In the September 25 RTCTF meeting materials for this topic, ERCOT had incorrectly stated that current RUC studies, in accordance with paragraph 1 of Nodal Protocol Section 5.5.2, RUC effectively uses a deployment factor of 1 for Ancillary Services.
Current RUC studies do not account for changes in Hour Beginning State Of Charge (HBSOC) from one hour to the next.
  The current constraint is instead focused on HBSOC, min. SOC, and max. SOC within an individual hour and a form of this constraint will remain with RTC+B.
Further, the specific constraint that considers HBSOCs and ASDFs is new in RTC-RUC and enables ERCOT during RUC studies to account for “expected” usage of energy for AS, based on AS awards, when evaluating hour-to-hour changes in HBSOC.
  “AS awards” and “usage of energy” are referring to the perspective of the RUC optimization and not binding AS awards and energy deployment to the Resource’s QSE, e.g., through the Real-Time Market.
The next few slides will share
  The ASDFs that ERCOT is expecting to adopt for setting AS deployment Factors in RUC studies following RTC+B go-live and
  The impacts of these on RUC results for an example snapshot, February 4th, when forecast uncertainly materialized closer to Real-Time.

## Slide 4: AS Deployment Factors For Go-live: Regulation Service
Regulation deployment data for 2024 and 2025 shows (1) year over year growth in average, (2) seasonal variations (higher averages in Summer) and (3) time of day variations (linked to sunrise and sunset).
ERCOT has derived DFs for Regulation Up and Regulation Down based on 75th percentile of the historical deployment of each service in the last two years, rounded to the nearest 5%. This approach learns from historic usage that is closer to average values while accounting for increases in intra-hour uncertainties that may materialize due to growth in installed capacity.

## Slide 5: AS Deployment Factors For Go-live: RRS PFR and FFR
RRS-PFR energy usage data for 2024 and 2025 show (1) relatively small usage of RRS-PFR, (2) no clear seasonal or time of day variations.
Based on this analysis, ERCOT expects to use a zero (0) DF for RRS-PFR for all hours. Further, with minimal RRS-FFR events, ERCOT expects to use a zero (0) DF for RRS-FFR as well. This selection essentially indicates that ERCOT expects energy usage due to deployment of these services will not significantly impact the next Operating Hour’s planned HBSOC.

## Slide 6: AS Deployment Factors For Go-live: ECRS and Non-Spin
ERCOT’s expects to use a deployment factor of one for ECRS and Non-Spin for all hours.
ERCOT recognizes this is a conservative approach. However, for RTC Go-Live, ERCOT considers this approach will best represent the expected energy used for AS due to uncertainties in the RTC-RUC studies until additional information is gathered and analyzed.
Further, ERCOT notes that the actual impacts of these DFs on commitments is dependent on many factors including HBSOC data submitted in Current Operating Plans.
ERCOT will continuously monitor RTC RUC results post Go-Live and is open to adjusting DFs for ECRS and Non-Spin based on experience gained from that period.

## Slide 7: RTC-RUC Study for Feb 4, 2025
Study Setup: Using 2/4/2025 near 10am HRUC snapshot:
Set HBSOC to actual from 1/29/2025, as a view of typical day when wind forecast error was relatively low.
Set penalties for violating HBSOC high (in alignment with current systems)
Run the following scenarios:
  B1: Set a baseline with all ASDFs for all hours = zero
  S1: Set ASDFs = RTC Go-Live expected values, as previously described in this presentation
  S2: Set ASDFs for all hours = One
Results:
Observation: In both comparative analysis,
ESRs are counted to provide volumes of Regulation, RRS-PFR, RRS-FFR that are similar to how these resources typically provide these services in Real Time. ESRs are counted to provide similar portion of ECRS and Non-Spin to the portion of these services that they provide today
Further there was a slight increase in commitment compared to DF=0.

## Slide 8: Summary
Following is a summary of the DFs that ERCOT expects to use for Go-Live
  Regulation Service: Derived from last two years Regulation energy deployment data.
  RRS-PFR and RRS-FR: Zero (0) for all hours
  ECRS and Non-Spin: One for all hours
Further ERCOT reiterates that post-RTC Go-Live, as more experience with RTC is gained, ERCOT intends to transition to setting deployment factors a day or two days prior to the Operating Day, informed by forecasted uncertainty,, and/or other relevant data.
ERCOT appreciates the feedback stakeholders have provided on this topic. ERCOT welcomes any further feedback stakeholders may have.

## Slide 9: Appendix

## Slide 10: RUC with Implementation of RTC+B Project
DRUC and HRUC will be the tools to assess if enough capacity (MW & MWh) is available (and in the right locations) to ensure RTC SCED will have enough capacity (and State of Charge) to solve for energy and Ancillary Services.
Similar to today, ESRs will NOT be seen as OFF and are therefore NOT available to be RUCed. In other words, the RUC software will NOT RUC an ESR to come online. (ESRs should have a status of “ON”, “ONOS” “ONTEST”, “ONEMR”, “ONHOLD” or “OUT.” “OUT” should be used only if the resource is “broken.”)
In evaluating the capability of the online Resources (and those shown off-line), the full capability of the Resources (including ESRs) planned to be available will be “fair game” for the RUC software. In other words, with the RTC+B implementation the RUC software will not assume Ancillary Services are carried by any particular Resource and will consider all possibilities of where to carry Ancillary Services for future hours.
The RUC software will use the Hour Beginning SoC (HB SoC) provided by the QSEs in their COPS for each ESR to appropriately limit the possible use/capability of each ESR.
The RUC process self-schedules ESRs to their HB SoC. The process of self-scheduling evaluates the change in the COP submitted HB SoC (change in stored energy SoC) across two consecutive hours and determines the best use of that change in energy – combination of charging or discharging the ESR as Base Points and/or procuring Ancillary Services considering Deployment Factors for that hour.
Deployment Factors (DFs) are used to simulate deployment of Ancillary Services for an hour. (Deployment Factors could be 0, 1 or between 0 and 1. There will be a projected DF for each AS and for each hour.)

## Slide 11: RUC with Implementation of RTC+B Project, Contd.
The RUC Capacity Short calculations will use optimization techniques to minimize a QSE’s potential energy and/or Ancillary Service shortfall. This optimization process, will also consider the change in the COP submitted HB SOC across consecutive hours for an ESR to determine the best use of that change in energy to cover the QSE’s energy and Ancillary Services position for each hour in the RUC study period.
Links to background information on RUC Capacity Short Calculation:
  RTC B Modifications to RUC Capacity Short Calcs 02192024 v2.pptx
  RTC B Additional examples RUC Capacity Short Calcs 03172024 v1.pptx
  RTC+B Modifications to RUC Capacity Short Calcs 03172024 (This is a spreadsheet)