## Slide 1
TSAT Implementation Updates
For CMWG 11/17/2025
Douglas Bernhoft,
Supervisor, Operations Engineering and Application Support

## Slide 2: Agenda
A Look at Real Time GTC Limits vs Offline Calculated Limits
Work in 2025 and Plans in 2026

## Slide 3: Real Time GTC Limits
Data from June, July, and August 2025
GTC | Average Offline Study Limit (no prior outage) | Average Real Time TSAT Limit (no prior outage)
CULBSN | 99999 | 99999
EASTEX | 99999 | 99999
HMLTN | 60 | 73
RV_RH | 99999 | 99999
TSAT limit for HMLTN GTC was initially lower than the offline limit when it was first tested in the production environment, even under no prior outage condition.
With further investigation and work with the REs, a modeling issue was identified, and an updated model was provided.
Since then, the limits have been improved.

## Slide 4: Real Time GTC Limits
Data from June, July, and August 2025
GTC | Average Offline Study Limit (no prior outage) | Average Real Time TSAT Limit (no prior outage)
CULBSN | 99999 | 99999
EASTEX | 99999 | 99999
HMLTN | 60 | 73
RV_RH | 99999 | 99999
There are instances in real time were TSAT limits are lower than the offline study limit for the HMLTN GTC.
These lower limits were caused by multiple outages, combination of planned and forced, that are not captured in the offline assessment.

## Slide 5: Work in 2025 and Plans in 2026
2025
  Online TSAT scenarios are implemented for 4 GTCs
  TSAT scenarios for 5 GTCs are currently in the testing
    Including both WESTEX and MCCAMY
  Improve modeling and computation capabilities
    Some specific UDMs identified that affect the computation time. ERCOT is continuing to work with the REs and the OEMs to resolve this issue.
    Through detailed testing, identified multiple features to be added to the TSAT software, such as oscillation detection, to ensure the proper identification of the instability and limits.
      Worked with TSAT software vendor to get delivery of and test enhancements
    ERCOT continue to enhance the computation capability since 2024
      New high performance computer acquired to allow for multiple test scenarios to always be running in parallel.
      Over doubled the computational servers used for real time TSAT calculations.
2026
  For GTCs with online stability limits being calculated in real time, switch to these as the primary limit. Continue to have offline calculated limit available as back up.
  Continue parallel testing of multiple scenarios and delivering them to real time operations as they are ready.
  Keep an eye out for market notices to announce these changes.

## Slide 6
Questions?