## Slide 1: CMWG Update
Shane Thommas

## Slide 2: Agenda
CRR LTAS Transactions & Performance Update
NPRR1301 - Align Protocols to Constraint Activation Procedure
TSAT Implementation Updates
RUC Analysis
NPRR1292: Granular Product Type for CRR TOU

## Slide 3: CRR LTAS Transactions & Performance Update
The latest auction (2026.1st6.Seq1) had fewer total and peak weekday transactions submitted than the previous Seq1 auction, resulting in faster solution times
ERCOT reduced the Per-CRRAH Transaction Limit for Seq2 from 2,800 to 2,500

## Slide 4: NPRR1301 - Align Protocols to Constraint Activation Procedure
ERCOT gave a presentation on the current tools and procedures used by operators
  May update to Transmission Constraint Manager (TCM) improves comparison of activated constraints vs. potential constraints
  Primary goal of the change was to help operators activate only the most impactful constraint by avoiding duplication and strengthening signals to affected units.
Discussion around the use of “will” vs “should” or “may”
Discussion around the percent different a constraint would need to be to be considered “similar”
  LCRA had proposed 10%
  ERCOT currently uses 2%
  There was some support for 5%
Further discussion scheduled for next CMWG meeting

## Slide 5: TSAT Implementation Updates
ERCOT has been seeing a difference in the real-time vs offline GTC limits in both directions
  Currently being calculated for 4 GTCs
  5 additional GTCs currently being tested including WESTEX and MCCAMY
Current practice is to use the lowest of the two limits so when real-time TSAT gives a lower limit, it would not be used
  As ERCOT gains confidence in the real-time limit they plan to transition to using them as the primary limit with the offline limit as back up in 2026
ERCOT noted the review of GTCs and consideration for removal as part of the QSA process

## Slide 6: RUC Analysis
ERCOT presented a detailed overview on RUC and recent RUC activity
  Increased RUC activity in 2025 compared to recent years and primary reason is to solve congestion but there are often multiple factors
  Some units with a hurting shift factor are RUC’d so that a units with a greater hurting shift factor will not run
  COP submissions remain a critical input, but data reliability issues persist
    ERCOT will be reaching out to QSEs to address COP issues
Stakeholders raised concerns about load forecast accuracy, forecast error, the use of HASL, and reliance on older long lead-time units and other issues
Further discussion scheduled for the next CMWG meeting

## Slide 7: NPRR1292: Granular Product Type for CRR TOU
Broad stakeholder support for the latest version of NPRR1292
  Many concerns were eliminated by the persistence of the existing TOUs
Concerns around the impact to CRR transaction limits remain for some stakeholders
  ERCOT anticipates longer run-times but expects other initiatives to offset impacts.
  Removal of the budget constraint simplifies implementation and reduces impact
    ERCOT is looking to file language to remove the constraint in December or January
CMWG has concluded discussion
Discussion on the removal of the budget constraint and credit will continue at the next meeting

## Slide 8
Placeholder slide for you to ask questions