## Slide 1
Monthly Review of Reliability Unit Commitment Market Impacts – December 2025
Wholesale Market Working Group
ERCOT Market Analysis

## Slide 2: RUC Resource-Hours
* The difference between “Instructed” and “Effective” values is a result of Resources starting up, shutting down, receiving partial hour instructions, or otherwise not being dispatchable by SCED.

## Slide 3: RUC Instruction Reasons: Last 13 Months RUC effective hours in December 2025 were lower than in previous months.
89 out of 131 Effective Resource-Hours in December 2025 occurred before the implementation of Real-Time Co-Optimization Plus Batteries (RTC+B)

## Slide 4: RUC Instruction Reasons in December 2025 82% of RUC effective hours in December 2025 were nominally attributed to congestion.
129.9 RUC effective Resource-hours:
  106.7 hours (82%) for congestion

## Slide 5: Non-opt-out and Opt-out Totals: Last 13 Months December 2025 had a total of 129.9 non-opt-out effective resource-hours (100%) and no opt-out effective Resource-hours, following a similar pattern to previous months.

## Slide 6: Non-opt-out and Opt-out Totals: December 2025 December 2025 had a total of 129.9 non-opt-out effective resource-hours (100%) and no opt-out effective Resource-hours.

## Slide 7: RUC Lead Time Margin: December 2025 Most RUC commitment windows (82%) had a lead time margin of 2 hours or less.
Lead time refers to the length of time between a RUC instruction and the start of the commitment window.
Lead time margin is the difference between lead time and the Resource’s startup time.
  In cases where a Resource is committed for multiple back-to-back time blocks, lead time margin is calculated from the first instruction.

## Slide 8: Average Resource Age: Last 13 Months In December 2025, the average age of RUC-committed Resources was 49.9 years for Non-opt-out Resource-hours.
Note: For Resource configurations with multiple physical generators, the age of the oldest generator is used.

## Slide 9: Age Category: Last 13 Months In December 2025, most RUC Effective Resource-Hours (80%) were provided by resources that were at least 50 years old.
Non-opt-out
Opt-out

## Slide 10: RUC-Instructed Resource Dispatch above Low Dispatch Limit (LDL) in Non-Opt-Out Hours
Out of all 129.9 non-opt-out Effective Resource-hours, RUC-instructed Resources were dispatched above their LDL for 1.8 Resource-hours.
  In 1.4 of these Resource-hours, the Locational Marginal Price (LMP) for the RUC-instructed Resource exceeded the RUC offer floor.
  In 0.3 of these Resource-hours, the LMP for the RUC-instructed Resource fell below the RUC offer floor.
    All 0.3 Resource-hours saw the RUC-instructed Resource being mitigated.
There were no Exceptional Fuel Cost submissions for any Resources committed by RUC.

## Slide 11: Reliability Deployment Price Adder: Last 13 Months December 2025 had a total of 65.2 RTORDPA hours with a time-weighted average value of $1.59/MWh.
These graphs show RTORDPA instances by reliability action: 'RUC Only' for instances triggered solely by Reliability Unit Commitment, 'RUC and other triggers' for instances with RUC and additional triggers, and 'Other triggers only' for instances with non-RUC triggers. The daily average RTORDPA is calculated using the total duration across all categories. See ERCOT protocol section 6.5.7.3.1 for details.

## Slide 12: Reliability Deployment Price Adder for Energy: December 2025 OD 12/8 had the highest daily time-weighted average RTORDPA of $1.93/MWh.
These graphs show RTORDPA instances by reliability action: 'RUC Only' for instances triggered solely by Reliability Unit Commitment, 'RUC and other triggers' for instances with RUC and additional triggers, and 'Other triggers only' for instances with non-RUC triggers. The daily average RTORDPA is calculated using the total duration across all categories. See ERCOT protocol section 6.5.7.3.1 for more details.

## Slide 13: Reliability Deployment Price Adder for Ancillary Services: December 2025 OD 12/8 had the highest daily time-weighted average RT RDPA for Ancillary Services.
The daily average values are calculated as time-weighted average Real-Time Reliability Deployment Price Adders for each Ancillary Service during SCED intervals with RDPA active for any reliability event trigger.
The RDPAs on 12/8 were triggered by both RUC and the deployment of Non-Spin from Non-Controllable Load Resources.
The RDPAs on 12/11 were triggered by the deployment of Non-Spin from Non-Controllable Load Resources.
The RDPAs on 12/18 were triggered by RUC only.
RDPA | Monthly Time Weighted Average ($/MWh)*
Regulation Up (Reg-Up) | 0.15
Regulation Down (Reg-Down) | 0.08
Non-Spinning Reserves (Non-Spin) | 0.14
Responsive Reserve Service (RRS) | 0.11
ERCOT Contingency Reserve Service (ECRS) | 0.11
* RDPAs for Ancillary Services are only available after RTC+B implementation on December 5, 2025

## Slide 14: RUC Make-Whole, Clawback, and Shortfall For December 2025, the total Make-Whole Payment was $271,995 and was lower than in previous months. The total Clawback Charge was $233,499, slightly higher than in previous months.
Of the $271,995 in Make-Whole Payments made in December 2025, $0.82 was uplifted to load due to rounding.
The remaining amount was collected through Capacity-Short Charges.
Data as of December 9th, 2025

## Slide 15: RUC Make-Whole by Settlement Type For December 2025, the total Make-Whole Payment was $271,995 in Initial Settlement. It was almost exclusively covered by Capacity Short Charge, and only $0.82 was uplifted to load due to rounding.
Negative dollars represent a payment from ERCOT to a market participant
“-” indicates settlement has yet to be completed.
Net figures may differ slightly due to rounding.
Month | Initial Settlement ($) | Final Settlement Change ($) | True-up Settlement Change ($) | Net as of Jan 4, 2026 ($)
Dec ‘24 | -179,587 | 0 | -53,342 | -232,929
Jan ‘25 | -834,867 | -80,530 | -1,947,157 | -2,862,554
Feb ‘25 | -1,198,579 | -17,762 | -4,344,131 | -5,560,472
Mar ‘25 | -1,701,707 | 0 | -111,462 | -1,813,169
Apr ‘25 | -594,864 | -3,693 | 104,830 | -493,728
May ‘25 | -493,728 | 0 | - | -
Jun ‘25 | -1,285,661 | 0 | - | -
Jul ‘25 | -382,594 | -294 | - | -
Aug ‘25 | -487,773 | 0 | - | -
Sep ‘25 | -2,035,251 | - | - | -
Oct ‘25 | -1,016,193 | - | - | -
Nov ‘25 | -1,119,452 | - | - | -
Dec ‘25 | -271,995 | - | - | -

## Slide 16: RUC Clawback by Settlement Type For December 2025, the total Clawback Charge was $233,499 in Initial Settlement.
Negative dollars represent a payment from ERCOT to a market participant
“-” indicates settlement has yet to be completed.
Net figures may differ slightly due to rounding.
Month | Initial Settlement ($) | Final Settlement Change ($) | True-up Settlement Change ($) | Net as of Jan 4, 2026 ($)
Dec ‘24 | 147,389 | -3 | 0 | 147,386
Jan ‘25 | 1,037,717 | 0 | -294,094 | 743,623
Feb ‘25 | 3,272,312 | 0 | -2,138,639 | 1,133,673
Mar ‘25 | 545,642 | 0 | -87,084 | 458,558
Apr ‘25 | 993,341 | 119 | -418,816 | 574,643
May ‘25 | 574,643 | 0 | - | -
Jun ‘25 | 173,176 | 0 | - | -
Jul ‘25 | 246,345 | 134 | - | -
Aug ‘25 | 12,319 | 0 | - | -
Sep ‘25 | 122,634 | - | - | -
Oct ‘25 | 128,343 | - | - | -
Nov ‘25 | 61,933 | - | - | -
Dec ‘25 | 233,499 | - | - | -