## Slide 1: Batch Zero Loads An Alternative Approach
Large Load Working Group 1/22/26

## Slide 2: Batch Study Process
Current study process is linear
  Projects are studied without honoring other loads in the process
  Leads to restudies to ensure all load can be served (whack-a-mole)
  With volume of requests the results have been untenable
Batch studies review needs of all loads in the batch
  Transmission solutions are created for all loads in the batch
  Solution should be most efficient group of lines to solve potential issues
  Can require limits to ensure the model doesn’t “blow up”
  With sufficient study runs the queue will be fully served in time

## Slide 3: Batch Zero
Initial run of the batch process
Load selection will be critical
ERCOT’s proposal is discriminatory to certain utility loads:
  “Requests that have met certain milestones but require restudy will be included in Batch Zero”
  For whatever reason, Oncor did not submit many of their loads in the process
  Oncor represents 35% of system load and likely a much larger share of interconnections requested
  This would disenfranchise a significant portion of ERCOT load
There is an alternative solution

## Slide 4: SB6 Ratio Share Allocation
What can be done is to create an “SB6 Ratio Share” allocation of large load requests as follows:
Step 1 – ERCOT determines the total capacity they believe can solve in the Batch Study
Step 2 – TSPs create lists of their SB6 compliant loads for submission to ERCOT
Step 3 – ERCOT uses a Ratio Share allocation for the load to include from each TSP
  TSP Allocation = (TSP SB6 Large Load/Total SB6 Large Load) * Study Capacity
Step 4 – The loads from each TSP are stacked by original submission date and loads are included until their allocation is reached
  Load zone separation can also be provided if desired
  Partial allocations for the “final load” may occur
  This is likely needed for smaller systems
  Partial loads will be carried over to subsequent batches until all the load is served

## Slide 5: Example
Step 1 – ERCOT establishes 50GWs as the study limit
Step 2 – Oncor has 120GWs of SB6 compliant load and provides that list to ERCOT in Submission Date order
Step 3 – ERCOT determines that there are 240GWs total SB6 compliant load from all TSPs in ERCOT
  Oncor’s allocation in Batch Zero is: 120GW/240GW * 50GW = 25GW
Step 4 – ERCOT goes down Oncor’s date ordered list until 25GWs is reached
  If needed a partial allocation is provided to the last load in the list
ERCOT applies this same logic to all other TSPs and creates its aggregate load list

## Slide 6: Benefits of the Proposal
Non-discriminatory – it provides Batch Zero access to loads of all the TSPs
  Methodologies using the factors from the existing process carry lingering biases that existed in that process
Repeatable – This methodology can be continued until the queue is cleared and afterward should a future batch study become overloaded (literally)
Doesn’t rely on factors that vary from TSP to TSP such as Signed Interconnect Agreements
Compliant with SB6 – Some loads that are in “restudy” have likely not met all criteria

## Slide 7: Questions?