## Slide 1
Annual Review of the Market Impacts of Reliability Unit Commitments
Analysis of 2025
Zhengguo Chu
Supervisor, Market Analysis
TAC
January 21, 2026
ERCOT Public

## Slide 2: Protocol Language
5.8 Annual RUC Reporting Requirement
  (1) ERCOT shall report to the Technical Advisory Committee (TAC), each January, an assessment of market impacts and Settlements for the aggregate Reliability Unit Commitment (RUC) activity, delineated by type of RUC instruction as follows:
(a) RUC instructions issued for irresolvable transmission system constraints;
(b) RUC instructions issued in anticipation of extreme cold weather/startup failures;
(c) RUC instructions issued for capacity;
(d) RUC instructions issued for expected Energy Storage Resource (ESR) energy consumption;
(e) RUC instructions issued for system inertia;
(f) RUC instructions issued to Resources receiving an Outage Schedule Adjustment (OSA); and
(g) A summary of RUC Settlements;
(i) RUC charges associated with RUC Make-Whole Amount Total per RUC, as defined in Section 5.7.4.1, RUC Capacity-Short Charge; and
(ii) RUC Shortfall Total, as defined in Section 5.7.4.1.1, Capacity Shortfall Ratio Share.

## Slide 3: Key Observations for 2025
Overall increase in the amount of RUC observed in 2025 (~5,300 Resource-hours) v. 2024 (~2,000 Resource-hours) and 2023 (2,500 Resource-hours). Factors that may have contributed to this trend include:
  A combination of rapid load growth and increased renewable penetration resulting in more congestion and less self-commitment by thermal resources.
  Limitations on ESR energy capability in pre-RTC RUC based on the COP target Hour Beginning State-of-Charge (HBSOC).
Change in the composition of RUC in 2025 compared to 2024
  In 2025, ~81% of total RUC effective Resource-hours were attributed to congestion concerns, compared to ~38% in 2024.
  Since Real-Time Co-optimization Plus Batteries (RTC+B) launched on December 5th, 2025, RUC commitments have been noticeably lower than in previous months. Factors that may have contributed to this trend include:
  The ability of RTC RUC to manage congestion by re-allocating both Energy and Ancillary Services among Resources without committing additional offline Resources.
  The ability of RTC RUC to trade off between Energy and Ancillary Services.
  Improved accuracy of COP target HBSOC data since RTC go-live.

## Slide 4: RUC-Instructed Resource-Hours in 2025
* The difference between “Instructed” and “Effective” values is a result of Resources starting up, shutting down, partial hour instructions, or otherwise not dispatchable by SCED.
 | Total | Capacity |  | Congestion | 
 |  | Opt-Out | Non-Opt-Out | Opt-Out | Non-Opt-Out
Instructed Resource-Hours |  |  |  |  | 
Total Count | 5336.4 | 36.0 | 944.4 | 84.0 | 4271.0
Effective Resource-Hours* |  |  |  |  | 
Total Count | 5128.7 | 37.9 | 915.7 | 78.9 | 4096.2
Average Megawatts (MW) for Effective Resource-Hours |  |  |  |  | 
Average LSL | 71.0 | 160.9 | 84.2 | 86.1 | 66.9
Average LDL | 77.2 | 184.2 | 90.6 | 117.2 | 72.4
Average BP | 79.4 | 216.2 | 91.5 | 142.1 | 74.2
Average HSL | 239.3 | 334.7 | 252.3 | 246.0 | 235.5

## Slide 5: RUC Instruction Reasons
5128.7 effective RUC Resource-hours in 2025,
  4,175.1 Resource-hours (81.4%) were attributed to resolving local thermal congestion or voltage concerns.
  953.6 Resource-hours (18.6%) were attributed to capacity concerns.
    7.6 of those 953.6 Resource-Hours were issued to Resources receiving an Outage Schedule Adjustment (OSA).
There were no Resource-hours committed for Ancillary Service shortages, system inertia, startup failures, or expected Energy Storage Resource (ESR) energy consumption.
116.8 effective Resource-hours (2.3%) were successfully bought back.
  This value is much less than last year (6.3% bought back in 2024).
  Included in this value are 51.0 effective Resource-hours (1.0% of total) where the Resource was DAM-committed.

## Slide 6: RUC-Effective Resource-Hours, 2022 - 2025
89 out of 131 Effective Resource-Hours in December 2025 occurred before the implementation of Real-Time Co-Optimization Plus Batteries (RTC+B)

## Slide 7: RUC-Effective Resource-MWh, 2022 - 2025
Top: Duration multiplied by Resource’s Base Point (BP).
Bottom: Duration multiplied by Resource’s High Sustained Limit (HSL).

## Slide 8: RUC Lead Time Margin
Lead time refers to the length of time between a RUC instruction and the start of the commitment window.
Lead time margin is the difference between lead time and the Resource’s startup time.
  In cases where a Resource is committed for multiple back-to-back time blocks, lead time margin is calculated from the first instruction.
Most RUC commitment windows had a lead time margin of 2 hours or less.

## Slide 9: Average Age of Effective Resource-Hours, 2022 - 2025
In the case of Resources with multiple physical generators, the age of the oldest generator is used.

## Slide 10: RUC-Effective Resource-Hours by Resource Age, 2022 - 2025
OPT-OUT
NON-OPT-OUT

## Slide 11: RUC-Effective Resource Dispatch above LDL
When Resources did not successfully opt out, there were 248.6 Resource-hours when the Resource was dispatched above its LDL.
  For 67.4 of these Resource-hours, the LMP for the RUC-instructed Resource was above the RUC offer floor.
  For 181.2 of these Resource-hours, the LMP for the RUC-instructed Resource was below the RUC offer floor.
    For 181.2 of these Resource-hours, the RUC-instructed Resource was mitigated.
    There were no Resource-hours associated with a RUC for additional capacity.
    There were no Resource-hours for which a non-mitigated RUC-instructed Resource was DAM-committed. (Hours meeting these criteria are treated as a RUC opt out.)

## Slide 12: Reliability Deployment Price Adder
Note:
These graphs show RTORDPA instances by reliability action: 'RUC Only' for instances triggered solely by Reliability Unit Commitment, 'RUC and other triggers' for instances with RUC and additional triggers, and 'Other triggers only' for instances with only non-RUC triggers. The monthly average RTORDPA is calculated using the total duration across all categories. See ERCOT protocol section 6.5.7.3.1 for details.
Month of 2025 | Total RTORDPA Time (Hours) | Time-weighted Average RTORDPA ($/MWh)
Jan | 111.75 | 4.64
Feb | 213.57 | 3.90
Mar | 219.67 | 2.31
Apr | 180.34 | 0.92
May | 97.75 | 1.95
Jun | 171.34 | 1.01
Jul | 105.26 | 1.37
Aug | 141.93 | 0.83
Sep | 238.34 | 0.94
Oct | 137.25 | 1.22
Nov | 123.84 | 1.18
Dec | 65.19 | 1.59
Since the implementation of Real-Time Co-Optimization Plus Batteries (RTC+B) on December 5, 2025, through the end of December 2025, the time-weighted average Real-Time Reliability Deployment Price Adders for each Ancillary Service during SCED intervals with RDPA active for any category are presented in the following table in ($/MWh):
RTRDPARUS | RTRDPARDS | RTRDPARRS | RTRDPAECRS | RTRDPANSS
0.15 | 0.08 | 0.11 | 0.11 | 0.14

## Slide 13: RUC Make-Whole and Claw Back, 2022 - 2025
$20.03M in Make-Whole paid out over the year. Only $701.19 uplifted to Load. Settlement data retrieved 01/09/2026.

## Slide 14: Summary
In 2025, 5,336 instructed RUC Resource-hours resulted in 5,129 effective RUC Resource-hours.
  As compared to 1,976 and 1,861 for 2024, respectively.
  2.3% of effective resource-hours were bought back.
The total RUC make-whole amount was ~$20.03M.
  Almost exclusively covered through capacity-short charges.
The total RUC claw back charge amount was ~$4.60M.
Initial data after the December 5, 2025 implementation of Real-Time Co-Optimization Plus Batteries (RTC+B) shows a noticeable reduction in RUC commitments compared to earlier months.
Settlement data retrieved 01/08/2026

## Slide 15: Appendix

## Slide 16: RUC Effective Resource-Hours by Opt Out Status*
Did Not Opt Out
Opted Out
* Effective Resource-hours rounded to nearest whole number
Month | 2022 | 2023 | 2024 | 2025
Jan | 80 | 167 | 101 | 321
Feb | 930 | 249 | 17 | 766
Mar | 200 | 147 | 209 | 654
Apr | 328 | 362 | 376 | 294
May | 382 | 445 | 71 | 214
Jun | 511 | 309 | 73 | 377
Jul | 672 | 114 | 21 | 227
Aug | 870 | 11 | 170 | 416
Sep | 1124 | 74 | 98 | 788
Oct | 305 | 33 | 235 | 439
Nov | 517 | 73 | 143 | 384
Dec | 381 | 7 | 229 | 131
Month | 2022 | 2023 | 2024 | 2025
Jan | 26 | 99 | 28 | 1
Feb | 62 | 0 | 0 | 44
Mar | 62 | 38 | 0 | 25
Apr | 163 | 42 | 25 | 6
May | 219 | 102 | 0 | 10
Jun | 108 | 31 | 11 | 25
Jul | 236 | 67 | 0 | 0
Aug | 176 | 2 | 13 | 0
Sep | 225 | 41 | 0 | 0
Oct | 106 | 12 | 20 | 0
Nov | 209 | 76 | 17 | 6
Dec | 19 | 0 | 5 | 0

## Slide 17: RUC Make-Whole and Claw Back, 2022-2023
Amounts rounded to nearest thousand. Settlement data retrieved on 01/09/2026.
Month | RUC Make-Whole Amount ($1000s) |  | RUC Capacity-Short Charges ($1000s) |  | Uplift Charges ($1000s) |  | Claw Back Charges ($1000s) |  | RUC Shortfall Total (MWh in 1000s) | 
 | 2022 | 2023 | 2022 | 2023 | 2022 | 2023 | 2022 | 2023 | 2022 | 2023
Jan | -320 | -301 | 320 | 301 | 0 | 0 | 38 | 822 | 3760 | 1886
Feb | -6970 | -327 | 6970 | 327 | 0 | 0 | 7628 | 157 | 7519 | 3045
Mar | -749 | -441 | 749 | 441 | 0 | 0 | 102 | 180 | 6203 | 5695
Apr | -742 | -914 | 742 | 914 | 0 | 0 | 1285 | 50 | 7138 | 11694
May | -3302 | -470 | 3302 | 470 | 0 | 0 | 7293 | 364 | 10604 | 8601
Jun | -6014 | -687 | 6014 | 687 | 0 | 0 | 12 | 149 | 17784 | 8007
Jul | -9841 | -168 | 9841 | 168 | 0 | 0 | 5245 | 158 | 17799 | 5138
Aug | -13274 | -12 | 13274 | 12 | 0 | 0 | 110 | 352 | 15788 | 322
Sep | -8806 | -35 | 8806 | 35 | 0 | 0 | 208 | 998 | 20310 | 562
Oct | -3675 | -116 | 3675 | 116 | 0 | 0 | 80 | 191 | 9482 | 757
Nov | -5665 | -213 | 5665 | 213 | 0 | 0 | 689 | 30 | 10589 | 2554
Dec | -10768 | -5 | 10768 | 5 | 0 | 0 | 0 | 0 | 6713 | 305

## Slide 18: RUC Make-Whole and Claw Back, 2024-2025
Amounts rounded to nearest thousand. Settlement data retrieved on 01/09/2026.
Month | RUC Make-Whole Amount ($1000s) |  | RUC Capacity-Short Charges ($1000s) |  | Uplift Charges ($1000s) |  | Claw Back Charges ($1000s) |  | RUC Shortfall Total (MWh in 1000s) | 
 | 2024 | 2025 | 2024 | 2025 | 2024 | 2025 | 2024 | 2025 | 2024 | 2025
Jan | -302 | -2863 | 302 | 2863 | 0 | 0 | 103 | 744 | 2724 | 13585
Feb | -29 | -5560 | 29 | 5560 | 0 | 0 | 88 | 1134 | 867 | 20488
Mar | -354 | -2436 | 354 | 2436 | 0 | 0 | 487 | 443 | 4756 | 24059
Apr | -478 | -652 | 478 | 652 | 0 | 0 | 2080 | 993 | 7897 | 14360
May | -3 | -1267 | 3 | 1267 | 0 | 0 | 2084 | 306 | 952 | 12641
Jun | -134 | -1808 | 134 | 1808 | 0 | 0 | 0 | 173 | 5413 | 19630
Jul | -114 | -479 | 114 | 478 | 0 | 1 | 0 | 227 | 1424 | 11318
Aug | -353 | -488 | 353 | 488 | 0 | 0 | 74 | 12 | 7150 | 18097
Sep | -432 | -2035 | 432 | 2035 | 0 | 0 | 132 | 123 | 5449 | 31663
Oct | -437 | -1020 | 437 | 1020 | 0 | 0 | 179 | 128 | 11868 | 18354
Nov | -482 | -1152 | 482 | 1152 | 0 | 0 | 1763 | 81 | 5278 | 16195
Dec | -233 | -272 | 233 | 272 | 0 | 0 | 147 | 233 | 8110 | 5607