## Slide 1
NPRR 1317 Creation of Non-Settled Generator (NSG) and Clarification of the Types, Usage, and Registration of Distributed Generation
Thinesh Devadhas Mohanadhas / Douglas Fohn
ERCOT

## Slide 2: NPRR 1317 Creation of Non-Settled Generator (NSG) and Clarification of the Types, Usage, and Registration of Distributed Generation
This NPRR incorporates the Resource Definition Task Force’s (RTF’s) RTF-5 defined terms “Non-Settled Generation” (NSG) to clarify the appropriate use of Distributed Generation (DG) or subtype of DG throughout the Protocols and meets the RTF’s objectives to “identify problematic terms” in the Protocols and “improv[e] the current structure and terms where practical.”
An NSG is not a Market Participant (MP). An NSG is a generator, including an Energy Storage System, with a nameplate capacity that is greater than 1 MW that is not registered with ERCOT as a different registrant type (i.e. Generation Resource, Settlement Only Generator, Energy Storage Resource, or Settlement Only Energy Storage System). Any NSG exports are NOT entitled to Settlement and will not be used for Settlement purposes.
NSG enables ERCOT to gain visibility into distributed and transmission generators that are not registered as any MP type by collecting basic registration details (>1 MW) and telemetry data (>10 MW).
NSG does not apply to generators that are:
  Registered with ERCOT as an MP; or
  That are not capable of being connected in parallel operation to the ERCOT System.
Notes: https://www.ercot.com/calendar/04162020-RTF-Meeting-by-WebEx

## Slide 3: RTF-5 Generation Framework
***
Notes: https://view.officeapps.live.com/op/view.aspx?src=https%3A%2F%2Fwww.ercot.com%2Ffiles%2Fdocs%2F2020%2F04%2F16%2FRTF5_Proposed_Revisions_to_Generation_Framework_v4.pptx&wdOrigin=BROWSELINK

## Slide 4: NSG Definitions
Non-Settled Generator (NSG)
A generator, including an Energy Storage System (ESS), with a nameplate capacity greater than one MW that is not registered with ERCOT as a Generation Resource, Settlement Only Generator (SOG), Energy Storage Resource (ESR), or Settlement Only Energy Storage System (SOESS). NSG exports to the ERCOT System are not entitled to Settlement and will not be used for Settlement purposes.
Non-Settled Distribution Generator (NSDG)
An NSG that is a Distributed Generator (DG).
Non-Settled Transmission Generator (NSTG)
An NSG that is either (i) directly or (ii) indirectly connected to the ERCOT Transmission Grid and that may be connected in parallel operation to the ERCOT System.

## Slide 5
Distributed Generation (DG)
Unregistered Distribution Generator (UDG)*
Typically ≤1 MW
Rooftop solar
Fossil-fuel units (Natural gas-fired and diesel)
Small commercial solar
Settlement- Only Distributed
Generator (SODG)
Typically <10 MW
Batteries
Compensated for energy and Ancillary Services
Compensated for energy
Distribution Generation Resources (DGR)
Typically <10 MW
Utility-scale solar
Fossil-fuel units (Natural gas-fired and diesel)
Commercial solar
Other technologies
Non-Settled Distribution Generator (NSDG)
Typically >1 MW
Utility-scale solar
Commercial solar
Fossil-fuel units (Natural gas-fired and diesel)
*NPRR 1265 Unregistered Distributed Generator
Fossil-fuel units (Natural gas-fired)
Batteries
NPRR 1317

## Slide 6: Douglas.Fohn@ercot.com Thinesh.DevadhasMohanadhas@ercot.com Thank You