## Slide 1
Overview/Discussion for
NPRR 1315 (Changes to Process of Evaluating the Potential Needs for Additional Capacity)
ERCOT Staff
PRS
February 11, 2026

## Slide 2: 1) RMR-MRA-C4C Workshop 10-17-25. 2) Reviewed feedback received after the Workshop. 3) NPRR 1315 posted December 12-19-25. (Along with 4 other RMR-MRA-C4C related NPRRs.) 4) Initial discussion January 2026 PRS meeting. (NPRR 1315 was not remanded to WMS.) Discussion expected at the February PRS. 5) Discussed NPRR 1315 with several Market Participants after January 2026 PRS. 6) NPRR 1315 not discussed at 2-4-26 WMS meeting 7) Second PRS discussion 2-11-26
History/Overview

## Slide 3: Overview of Protocol Revisions
Summary of NPRRs:
  NPRR 1315 - Changes to Process of Evaluating the Potential Needs for Additional Capacity:
    Extend the Study Horizon Beyond the Current or Next Season when evaluating the potential needs for capacity based on ERCOT’s requirement per PURA 39.151(a),
    Expand the Set of Eligible Resources to Include New Resources,
    Allow Incentive Factors Other Than 10% for Resources Contracted Under Section 6.5.1.1
    Add notification requirements for ERCOT to PUCT
  NPRR 1316 - Implement an Annual ERCOT RFI Process to Gather Information Related to Retirement and Mothballing Plans of Select Resources
  NPRR 1319 -Modifications to Seasonal Mothball Periods and Clarification to Evaluation Process
  NPRR 1313 - Adjustment to the Calculation of the Initial Standby Cost for RMR Resources
  NPRR 1318 - Specific Exclusion of the Incentive Factor to ERCOT Approved Outside Attorney Fees and Approved Emissions Costs
At the Workshop there was discussion on the idea of changing the Notice of Suspension of Operation (NSO) deadline to allow for more than the current 150-day notice. However, the 150-day notice is mandated by PUCT Rule. Therefore, no NPRR has been written to address this issue as any change would have to be made to the PUCT rule first.

## Slide 4: Contract for Capacity (C4C)
The Public Utility Regulatory Act (PURA) §39.151 (a) (2) requires that ERCOT must …Ensure the reliability and adequacy of the regional electrical network.
  Protocol Section 6.5.1.1 ERCOT Control Area Authority:
  (1) (e) Perform additional actions required to prevent an imminent Emergency Condition or to restore the ERCOT Transmission Grid to a secure state in the event of an ERCOT Transmission Grid Emergency Condition.
  (4) Consistent with paragraph (1)(e) above, if ERCOT seeks to exercise its authority to prevent an anticipated Emergency Condition relating to serving Load in the current or next Season by procuring existing capacity that may be used to maintain ERCOT System reliability in a manner not otherwise delineated in these Protocols and the Nodal Operating Guides, ERCOT shall take the following actions: …….
ERCOT calls this a Contract for Capacity (C4C) and follows an open, RFP process for procurement.

## Slide 5: Protocol Language [Section 6.5.1.1 ERCOT Control Area Authority paragraph (4)]
(4) Consistent with paragraph (1)(e) above, if ERCOT seeks to exercise its authority to prevent an anticipated Emergency Condition relating to serving Load in the current or next Season by procuring existing capacity that may be used to maintain ERCOT System reliability in a manner not otherwise delineated in these Protocols and the Nodal Operating Guides, ERCOT shall take the following actions:
(a) Upon determination by ERCOT that additional capacity is needed to prevent an Emergency Condition and prior to any procurement activity associated with such additional capacity, ERCOT shall issue a Notice as soon as practicable with the following information:
(i) A detailed description of the reliability condition and need for additional capacity as determined by ERCOT and the timing of the proposed procurement;
(ii) Justification for the quantity of additional capacity to be requested;
Identification of potential Generation Resources or Load providing capacity considered by ERCOT to be acceptable for providing the additional capacity. Load capacity may be provided by Entities who, at ERCOT’s direction, would interrupt consumption of electric power and remain interrupted until released by ERCOT; and
A schedule of activities associated with the proposed procurement.

## Slide 6: Protocol Language [Section 6.5.1.1 ERCOT Control Area Authority paragraph (4)] continued
(4) (c) (ii)
Each contract will include specified financial terms and termination dates. For purposes of Settlement, any contract associated with a Generation Resource or ESR will include substantially the same terms and conditions as an RMR Unit under a RMR Agreement, including the Eligible Cost budgeting process.

## Slide 7: Change Time Horizon and Capacity Types for Contract for Capacity
Objective: Successful procurement of capacity to maintain reliability
Proposal:
Extend the study horizon beyond the current or next season and modify "by procuring existing capacity" to allow for proposals of “existing or new” resources.
  ERCOT proposes the following:
  Allow for a C4C analysis over a 2-year study horizon instead of analysis limited to the current or next season.
  Lengthen the C4C timeline between RFP issuance and offering entity responses to allow more time for entities to submit offers.
  Allow for a contract period longer than one season, if studies support the need.
Note: This does not require a PUCT Rule change.

## Slide 8: Change Time Horizon and Capacity Types for Contract for Capacity
Benefits:
ERCOT will have more time to:
  Assess the necessity of a C4C and to identify any potential grid reliability risks associated with the identified capacity shortfall.
  Develop the Request for Proposal (RFP) for C4C services.
  Evaluate C4C Offers.
There will be more time for Market Participants to develop suitable resource proposals and submit C4C Offers that meet specifications identified in the RFP.
There will be more time for awarded resources to get ready to meet their C4C contractual obligations.

## Slide 9: Discussion Items
When is the use of C4C procurement acceptable?
  Has this policy question already been answered with the PURA language?
  Only for projected system-wide insufficiency?
  Only for projected local transmission issues?
  Both for system-wide insufficiency or local transmission issues?
  What is the process and input data used to project the state of the system for future months?
What types of Resources/Capacity should be eligible? (Need to improve NPRR language)
  Existing Resources (Mothballed or Retired)
  Resources in the queue that could accelerate their Commercial Operation Date (COD)
  New Resources (mobile generation and ESRs) that can be installed quickly
  Demand Response
    Only new DR
    Any DR that appears to have responded to price prior to the posting of this RFP is not eligible
  Newly added Settlement Only Generation (covers load only or covers load and has net injection)
  Settlement Only Generation existing prior to the posting of the RFP is not eligible

## Slide 10: Discussion Items (Continued)
What incentive factor should be used? Options:
  Substantially similar to RMR contract (current language of Protocols)?
  An Incentive Factor with a cap? 15%, 25% 75%????
  An Incentive Factor/budget approach only for existing (mothballed or retired) and all the others submit offers and payment is “paid as offered” … (no receipts and no Incentive Factor)?
Can and should the impact of new Demand Response be captured and used to make sure the Real-Time Prices are not decreased? (A separate NPRR?)
Can and should the impact of new small generation not directly seen by SCED as Resource be captured and used to make sure the Real-Time Prices are not decreased? (A separate NPRR?)

## Slide 11
  Questions?

## Slide 12: Appendix

## Slide 13: Recent History Prompting NPRRs related to Reliability Must-Run (RMR), Must-Run Alternative (MRA) and Contract for Capacity Provisions:

## Slide 14: Recent Capacity Procurement Background
Resource | Contract Type | Rated Capacity | MRA Awarded | Service Period | Number of Deployments | Actual Termination Month | Budget | Final Actual Costs
Greens Bayou 5A | RMR | 371MW | None | June 1, 2016, through June 30, 2018 | None | May 2017 | Approx. $58M | Approx. $22M
Braunig 3B | RMR | 400 MW | None | March 2, 2025, through March 1, 2027 | TBD | TBD | Approx. $46M | Pending
Lifecycle Mobile GenerationC | Emergency Generation Service | 450 MW | N/A | June 4, 2025, through March 31, 2027 | TBD | TBD | Approx. $54M | Pending
ANote: An MRA RFP was issued for GBY5. 8 offers from 4 QSEs. No MRA awards.
BNote: An MRA RFP was issued for the three Braunig Units. One offer from one QSE. No MRA awards.
CNote: An RFP was issued seeking alternative(s) to Lifecycle Power Mobile Generation and Braunig Units 1 & 2. Three offers, including one valid offer, were received. No awards.

## Slide 15: “C4C-Like” and C4C Background
ID | RFP Posting and Responses | Service Period | Max. Quantity Requested | Responses Received | Number of Deployments | Notes
1 | No RFP posted. ERCOT negotiated with 2 entities and contracted for 4 Resources | ~08/15/2011 - 10/31/2011 | Initially 310 MW were under contract. One Resource (118 MW) was cancelled one month after the contract was signed | N/A | None | Mothballed Resources returned to service to help with the potential of ERCOT-Wide Insufficiency. This procurement was conducted before NPRR 432 was effective which added specific C4C protocol language
2 | RFP posted 10/02/2023 Responses due 11/06/2023 | 12/01/2023 -02/29/2024 | 3,000 MW | 11.1 MW | N/A | The RFP was seeking generation or Demand response capacity to help with potential ERCOT-Wide Insufficiency RFP cancelled 11/17/2023
3 | RFP posted 05/08/2024 Responses due 06/13/2024 | ~07/01/2024 - 09/30/2024 | 500 MW | 21.5 MW Ultimately only 6.5 MW deemed eligible | N/A | The RFP was seeking Demand response capacity to help provide relief on relevant transmission facilities (South Texas IROLs) RFP cancelled 06/21/2023

## Slide 16: Impact Analysis Info and Potential PRS Assignments
NPRR | Title | Likely PRS Assignment to Subcommittees | Impact Analysis Date | Estimated Cost/Budget Impact | Estimated Time Requirements | ERCOT Staffing Impacts (across all areas) | ERCOT Computer System Impacts | ERCOT Business Function Impacts | Grid Operations & Practices Impacts
1313 | Adjustment to the Calculation of the Initial Standby Cost for RMR Resources | WMS | 12/16/2025 | None | No Project | None | None | ERCOT will update its business processes | None
1315 | Changes to the Process of Evaluating the Need for Additional Capacity | WMS and ROS | 12/19/2025 | None | No Project | None | None | None | None
1316 | Implement an Annual ERCOT RFI Process to Gather Information Related to Retirement and Mothballing Plans of Select Resources | WMS | 12/19/2025 | Less than $10k | O&M, less than four hours | None | None | None | None
1318 | Specific Exclusion of the Incentive Factor to ERCOT Approved Outside Attorney Fees and Approved Emissions Costs | WMS | 12/23/2025 | None | No Project | None | None | ERCOT will update its business processes | None
1319 | Modifications to Seasonal Mothball Periods and Clarification to Evaluation Process | WMS and ROS | 12/29/2025 | None | No Project | None | None | ERCOT will update its business processes | None