## Slide 1
OBDRR055 - Revisions to Non-Spinning Reserve Deployment and Recall Procedure for RTC+B
TAC
2/25/2026

## Slide 2: Overview
ERCOT has submitted OBDRR055 to reflect these key changes:
  Remove outdated references of Ancillary Service Responsibility and Schedules, telemetered schedule performance monitoring, HASL calculation, Non-Spin deployment grouping, online Generation Resource sand Controllable Load Resources
  Add in references for RTC+B AS Awards
  Enhance the offline Non-Spin deployment trigger
ERCOT previously presented at RTCBTF on 12/15/2025, and 1/20/2025, and PDCWG on 2/18/2026 to share updates needed for Non-Spinning Reserve Deployment and Recall Procedure. These changes were needed to align the procedure with ERCOT market rules that are now effective post implementation of RTC+B. This OBDRR also enhances the trigger calculation that is used to recommend deployment of offline Non-Spin such that it takes the available energy into account when assessing capability to meet the 30-minute out forecasted Load.
We are requesting TAC’s endorsement, at this meeting or by the next, to allow review and approval at Board meeting in April, followed by the PUC review and approval before summer. Please note, that this trigger is available to the control room today for situational awareness.

## Slide 3: Impact on offline Non-Spin Deployment for 1/28/2026
On this morning, we see the current trigger does not indicate a need to deploy offline Non-spin, which is due to some of the short limitations mentioned on the previous slide.
Operators, using awareness system conditions deployed offline Non-Spin at ~7:00.
The Proposed Trigger suggests a deployment at ~6am due to AS Plan shortfall and dwindling ESR capability, and increased Non-Spin not covered by thermal Resources.
Shaded area represents offline Non-Spin Deployment

## Slide 4: Questions?