## Slide 1: LLWG Update: Large Load Interconnection Batch Study Workshops
Matt Mereness
March 13, 2026

## Slide 2: Batch Zero revision request timeline
Forums
Workshops and working groups
PRS (Protocols Review Subcommittee)
ROS (Reliability and Operations Subcommittee)
TAC
ERCOT Board
2026
Q1
Q2
Q3
Feb
Mar
Apr
May
Jun
Jul
Workshop #2 Feb 12
Workshop #4 Mar 10
Workshop #5 Mar 24
Workshop #6 Mar 30
PRS Update 3/11
ROS Update 3/5
ROS Vote 5/7
Board Vote 6/1
3/4 ERCOT files Batch Zero Revision Request(s)
8/1 Target effective date of protocols
Objective
Align stakeholders on direction/scope following Commission decision
Define the scope, boundaries, and intended role of Batch Zero
Preview structure/governing concepts of Batch Zero NPRR before filing
Confirm proposed protocol changes are ready for governance review
Endorse NPRR 1325 for advancement to TAC
File PGRR145 for Workshops and ROS review
Endorse PGRR145 for advancement to TAC
Review/endorse combined NPRR/PGRR package for Board approval
Consideration Batch Zero NPRR/PGRR
LLWG Feb 19
Workshop #3 Feb 26
TAC Vote 5/19-20
Close outstanding design and drafting issues, incorporate vetted stakeholder feedback, and finalize Revision Request language for committee approval
Target Board approval date
Board Meeting 4/20
Regular PRS 4/15
ROS Update 4/2
Monthly TAC updates
Workshop #7 Apr 9
Note that TAC leadership is involved in considering options to ensure successful review and approval
Special PRS 4/22
Regular TAC 4/29
Special TAC 5/13
PRS Vote 5/6
Monthly LLWG updates
Apr (TBD) ERCOT files CLR/BYOG Revision Request(s)

## Slide 3: Revision Request Process Flow
Comments may be filed between each step of the process.
Comments for NPRR1325 may be submitted using the Comments Form found here.
Comments for PGRR145 may be submitted using the Comments Form found here.
NPRR Comments
PGRR Comments
Large Load Interconnection Workshops
NPRR/PGRR
Review
BOARD
PUCT
TAC
ROS
PGRR Language/IA Review
PRS
NPRR Language/IA Review

## Slide 4: Reminder of Scope and Priorities for Workshops
March 4 filings completed for Batch Zero: ERCOT filed the Batch Zero PGRR145 and related NPRR1325 on March 4, initiating the formal governance process and aligning with the May PRS/ROS/TAC sequence and June 1 Board target reflected in the critical path timeline
Additional filings on target (CLR and BYOG): ERCOT is advancing targeted revision requests to clarify CLR and BYOG treatment and is currently targeting an April filing (TBD)
Continuous feedback collection: ERCOT follow-up stakeholder survey to gather additional input (e.g., eligibility criteria, development activity standards) for Batch Zero, CLR, and BYOG. Responses are being evaluated and incorporated, where appropriate, to further refine the proposal
Long-term Batch Process revisions: development of the enduring batch framework is out of scope for the current filing. ERCOT will incorporate lessons learned from Batch Zero to inform future revision requests and the design of a durable, repeatable batch study process

## Slide 5: Process redesign survey insights summary
CLR and BYOG
BYOG Self-Limiting Facility
F2
Stakeholders broadly support the BYOG self-limiting facility framework as a workable interim solution until transmission upgrades are completed
BYOG Configurations
F1
Stakeholders strongly prefer co-location models anchored by dispatchable thermal generation, particularly when paired with storage
Key insights
Key questions
Module
CLR as a bridge solution
F3
Stakeholders broadly support leveraging CLR as a bridge solution to access additional capacity while transmission upgrades are under development
CLR concept expansion
F4
Stakeholders broadly favor formalizing CLR within the BYOG framework, signaling strong interest in maintaining operational flexibility within co-location models
Pre-registration of non-firm MW as CLR
F5
Stakeholders broadly favor enabling pre-registration of non-firm MW as CLR, reinforcing strong interest in flexible pathways to utilize capacity ahead of full firm availability
Source: Feb 26, 2026 ERCOT Large Load Interconnection (LLI) Batch Study Process Stakeholder Survey results

## Slide 6: CLR and BYOG: Configurations
Commentary
Strong majority of respondents favor prioritizing Load + dispatchable thermal generation (71%), followed by Load + thermal + storage hybrid (52%) and other hybrid configurations (40%)
Overall stakeholder alignment: “T(D)SPs,” “Large Load customers,” and “Generators” are aligned in prioritizing configurations that include dispatchable thermal resources
Other suggestions:
  Preference for a technology-agnostic, non-discriminatory framework focused on reliability attributes rather than fuel type
  Support for broader hybrid “energy campus” models, incl. combinations of renewables + storage + thermal, nuclear + storage, geothermal, and fast-deploying resources
  Strong emphasis on integrated energy storage to enhance operational flexibility, manage ramping, and reduce grid withdrawals
  Consideration of non-co-located resource arrangements and simplified CLR structures
Chart: 
 | 16.129 | 6.4516 | 8.0645 | 6.4516 | 12.9032 | 8.0645 | 4.8387 | 9.6774
 | 1.6129 | 0 | 1.6129 | 0 | 0 | 1.6129 | 1.6129 | 6.4516
 | 38.7097 | 14.5161 | 20.9677 | 16.129 | 29.0323 | 16.129 | 8.0645 | 20.9677
 | 14.5161 | 1.6129 | 3.2258 | 1.6129 | 9.6774 | 6.4516 | 0 | 3.2258
Load + renewable generation
Load + storage
Load + renewable + storage hybrid
Load + thermal + storage hybrid
Generation capacity is greater than the load
Load is greater than the generation capacity
Other
71%
23%
34%
24%
52%
32%
15%
40%
2%
3%
2%
2%
2%
3%
15%
39%
2%
16%
15%
6%
21%
2%
8%
16%
6%
10%
Load + dispatchable thermal generation
13%
6%
16%
8%
29%
5%
21%
6%
10%
8%
T(D)SPs
LL Customers
Other
Generators
F1
“Which co-location configurations (e.g., load plus battery, load plus solar) should ERCOT prioritize when defining BYOG rules?” (% of overall respondents that selected a specific option)
Source: Feb 26, 2026 ERCOT Large Load Interconnection (LLI) Batch Study Process Stakeholder Survey results
N=62 (11 T(D)SPs, 35 LLC, 5 Other, 11 Generators). Note: respondents could multi-select responses so total % > 100

## Slide 7: CLR and BYOG: BYOG Self-Limiting Facility
Commentary
Strong majority of respondents (80%) agree that the BYOG self-limiting facility concept is adequate, while a minority (20%) do not
Overall stakeholder alignment: “T(D)SPs,” “Large Load customers,” “Generators,” and “Other” stakeholders each show majority support for the self-limiting facility concept
Reasons of opposition:
  Operational and reliability concerns, including need for real-time controls, enforceability, and clear compliance mechanisms
  Preference for dynamic (rather than fixed) injection/withdrawal limits, potentially reflecting seasonal or system conditions
  Need for greater flexibility, including ramping as transmission is built or site-specific agreements among ERCOT, TSP, and the customer
  Concerns that SLF may be impractical or misaligned with certain configurations (e.g., fully dispatchable co-located generation, G-1 events, maintenance scenarios)
  Requests for clearer BYOG/SLF definitions and implementation details before full endorsement
Chart: 
 | 11.8644 | 6.7797
 | 3.3898 | 3.3898
 | 47.4576 | 5.0847
 | 16.9492 | 5.0847
Yes
No
80%
20%
3%
17%
47%
3%
12%
5%
5%
7%
T(D)SPs
LL Customers
Other
Generators
N=59 (13 T(D)SPs, 31 LLC, 4 Other, 11 Generators)
F2
“For BYOG, is the self-limiting facility concept adequate? In other words, BYOG site agrees to fixed injections/withdrawal limitation until transmission is built?” (% of overall respondents)
Source: Feb 26, 2026 ERCOT Large Load Interconnection (LLI) Batch Study Process Stakeholder Survey results

## Slide 8: CLR and BYOG: CLR as a bridge solution
Commentary
Strong majority of respondents (79%) would consider using CLR status to consume power above their firm allocation while upgrades are being built, while a smaller share (21%) would not
Overall stakeholder alignment: “T(D)SPs,” “Large Load customers,” “Generators,” and “Other” stakeholders each show majority support for using CLR status as a transitional mechanism
Additional comments:
  Need for clearer definition and consistent understanding of what constitutes CLR participation and its reliability expectations
  Some stakeholders prefer BYOG or alternative mechanisms over CLR, particularly where operational dispatchability is constrained
  Concerns about real-time dispatch feasibility, monitoring requirements, and cost implications for certain large loads
  Broad interest in using CLR (or expanded definitions that include BYOG) to maximize early energization, provided it does not delay the batch process
Chart: 
 | 15.7895 | 3.5088
 | 5.2632 | 1.7544
 | 47.3684 | 14.0351
 | 10.5263 | 1.7544
Yes
No
79%
21%
2%
2%
4%
11%
47%
5%
16%
14%
T(D)SPs
LL Customers
Other
Generators
N=57 (7 T(D)SPs, 35 LLC, 4 Other, 11 Generators)
F3
“If Batch Zero provides less firm capacity than your requested ramp, would you consider using CLR status to consume power above your firm allocation while upgrades are being built?” (% of overall respondents)
Source: Feb 26, 2026 ERCOT Large Load Interconnection (LLI) Batch Study Process Stakeholder Survey results

## Slide 9: CLR and BYOG: CLR concept expansion
Commentary
Strong majority of respondents (74%) support expanding the Controllable Load Resource (CLR) concept to be explicitly included as a co-location configuration option under BYOG rules, while 26% do not
Overall stakeholder alignment: “T(D)SPs,” “Large Load customers,” “Generators,” and “Other” stakeholders each show majority support for explicitly incorporating CLR into BYOG
Additional comments:
  Broad support for CLR inclusion, but strong caution against adding complexity or delaying BYOG implementation
  Preference by several stakeholders to treat CLR and BYOG separately, at least initially
  Recognition that CLR could provide valuable operational flexibility, particularly for storage-integrated or “powered campus” configurations
  Concerns about market design, metering, and implementation readiness
  Emphasis that participation in CLR should remain optional and flexible, not mandatory for BYOG configurations
Chart: 
 | 14.0351 | 5.2632
 | 3.5088 | 1.7544
 | 45.614 | 12.2807
 | 10.5263 | 7.0175
Yes
No
74%
26%
2%
11%
46%
4%
14%
7%
12%
5%
T(D)SPs
LL Customers
Other
Generators
N=57 (10 T(D)SPs, 33 LLC, 3 Other, 11 Generators)
F4
“When defining BYOG rules, should Controllable Load Resources (CLRs) concept be expanded to be explicitly included as a co-location configuration option?” (% of overall respondents)
Source: Feb 26, 2026 ERCOT Large Load Interconnection (LLI) Batch Study Process Stakeholder Survey results

## Slide 10: CLR and BYOG: Pre-registration of non-firm MW as CLR
Commentary
Strong majority of respondents (82%) support allowing Large Load customers in Batch Zero to pre-register non-firm allocated MWs as a CLR after study results are released, while 18% do not
Overall stakeholder alignment: “T(D)SPs,” “Large Load customers,” “Generators,” and “Other” stakeholders each show strong majority support for providing this pre-registration option
Additional comments:
  Support for pre-registration as a flexible, optional bridge mechanism, but not as a condition tied to Batch Zero approval
  Operational and reliability concerns, including dispatch authority, emergency procedures, and system risk management
  Need for clear definitions and implementation details, incl. timing of registration/revocation risk
  Preference to keep CLR participation voluntary/ separate from traditional interconnection rights
  Strong interest from large loads in using CLR to energize non-firm MW early, often paired with private mitigation or on-site resources
Chart: 
 | 15 | 3.3333
 | 5 | 1.6667
 | 50 | 6.6667
 | 11.6667 | 6.6667
Yes
No
82%
18%
2%
3%
12%
50%
5%
15%
7%
7%
T(D)SPs
LL customers
Other
Generators
N=60 (11 T(D)SPs, 34 LLC, 4 Other, 11 Generators)
F5
“Should Large Load customers included in Batch Zero have the option to pre-register non-firm allocated MWs as a CLR after study results are released, to operate those MWs as controllable load until full firm capacity is available?” (% of overall respondents)
Source: Feb 26, 2026 ERCOT Large Load Interconnection (LLI) Batch Study Process Stakeholder Survey results

## Slide 11: Four different constructs were identified by ERCOT to integrate CLR and BYOG concepts into Batch Zero
Construct
Description
Feasibility
1A
Load-Only CLR (No Generation/No Batteries Behind the POI)
Large Load registers entirely as a CLR at the POI. No generation or storage is electrically connected in a way that can synchronize with, parallel, or export to the ERCOT grid
Potentially feasible
1B
CLR with Non-Synchronous Backup Generation
Large Load registers as a CLR and utilizes behind-the-meter backup generation that is not synchronized with the ERCOT grid
Potentially feasible
2
BYOG Self-Limiting Facility (SLF)
Colocated Large Load and Generation operate behind a single POI under a defined net injection/withdrawal limit enforced at the POI
Potentially feasible
3
Netted Network
Colocated Large Load and Generation operate behind a single POI (physically similar to SLF), but are permitted to participate simultaneously on both the supply and demand sides of the ERCOT market, subject to the POI interconnection limit
Not feasible

## Slide 12: Load-Only CLR (No Generation or Batteries)
Source: ERCOT discussions
Point of interconnection
Large Load registers entirely as a CLR, with no associated generation or storage behind the POI
Load-Only CLR leverages the existing CLR framework as the simplest near-term option1, subject to required market/system implementation items (e.g., SCED/mitigation enhancements) before energization
Participates as dispatchable demand and must follow SCED basepoints within its registered operating range (PC/LPC/MPC)
No assurance of service above awarded firm MW; real-time consumption may be reduced below PC based on system conditions and SCED mitigation
ERCOT observes and verifies performance based on net MW at the POI and adherence to SCED dispatch instructions
Must meet existing CLR telemetry and dispatch performance requirements (subject to SCED instructions and registered operating limits)
Load may register operational capability above awarded firm MW, subject to real-time dispatch and congestion mitigation2
Illustrative example
  150 MW requested in Year 1
  ERCOT performs steady-state and stability studies and allocate phased MW (e.g., 100 MW in Years 1–4 until transmission upgrade in Year 5)
  Operational parameters:
    PC = 0–100 MW (firm)
    LPC = 0–100 MW
    MPC = 150 MW (upper operational capability; not a planning guarantee)
    CLR quantity may be modified in later years as transmission capability increases
1. NPRR1188 later in 2026: Nodal pricing align local congestion prices. NPRR1255 mitigation methods needed (small project) | 2. Potentially subject to additional limits identified in dynamic studies
Description
Details
Load
Illustrative scheme
Chart: 
 | 100 | 100 | 100 | 100 | 1000
 | 50 | 200 | 400 | 600
50
Year 1
Year 2
Year 3
Year 4
Year 5
150
300
500
700
CLR Load
Firm Load
POTENTIALLY FEASIBLE CONFIGURATION
1A
ERCOT grid

## Slide 13: CLR with Non-Synchronous Backup Generation
Source: ERCOT discussions
Point of interconnection
Large Load registers as a CLR and utilizes behind-the-meter backup generation that is not synchronized1 with the ERCOT grid
This construct allows internal self-supply during curtailment without parallel operation or export to the ERCOT system
To qualify under this construct, backup generation must not be synchronized with or operate in parallel with the ERCOT grid and must be incapable of exporting power at the POI
ERCOT models the facility as load only at the POI for steady-state and stability studies and observes only net load at the POI
Transmission study limits remain binding on the net load at POI
Load must follow SCED basepoints within its LPC–MPC range
Large Load may need to segment internal load into controllable tranches (e.g., 10 MW blocks) to comply with SCED
Any internal switching to backup generation is behind-the-fence and not visible to ERCOT
If backup generation fails, the load remains responsible for meeting SCED dispatch instructions
No export or generation market participation is permitted under this construct2
Description
Illustrative scheme
POTENTIALLY FEASIBLE CONFIGURATION
1B
1. Any behind-the-meter generator or storage that can operate in parallel with the ERCOT grid (i.e., can be synchronized/connected while the POI remains energized) must be registered as a GR/ESR and is not compatible with a Load-Only CLR construct | 2. No energy or ancillary service participation from the backup resource is permitted
Load
ERCOT grid
Backup Gen
Backup Gen
Details
Load
ERCOT grid
Backup Generation
Backup Generation
No AC path to ERCOT grid

## Slide 14: BYOG Self-Limiting Facility (SLF)
Source: ERCOT discussions
Point of interconnection
Colocated Large Load and Generation operate behind a single POI under a defined net injection/ withdrawal limit enforced at the POI
Facility is structured as a PUN with a Self-Limiting Feature (SLF) (consistent with NPRR1026 framework)
The SLF ensures that net real power at the POI never exceeds the approved interconnection limit, regardless of internal load or generation configuration
Load and Generation are both registered with ERCOT
Interconnection limit applies to net MW at the POI
Requires operational coordination agreement between Load and Generator
ERCOT models the facility as a net resource at the POI, subject to the self-limiting cap
Facility must ensure net injection/withdrawal does not exceed POI cap at any time (may require breaker logic and/or reverse power relay to enforce the limit)
Transmission planning does not assume simultaneous full load and full generation at the POI:
  Either supply-side (GR/ESR) or demand-side (CLR) may participate at a given time
  Simultaneous full participation on both sides is not permitted unless structured as a Netted Network (separate construct)
The largest modeled contingency depends on internal configuration (e.g., if generators share a common step-up transformer, transformer loss may be most limiting event; if generators are electrically independent, individual G-1 may apply)
Description
Illustrative scheme
Load = 1,000 MW
Gen = 5 x 250 MW
G-1 compliant (serve 1,000 MW load) or most limiting contingency
POTENTIALLY FEASIBLE CONFIGURATION
2
Load
ERCOT grid
Gen 1
Gen 2
Gen 3
Gen 4
Gen 5
Load = 1,000 MW
Gen = 2 x 500 MW
G-1 compliant (only serve 500 MW load)
Load
ERCOT grid
Gen 1
Gen 2
Details

## Slide 15: Netted Network
Source: ERCOT discussions
Point of interconnection
Colocated Large Load and Generation operate behind a single POI (physically similar to SLF), but are permitted to participate simultaneously on both the supply and demand sides of the ERCOT market, subject to the POI interconnection limit
Same physical configuration as SLF (Load and GR/ESR behind one POI)
Net injection/withdrawal at the POI remains capped by the interconnection agreement
Unlike SLF:
  Supply and demand may participate simultaneously in Energy and AS1 markets
  Enables concurrent market activity from load and generation behind the same POI
Description
UNFEASIBLE CONFIGURATION
3
Illustrative scheme
Load = 1,000 MW
Gen = 5 x 250 MW
G-1 compliant (serve 1,000 MW load) or most limiting contingency
Load
ERCOT grid
Gen 1
Gen 2
Gen 3
Gen 4
Gen 5
Load = 1,000 MW
Gen = 2 x 500 MW
G-1 compliant (only serve 500 MW load)
Load
ERCOT grid
Gen 1
Gen 2
1. Ancillary services
Details

## Slide 16: Next Steps
Target RRs for March 4 filings completed for Batch Zero: ERCOT filed the Batch Zero PGRR145 and related NPRR1325 on March 4, initiating the formal governance process and aligning with the May PRS/ROS/TAC sequence and June 1 Board target reflected in the critical path timeline
  Comments encouraged by noon next Friday, March 20 to discuss at March 24 workshop
Additional filings on target (CLR and BYOG): ERCOT is advancing targeted revision requests to clarify CLR and BYOG treatment and is currently targeting an April filing (TBD)
  Additional discussion at Workshops #5 and 6
  Target Revisions Requests for Workshop #7 (April 9)
Questions?