## Slide 1
Large Load Interconnection Batch Study for Special ROS
April 23, 2026
Note Sections 4 & 5 will be updated prior to ROS (after ERCOT files comments)

## Slide 2: Agenda
Timeline and governance recap
Update on timeline and key workshop dates
Outline PRS/ROS/TAC pathways to June Board with key submission dates
1
7
BYOG discussion
Further discussion of BYOG approach
Advance discussion on BYOG framework for Batch Zero
CLR discussion
Review revision language for CLR filed on April 17
3
6
Market Comments filed
Review stakeholder comments received
Batch Zero Concepts
Detailed review of Batch Zero Concepts
5
Feedback from PUCT and ERCOT comments
Review feedback received from PUCT on April 17 Open Meeting
Review updated ERCOT comments to PGRR145 filed on April 22
4
2
Year 6 allocation approach
Review alternative approach for dealing with year 6 allocation and discuss advantages and disadvantages

## Slide 3: Agenda
Timeline and governance recap
Year 6 allocation approach
CLR Discussion
Feedback from PUCT and ERCOT comments (chapter to be filled out after ERCOT comments are filed)
Batch Zero Concepts (chapter to be filled out after ERCOT comments are filed)
Stakeholder Feedback
BYOG Discussion
3

## Slide 4: Batch Zero Revision Request Timeline
Forums
ROS (Reliability and Operations Subcommittee)
2026
Q1
Q2
Q3
Feb
Mar
Apr
May
Jun
Jul
Workshop #2 Feb 12
Workshop #4 Mar 10
Workshop #5 Mar 24
Workshop #6 Mar 30
PRS Update 3/11
ROS Vote 5/7
Board Vote 6/1
3/4 ERCOT files Batch Zero Revision Request(s)
7/10 Target effective date of protocols
Consideration of Batch Zero NPRR 1325 and PGRR 145
LLWG Feb 19
Workshop #3 Feb 26
TAC Vote 5/19-20
Target Board approval date
Board Meeting 4/20
ROS Update 4/2
Monthly TAC updates
Workshop #7 Apr 9
Special PRS 4/22
Regular TAC 4/29
Special TAC 5/13
PRS Vote 5/6
Monthly LLWG updates
4/17 ERCOT filed comments to PGRR145 and NPRR1325 for CLR, followed by BYOG (TBD)
ROS Update (special) 4/14
ROS Update 3/5
ROS Update (special) 4/23
PRS (Protocols Review Subcommittee)
Workshops and working groups
TAC
ERCOT Board
Objective
Align stakeholders on direction/scope following Commission decision
Define the scope, boundaries, and intended role of Batch Zero
File NPRR 1325 for Workshops and PRS review
Endorse NPRR 1325 for advancement to TAC
File PGRR 145 for Workshops and ROS review
Endorse PGRR 145 for advancement to TAC
Review/endorse combined NPRR/PGRR package for Board approval
Close outstanding design and drafting issues, incorporate vetted stakeholder feedback, and finalize Revision Request language for committee approval
Preview structure/governing concepts of Batch Zero PGRR before filing
Note that TAC leadership is involved in considering options to ensure successful review and approval
Source: ERCOT discussions
Regular PRS 4/15

## Slide 5: Revision Request Process Flow
Comments may be filed between each step of the process
Comments for NPRR1325 may be submitted using the Comments Form found here
Comments for PGRR145 may be submitted using the Comments Form found here.
Submit to RevisionRequest@ercot.com
NPRR Comments
PGRR Comments
Large Load Interconnection Workshops
NPRR/PGRR
Review
BOARD
PUCT
TAC
ROS
PGRR Language/IA Review
PRS
NPRR Language/IA Review

## Slide 6: Related PUCT Activities
PUC Project 58480, 16 TAC § 25.370, Large Load Forecasting Rule (Adopted & Effective March 1, 2026)
  After 2026, only Large Loads that have executed an interconnection agreement that satisfies the requirements in PUC Project 58481 will be included in the Large Load forecast. These requirements will be reflected in future revision requests.
  Establishes alternative gating criteria for Large Loads to be included in the 2026 Large Load Forecast, which is used in planning assessments until new cases are constructed in 2027 using new rule criteria.
Source: PUCT Project No. 58480 (final rule) and Project No. 58481 – Proposal for Publication of 16 TAC §25.194 (filed March 12, 2026)
PUC Project 58481, proposed to be 16 TAC § 25.194, Large Load Interconnection Standards (Proposal for Publication published on March 12, 2026)
  Intermediate Agreement Requirements:
    Site control (updated)
    Financial Security ($50,000/MW in current PFP; subject to final rule)
    Disclosures
    Option to pay for significant equipment or services
  Interconnection Agreement Requirements:
    Site control (updated)
    Financial security
    Interconnection fee ($50,000/MW, non-refundable)
    CIAC
    Reallocation
    Withdrawal Consequences
    Refund Eligibility and Timing
  After the PUCT adopts a final rule, ERCOT will file a revision request to align Section 9.7 with the requirements in the final rule.

## Slide 7: Reminder of Scope and Priorities for Workshops
March 4 filings completed for Batch Zero: ERCOT filed the Batch Zero PGRR145 and related NPRR1325 on March 4, initiating the formal governance process and aligning with the May PRS/ROS/TAC sequence and June 1 Board target reflected in the critical path timeline
  March 17 ERCOT comments filed
  April 4 ERCOT comments filed: incorporated stakeholder feedback (received by March 20), including targeted clarifications and refinements
  April 22 ERCOT comments filed: updated proposal to reflect guidance received from the PUCT April 17 Open Meeting, including adjustments to eligibility framework, study treatment, and overall Batch Zero design
ERCOT progressing CLR and BYOG design through parallel comment tracks: Batch Zero comments may include or exclude CLR/BYOG elements, with ERCOT Market Rules managing versioning
  CLR status: April 17 comments filed, formally introducing and detailing PCLR framework (e.g., modular construct, operational treatment, linkage to future market implementation)
  BYOG Status: Concepts in progress, targeting filing comments for end of April
Long-term Batch Process revisions: out of scope for the current filing but soon after June 1. ERCOT will incorporate lessons learned from Batch Zero to inform future revision requests and the design of a durable, repeatable batch study process

## Slide 8: Agenda
Timeline and governance recap
Year 6 allocation approach
CLR Discussion
Feedback from PUCT and ERCOT comments (chapter to be filled out after ERCOT comments are filed)
Batch Zero Concepts (chapter to be filled out after ERCOT comments are filed)
Stakeholder Feedback
BYOG Discussion

## Slide 9: Year 6 allocation design choice: recap
Year 6 allocation remains a key design challenge for Batch Zero: process must balance early visibility for developers with alignment to actual transmission readiness, avoiding both over-commitment and lack of certainty
Two main approaches have been considered to date, each with clear trade-offs
  Current PGRR145 approach: allocates full MWs by Year 6 upfront, providing clarity but risking a step-change not supported by transmission development timelines
  “Rollover” approach: defers full MW allocation to a subsequent batch, ensuring realism but creating customer uncertainty and requiring commitment without clear visibility on full delivery
A third approach (“bookend” allocation) emerges as a more balanced solution:
  Description: focus the study on key years (2, 4, 6) to enable a 6-month Batch Zero while providing a full Year 1–6 capacity trajectory and anchoring Year 6 allocation to identified transmission solutions
  Enabler: early TSP involvement to define transmission solutions in parallel with the study
  Advantages: combines customer certainty (clear ramp) with transmission realism, enables an actionable 6-year plan within timeline, and reduces complexity and rework

## Slide 10: Existing approaches to Year 6 allocation present clear trade-offs between certainty and realism
PGRR145 Approach
“Rollover” approach to subsequent batch
Example: 1,000 MW data center requiring full capacity by Year 6
Years 1-5
Request studied in Batch Zero: initial MWs allocated based on system capability; transmission constraints and required upgrades identified
Request studied in Batch Zero: initial MWs allocated based on system capability; transmission constraints and required upgrades identified
Considerations
Provides certainty by guaranteeing full MWs by Year 6
Creates a potential step-change in MWs between Years 5 and 6, with limited time to develop required transmission
Full MW allocation is aligned with identified transmission upgrades
Requires financial commitment for partial MWs without clear visibility on timing or certainty of full MW delivery
Year 6
Full MW automatically allocated based on Batch Zero results; transmission solutions further defined in the 2027 RTP
Full MW not committed in Batch Zero; additional MWs studied and allocated through a subsequent Batch 1 process
Chart: 
 | 100 | 100 | 450 | 600 | 600 | 1000
Year 1
Year 2
Year 3
Year 4
Year 5
Year 6
Illustrative ramp schedule, MW
Chart: 
 | 100 | 100 | 450 | 600 | 600 | 600
 | 400
Year 1
Year 2
Year 3
Year 4
Year 5
TBD
Year 6
Automatically set at requested peak Demand
TBD: additional MWs studied in next batch and allocated based on available capacity

## Slide 11: “Bookend” allocation approach: resolving trade-off between early certainty and transmission alignment
Example: 1,000 MW data center requiring full capacity by Year 6
Chart: 
 | 100 | 300 | 300 | 500 | 500 | 1000
Year 1
Year 2
Year 3
Year 4
Year 5
Year 6
Illustrative ramp schedule and allocation methodology by year, MW
Key highlights
Not studied: based on existing system capacity (no upgrades)
Fully studied (all cases)
Not studied: conservative assumption equal to Year 2
Fully studied (all cases)
Not studied: conservative assumption equal to Year 4
Fully studied (all cases)
Studied
Not studied
Approach shifts from a fully prescriptive multi-year study to a targeted “bookend” approach to balance feasibility and value while reducing computational burden
Objectives:
  Preserve decision-quality outputs while making the study executable within a 6-month Batch Zero timeline
  Balance customer visibility with transmission realism
Process flow:
  Batch study produces Year 1–6 allocation trajectory and required transmission upgrades
  Customers use outputs to assess viability and commit
  Refinement removes non-committed load and refines projects and costs
  Output is a coherent, actionable transmission plan
Enablers
Early TSP involvement at study kickoff, with a shared Year 6 system case
Parallel development of transmission solutions and cost estimates
Centralized ERCOT coordination, consolidating TSP inputs into a single plan
Advantages
Delivers an actionable 6-year transmission plan within Batch Zero timeline, avoiding reliance on future cycles
Provides full Year 1–6 visibility for customer decisions
Reduces complexity and rework

## Slide 12: Agenda
Timeline and governance recap
Year 6 allocation approach
CLR Discussion
Feedback from PUCT and ERCOT comments (chapter to be filled out after ERCOT comments are filed)
Batch Zero Concepts (chapter to be filled out after ERCOT comments are filed)
Stakeholder Feedback
BYOG Discussion

## Slide 13: Overview of Provisional Controllable Load Resource (PCLR)
  Large Load participates as a Provisional Controllable Load Resource (PCLR), where a portion of load is firm (LPC) and the remaining load is flexible and subject to dispatch
  The PCLR framework enables Load to consume more energy in unconstrained hours of the day ahead of full transmission build-out, with firm MW defined in the Batch Zero study and non-firm MW managed through SCED
Description
Details
  Split between firm and flexible load defined through the Load Commissioning Plan (LCP) (LPC = firm MW; remaining load operates as PCLR)
  PCLR participates as dispatchable demand and must follow SCED basepoints within its operating range
  Full requested load is studied in Batch Zero, with transmission upgrades identified to transition PCLR to firm service over time
Provisional Controllable Load Resource (PCLR)
Point of interconnection
Load
Illustrative scheme

## Slide 14: Provisional CLRs – Definition1
New Resource Type: ‘Provisional CLR’
A Large Load electing to operate as a CLR post-Batch Zero, with LPC defined in study and commitment via Form
What’s different?
PCLR load bids can be ‘capped’ to mitigate transmission constraints identified in SCED
PCLR bids are capped dynamically (“last-in-line/just-in-time”) in each run of SCED to a price that will just allow SCED to resolve a constraint
PCLRs are not eligible to provide Ancillary Services
Submits CLR Energy Bid Curve  bid-to-buy prices between Low Power Consumption (LPC) and Maximum Power Consumption (MPC) – same as any other CLR
1. Design and NPRR/PGRR language still under internal review and may change prior to filing
Reference: Batch Zero PGRR145 (April 22, 2026), Sections 9.2.2.1, 9.3.2.1, 9.4.1, 9.5.3, and 9.6.1 (Provisional Controllable Load Resource design, study treatment, and operations)

## Slide 15: Provisional CLRs – Structure of Revision Requests1
Will consist of a comments to existing PGRR145 and companion NPRR1325
Modular structure adds to PGRR145 and NPRR1325
  Example – Section 9.2.2.1, Additional Information Required for Provisional Controllable Load Resources (PCLRs) compliments Section 9.2.2 as written in PGRR145
This structure will allow the PCLR concepts to move forward in parallel with PGRR145 and NPRR1325 if possible, without interfering with the core Batch Zero language
Language related to PCLR approval to energize and PCLR bid capping in SCED is intended to remain grey-boxed until implementation of NPRR1188 and until system changes for the bid capping are in place
1. Design and NPRR/PGRR language still under internal review and may change prior to filing

## Slide 16: PCLR Language – Foundational Concepts1
Allocation in Batch Zero
Registration Requirements
Ensure Real-Time Dispatch
Load is assessed through the Batch Zero process in the same manner as load requesting firm service for steady state and at full consumption for stability
The level of firm load that can be reliably served becomes the maximum Low Power Consumption (LPC) value for the PCLR in real-time (instead of a hard limit)
The remaining requested load amount is approved contingent on qualification as a PCLR
Intention to register as a PCLR must be declared prior to the start of Batch Zero
Once allocated in Batch Zero, the load must register and qualify as PCLR before it may consume above initial limits
Load must remain registered as a PCLR until an exit date identified in Batch Zero
Obligation to remain a PCLR transfers to subsequent owners of the Large Load
Like traditional CLRs, PCLRs must follow SCED basepoints when consuming energy2
Dynamic bid capping logic is added to ensure the PCLR will be dispatched rather than allowing the constraint to violate
1. Design and NPRR/PGRR language still under internal review and may change prior to filing | 2. On implementation of NPRR1188

## Slide 17: Provisional Controllable Load Resources (PCLRs) in Batch Zero1
ERCOT validates completion of all steps prior to granting Approval to Energize
8
QSE establishes required ICCP telemetry points
7
RE coordinates with ERCOT to establish metering and submit CLR parameters via RIOO
6
ILLE registers with ERCOT as a Resource Entity (RE) and designates a QSE
5
ERCOT studies the full load amount in the Batch Zero Refinement Study
4
ILLE submits updated Declaration to accept allocation amounts2
3
ERCOT studies PCLR in Batch Zero
2
Submission of Declaration and required information to ERCOT
(by July 24)
1
Must be done before non-firm load may energize
May be done in parallel with QSA
1. Design and NPRR/PGRR language still under internal review and may change prior to filing
2. Failure to submit Form W removes project from the refinement story
Detailed next

## Slide 18: Post–Batch Zero, ILLE must elect path via Form W to retain position and proceed
Context
After Batch Zero results, each ILLE receives allocated LPC (firm) and MPC (total) values
To proceed, ILLE must submit Form W Part B election by deadline
Failure to elect leads to project being removed from Refinement study and loses queue position
Description
Option
Accept ERCOT-defined LPC and MPC values without modification
Maintains ability to consume above LPC, subject to PCLR qualification, dispatch, and bid capping
Accept PCLR as is
1
Elect to proceed as PCLR but reduce LPC and/or MPC below awarded levels
Provides flexibility while aligning with project readiness or infrastructure constraints
Accept PCLR with reduced values
2
Withdraw from PCLR and accept LPC values as firm load (with optional reduction), eliminating ability to exceed LPC
Withdraw PCLR, retain firm load
3
Withdraw from process
Decline participation and exit Batch Zero entirely
Project is removed from Refinement Study and must re-enter through a future process
4
Form W Part B election is binding and determines eligibility for Refinement Study and eventual energization. Failure to submit Form W Part B results in removal from Batch Zero

## Slide 19: Provision CLR (PCLR) – Dynamic Bid Capping Process
PUBLIC
1
SCED₋₁ (Previous Run)
After each SCED run, generate a fresh list of transmission constraints whose Shadow Price ≥ 90% of Max Shadow Price:
Constraint₁₂₃
Constraint₂₃₄
Constraint₃₄₅
Constraint₄₅₆
⚡ Shadow price threshold triggered
Match
2
SCEDcurrent (Before Step 2)
Compare the matching list against all active constraints in the current SCED run:
Constraint₂₃₄
Constraint₄₅₆
Constraint₆₇₈
Constraint₇₈₉
✔ 2 constraints match — evaluate PCLRs
Cap
3
SCED Step 2 (Bid Capped)
−0.02
Shift Factor Rule
Only PCLRs with a Shift Factor ≤ −0.02 on a matching constraint are eligible for bid capping
CAP
Bid Cap Applied
The PCLR's Energy Bid Curve is capped at the Adjusted Bid Cap (ABC) value before Step 2 executes
✓
Adjusted Bid Cap Formula:
ABC = Step 1 System Lambda − max ( MaxShadowPrice × ShiftFactor ) − $0.01 / MWh
Only applied where PCLR Shift Factor ≤ −0.02 | Constraint must appear in prior-run trigger list | No standard market mitigation applies to Energy Bid Curves

## Slide 20: CLR and BYOG frameworks are being integrated into Batch Zero filing, forming a first comprehensive design with further refinement over time
PCLR comments
PCLR comments
PCLR comments
BYOG comments
PCLR comments
BYOG comments
March 4: ERCOT files PGRR145 and NPRR1325
March 17 and April 4: targeted ERCOT comments to incorporate stakeholder feedback
Establishes foundational framework for Batch Zero execution and LLI processing
April 17: PCLR introduced as modular enhancement via comments to PGRR145/ NPRR1325
Enables early shaping of controllable load pathway without delaying core filing
April (TBD): BYOG introduced as modular enhancement via comments to PGRR145 / NPRR1325
Enables integration of generation-backed load pathway without delaying core filing
Path of PGRR145 and NPRR1325 towards governance approval
Key takeaways
Modular approach enables speed without locking design: core framework advanced while PCLR and BYOG are developed in parallel
Convergence toward June Board: PGRR145/NPRR1325, PCLR, and BYOG converge into a complete, minimum viable package for decision-making
Minimum viable, not final design: PCLR and BYOG are introduced as initial concepts, with further refinement expected post June Board
Source: ERCOT discussion
1
2
3
Core Batch Zero framework established
PCLR framework integration
BYOG framework integration
Detailed next
PGRR145
PGRR145
PGRR145
NPRR1325
NPRR1325
NPRR1325

## Slide 21: PCLR introduces a controllable-load pathway within Batch Zero, enabling staged interconnection while preserving full transmission planning
PGRR145 reference section
Section 9.2 – Applicability, Eligibility, and Submission Requirements
Section 9.3 – Batch Zero Interconnection Study Methodology
Section 9.4 – Batch Zero Results and Commitment Requirements
Section 9.5 – Refinement Study and Transmission Planning
Section 9.6 – Energization and Operational Requirements
How PCLRs impact/integrate PGRR145 sections
Expand applicability to include PCLR as a distinct pathway, alongside Base Load and Studied Load
Introduce enhanced data and modeling requirements for controllable loads
Define LPC (firm, reliable level) and MPC (conditional full demand), enabling flexible load ranges
Decouple planning vs. reliability modeling: plan system for full requested load (MPC), assess reliability at LPC (constrained level)
Establish LPC as the maximum reliably serviceable load in each study year
Enable two-tier outcomes: firm allocation at LPC, and conditional approval of additional demand (MPC)
Introduce dual commitment structure: interconnection Agreement (infrastructure) and PCLR operational commitment (Form W)
Require formal election of PCLR pathway, including ability to accept, modify, or decline LPC/MPC structure
Link study results to binding operational limits and qualification requirements
Plan transmission for full requested demand (MPC) to avoid underbuilding
Decouple long-term system design from near-term operations
Maintain LPC as the planning input for committed PCLRs in refinement
Enable staged energization, with initial operation limited to LPC
Require PCLR qualification (registration, telemetry, testing) before exceeding LPC
Enforce dispatchability and ERCOT control, with operations capped until full approval
Source: 145PGRR-45 ERCOT Comments 041726

## Slide 22: PCLR enables dispatchable, price-responsive load by integrating large load into ERCOT market operations and SCED
Source: 1325NPRR-05 ERCOT Comments 041726
NPRR1325 reference section
Section 2 – Definitions, acronyms and abbreviations
How PCLRs impact and integrate NPRR1325 sections
Introduce PCLR as a new controllable load construct, extending CLR into large-load interconnection
Define LPC (firm level) and MPC (conditional level) and associated operational constraints
Establish standardized terminology linking planning, dispatch, and compliance
Section 3.2.5 – Publication of resource and load information
Represent demand as price-responsive curves (LPC to MPC) instead of static load
Publish aggregate demand curves from Energy Bid Curves reflecting flexible consumption
Provide visibility into real-time demand response capability in SCED
Section 4.4.9.4 and 4.4.9.4.4 – Mitigation and Adjusted Bid Caps (ABC)
Extend mitigation framework to include dispatchable load alongside generation and ESRs
Introduce constraint-driven bid capping (ABC) for PCLRs: triggered by binding constraints (≥90% shadow price) and applied based on PCLR shift factor contribution to congestion
Align demand-side participation with efficient and consistent price formation
Section 6.5.7.11 – PCLR ramp rate requirements
Define minimum controllability requirements (10–20%/min ramp rates)
Establish performance monitoring and compliance thresholds
Enable ERCOT to enforce dispatch responsiveness and reliability performance
Section 23 (Form W) – PCLR registration and commitment
Establish formal PCLR registration mechanism (Part A election, Part B commitment)
Bind LPC/MPC outcomes from planning to operational obligations
Require continuous qualification, dispatch compliance, and telemetry
Define exit conditions, de-registration, and enforcement mechanisms
Section 6.5.7.3 – Security Constrained Economic Dispatch (SCED)
Integrate PCLRs into SCED as dispatchable, price-responsive resources
Implement two-step SCED process: Step 1 (reference prices without constraints) and Step 2: constrained dispatch with PCLR bid capping (ABC)
Use Energy Bid Curves (vs. fixed load) to represent flexible demand
Enable real-time congestion management via demand response while maintaining reliability
New section introduced

## Slide 23: Provisional CLRs – Declaration of Intent and Batch Treatment

## Slide 24: Commitment process (1/3)

## Slide 25: Commitment process (2/3)

## Slide 26: Commitment process (3/3)

## Slide 27: PCLR in Refinement Process

## Slide 28: PCLR Energization Requirements

## Slide 29: Agenda
Timeline and governance recap
Year 6 allocation approach
CLR Discussion
Feedback from PUCT and ERCOT comments (chapter to be filled out after ERCOT comments are filed)
Batch Zero Concepts (chapter to be filled out after ERCOT comments are filed)
Stakeholder Feedback
BYOG Discussion

## Slide 30: Agenda
Timeline and governance recap
Year 6 allocation approach
CLR Discussion
Feedback from PUCT and ERCOT comments (chapter to be filled out after ERCOT comments are filed)
Batch Zero Concepts (chapter to be filled out after ERCOT comments are filed)
Stakeholder Feedback
BYOG Discussion
30

## Slide 31: Agenda
Timeline and governance recap
Year 6 allocation approach
CLR Discussion
Feedback from PUCT and ERCOT comments (chapter to be filled out after ERCOT comments are filed)
Batch Zero Concepts (chapter to be filled out after ERCOT comments are filed)
Stakeholder Feedback
BYOG Discussion
31

## Slide 32: Comments Filed after April 9th, 2026
Source: ERCOT PGRR145 “Key Documents” section
Date
Company
April 17th
April 17th / April 21st
April 21st
April 21st
April 21st
April 21st
April 21st
1. Agentic, Reliant, Eolic, Enchanted Rock, and Cholla filed comments together on Apr 21
Author
Kevin Marquardt
Bill Barnes1
Paul Townsend / Michele Richmond
Samuel Brandin1
Shannon Caraway1
Monica Batra-Shrader1
Gideon Powell1

## Slide 33: Agenda
Timeline and governance recap
Year 6 allocation approach
CLR Discussion
Feedback from PUCT and ERCOT comments (chapter to be filled out after ERCOT comments are filed)
Batch Zero Concepts (chapter to be filled out after ERCOT comments are filed)
Stakeholder Feedback
BYOG Discussion

## Slide 34: A Bring Your Own Generation (BYOG) approach should help stakeholders to solve some of the issues raised with the LLI process
Interconnecting Large Load Entities (ILLEs) can co-develop or contract with co-located generation to:
Secure their own path to energization, independent of grid constraints
Align load ramp with generation availability
Reduce reliance on uncertain transmission upgrades
Intent of BYOG
Potential benefits
  For the ILLEs
  Greater certainty on energization timing and scale
  Ability to bypass grid-driven delays and curtailment risk
  For the generators
  Direct, contracted demand from day one
  Improved bankability vs. merchant exposure
  Clear role in solving interconnection bottlenecks
  For the system
  Accelerates capacity build where it is needed most
  Reduces congestion and transmission pressure
  Improves resource adequacy through demand-linked generation

## Slide 35: A coordinated load–generation study framework is required to enable a viable BYOG construct
Generation Interconnection (Normal GINR process – Planning Guide Section 5)
Large Load Interconnection (PGRR145 process – Planning Guide Section 9)
BYOG agreement
Detailed next
Monitoring and compliance
Establishing metering, telemetry, and real-time compliance mechanisms to ensure the facility continuously operates within its defined limits
Operations
Specifying the facility operating envelope (net import/export limits at POI) and dispatch/curtailment behavior for co-located load, generation, and storage
Study treatment
Defining an integrated study approach where load and generation are modeled as a single facility with consistent assumptions across planning and reliability analyses
Registration
Setting the registration model and load commitment requirements, aligning timing, scale, and obligations across generation and load interconnection processes

## Slide 36: Study treatment should separate generation, load allocation and transmission planning while capturing full facility impact
Generation interconnection study
Studies generation independently under standard GINR assumptions to determine interconnection requirements and export capability
Batch Study
Evaluates load as grid-supplied only (co-located generation not counted) to determine firm load allocation based on system capability
Transmission planning study
Models load and generation together as a single facility to assess full system impact under N-1 (single-contingency) conditions (e.g., generator or transmission outages) and drives upgrades based on worst-case conditions
New discussion topic

## Slide 37: Co-located load and generation are governed by three separate ERCOT evaluation processes
Illustrative scheme
ERCOT lens
Description
Output
Batch Study (Load Interconnection)
Evaluates large load interconnections to determine the maximum import (withdrawal) capability under steady state conditions from the ERCOT grid, independent of on-site generation
Withdrawal limits1 and initial load allocation (subject to stability limits from Gen+Load studies)
Source: ERCOT discussions
1. Import (withdrawal) limit applies to total site demand, including co-located load and any storage charging | 2. Where generation and load share a POI, ERCOT/TSP studies may evaluate both independent and combined configurations; combined cases are particularly relevant for stability and system modeling
Focus
1,000MW
~
~
600MW
600MW
ERCOT Grid
1,000MW
~
~
600MW
600MW
1,000MW
~
~
600MW
600MW
Generation Interconnection
Assesses generation to determine export capability and interconnection requirements; co-located load is included in the study when it materially affects system performance (e.g., stability, voltage, operations)2
Maximum export (injection) limits, stability constraints, and interconnection requirements
ERCOT Grid
ERCOT Grid
1,000MW
~
~
600MW
600MW
Transmission planning
Identifies system constraints and determines network upgrades required to reliably support the combined load and generation under normal planning assumptions (e.g., N-1/G-1)
Required transmission upgrades and validation of SLF-exit (full load) conditions for reliable operation in the long-term (post-BYOG) configuration
ERCOT Grid
Final allowable load is determined by withdrawal limits (Batch Study) and may be further constrained by stability limits (Gen+Load studies) Example: Batch study sets a withdrawal limit of 100 MW. Stability studies identify a maximum stable load of 500 MW. Final allowable load = 500 MW, with up to 100 MW from the grid and the remainder supplied by on-site generation. If no stability constraint is identified, load can reach the full 1,000 MW using on-site generation

## Slide 38: PUN with Self-Limited Withdrawal (BYOG) – Operational Model
Interim operation (pre-transmission): BYOG agreement in place
Post-transmission operation: BYOG agreement exited
ERCOT Grid
1,000MW
~
~
600MW
600MW
New 400 MW transmission line
Export (injection): determined by SCED based on available surplus generation and dispatched at the resource level via COP/telemetry
Import (withdrawal): determined through batch study as a maximum withdrawal from the ERCOT grid, independent of co-located generation; total load cannot exceed identified stability limits
Operations: facility operates as a PUN with self-limited withdrawal
  Load is primarily served by on-site generation and must reduce load to remain within the withdrawal limit if generation is unavailable, within defined operational response times (e.g., cycles to seconds)
  Injection is governed by standard generation interconnection limits and SCED dispatch
SLF agreement dissolved and normal operations
Transmission upgrades: determined through ERCOT transmission planning studies, which evaluate the combined load and generation under standard reliability criteria (e.g., N-1 / G-1) to identify required network upgrades
Import and export: governed by standard interconnection limits and system constraints (no BYOG-specific caps); fully dispatchable through SCED subject to study results
Operations: transitions to standard ERCOT operation
  Generation and load treated as independent resources
  No self-limiting withdrawal requirement
  Full participation in market dispatch and planning
Source: ERCOT discussions
ERCOT Grid
1,000MW
~
~
600MW
600MW
Import: max withdrawal limit (Batch study)
Export: available export (SCED dispatch)

## Slide 39: Sequential BYOG interconnection timeline across Batch, Generation, and Transmission planning processes
Source: ERCOT discussions
Batch Study
Generation study
Transmission Planning
LLIS (meeting PG 9.4 and 9.5)
Jan 2027
Mar 2027
Developer commitment period (60 days)
BYOG declaration executed to identify load–generation pairing for studies (pre- PG 6.9 milestone of generation)
July 2026
Case building
Batch Study allocation
~
~
Focus on load only
Upgrade identification
Focus on load and gen
Refinement study
Focus on load and gen
Gen FIS studies
Focus on gen only
Focus on load and gen
Gen + load FIS studies (includes load for stability/operability assessment)
PRELIMINARY

## Slide 40: Appendix

## Slide 41: Load energization is limited by withdrawal limits and further enabled by co-located generation
1,000MW
~
~
500MW
500MW
ERCOT Grid
Jan 1: Load built first, energization is allowed up to withdrawal limit
Jun 1: Load increases beyond the withdrawal limit as gen comes online
Dec 1: Full generation online, full load energization
Key takeaways
Load infrastructure is completed ahead of generation
Load is allowed to energize up to the withdrawal limit (e.g., 100 MW)
Load beyond the withdrawal limit requires on-site generation
First generation unit reaches COD
Load can increase above the withdrawal limit as generation becomes available (up to withdrawal + generation, subject to stability limits)
Total load is limited by available generation plus the withdrawal limit (and stability limits)
Second CT reaches COD, completing generation build-out
Load can now fully energize to planned capacity
Facility transitions to steady-state operation
Source: ERCOT discussions
Jan 1
Dec 1
Jun 1
≤100
Load energization is limited by the withdrawal limit; generation availability enables additional load beyond that level
Energization is staged, not binary: load ramps in line with generation commissioning
At all times (including contingencies), load ≤ (available generation + withdrawal limit), subject to stability limits
This sequencing must be explicitly defined in agreements and Planning Guide language
1,000MW
~
~
500MW
500MW
ERCOT Grid
Jan 1
Dec 1
Jun 1
≤600
1,000MW
~
~
500MW
500MW
ERCOT Grid
Jan 1
Dec 1
Jun 1
≤1100
xxx
xxx
Commercial Operation Date
Allowed load energization, MW
Online (available)
100MW withdrawal limit
100MW withdrawal limit
100MW withdrawal limit
ILLUSTRATIVE

## Slide 42: Clarifications on example configurations and their classification as PCLR and/or BYOG
ERCOT Grid
ERCOT Grid
Source: ERCOT discussions
Load and battery, always grid-synchronized
Load and unsynchronized on-site generation
Configuration
  Large load directly connected to ERCOT grid
  Co-located battery electrically synchronous with the grid (AC-coupled or DC behind inverter)
  No ability to island or disconnect from grid in real time
Description
  Load is fully dependent on grid supply at all times
  Battery has no ability to respond to dispatch instructions independently of grid availability
Classification: not a PCLR, might be a BYOG
Configuration
  Large load directly connected to ERCOT grid
  On-site generators not synchronized to grid
  Transfer scheme allows fast disconnection from grid and switching to on-site supply
Description
  Under normal conditions, load consumes from grid
  Under constraint / dispatch, Load can rapidly disconnect from grid and Switch to on-site generation (or curtail)
Classification: PCLR if meeting dispatch instructions (SCED basepoints) and ramping down/up within required timelines
ESR
~
~
~
Generator
Load
Point of interconnection
Switch
~
~
~

## Slide 43: Co-located generation enables net export while serving large load under defined operating limits
PUN / SLF
Interconnection model
At steady state (full gen + load)
  COP/ SCED sees 500MW of excess to dispatch
  Reactive support obligation is based on total installed generation capacity at the POI (e.g., full 1000 MW), not net export
  Seen as:
    LSL = 0
    HSL = 500
  at POI or resource
1000 MW – 500 MW = 500 MW
of excess generation
~
~
~
1000 MW CC Generation in model with telemetry
500 MW Large Load Interconnection