## Slide 1
Firm Fuel Supply Service (FFSS) Deployment Report
2025-2026 Obligation Period
Zhengguo Chu
Supervisor, Market Analysis
Technical Advisory Committee
April 29, 2026

## Slide 2: Background
This presentation is required by Protocol 3.14.5(13):
  “If FFSS is deployed, then ERCOT will provide a report to the TAC or its designated subcommittee within 45 days of the end of the FFSS obligation period. The report must include the Resources deployed and the reason for any deployments.”
Additional reporting is required by Protocol 3.14.5(15):
  “On an annual basis after the FFSS season, ERCOT will provide a report separately for the total amounts from Section 6.6.14.1, Firm Fuel Supply Service Fuel Replacement Costs Recovery, and Section 6.6.14.2, Firm Fuel Supply Service Hourly Standby Fee Payment and Fuel Replacement Cost Recovery, to the TAC or its designated subcommittee.”

## Slide 3: Cold Weather Event Timeline
During 2025/26 FFSS obligation period, one winter watch resulted in the deployment of FFSS from 1/24 10:00 to 1/27 12:00.
  There was one additional winter watch during this period that did not result in FFSS deployments (1/31-2/1)
Leading up to this cold weather event, ERCOT was informed of gas supply restrictions impacting generating resources
  This resulted in the decision to deploy FFSS resources
09:00 - Watch begins due to forecasted cold weather from 01/23 through 01/27
Public Notice posted
10:00 - FFSS deployed.
Public notification of FFSS deployment instructions.
12:00 – FFSS Deployments end. Winter Watch is cancelled.
Public notification of watch end.
01/23
01/24
01/25
01/26
01/27

## Slide 4: Summary of FFSS Deployments
Resources Deployed​ | Maximum FFSS Capacity Obligation​ | Maximum Total HSL​ | Maximum Total Base Point​
5 | 650 MW​ | 827 MW​ | 681 MW​

## Slide 5: Deployment Details
Resource | Initiation time | Completion time | FFSS MW Award | Reason
MIL_MILLERG2 | 1/24 10:00:00 | 1/27 12:00:00 | 75 | Capacity
MIL_MILLERG3 | 1/24 10:00:00 | 1/27 12:02:00 | 155 | Capacity
MIL_MILLERG4 | 1/24 10:00:00 | 1/27 12:03:00 | 105 | Capacity
MIL_MILLERG5 | 1/24 10:00:00 | 1/27 12:03:00 | 105 | Capacity
TEN_CC1_1 | 1/24 10:00:00 | 1/24 13:24:00 | 210 | Capacity
TEN_CC1_1 | 1/25 05:00:00 | 1/27 12:05:00 | 210 | Capacity
These deployments were issued through multiple Verbal Dispatch Instructions (VDIs), spanning three Operating Days.

## Slide 6: FFSSR Performance
FFSSRs are evaluated on their performance in accordance with Protocol 8.1.1.2.1.6
  4 FFSSRs passed all performance requirements.
  1 FFSSR tripped offline while switching to fuel oil during its initial deployment. As a result, it failed some requirements.
Additionally, all FFSSRs are required to show availability during the winter watch timeframe regardless of receiving a deployment or not.
  7 units indicated unavailability at some point during the winter watch from 1/23 to 1/27.
  1 unit indicated unavailability at some point during the winter watch from 1/31 to 2/1.

## Slide 7: Next Steps
A subsequent report will be presented separately for the total amounts from Section 6.6.14.1, Firm Fuel Supply Service Fuel Replacement Costs Recovery, and Section 6.6.14.2, Firm Fuel Supply Service Hourly Standby Fee Payment and Fuel Replacement Cost Recovery

## Slide 8: FFSS Current NPRRs
NPRR1275, Expansion of Qualifying Pipeline Definition for Firm Fuel Supply Service in Phase 3 would adopt expanded definition of FFSS Qualifying Pipeline to include natural gas resources which meet certain qualifying conditions for reliable fuel delivery.
  Approved by Board 4/21/2026. Pending PUCT consideration.
NPRR1281, Improvements to Alternate FFSS Resource Designation proposes to clarify the inputs to the calculation of the Firm Fuel Supply Service Standby Fee, specifically the Hourly Rolling Equivalent Availability Factor.
  Approved by PUCT on 11/6/2025.
NPRR1327, As-Built for NPRR1281, Improvements to Alternate FFSS Resource Designation documents the as-built solution for NPRR1281, Improvements to Alternate FFSS Resource Designation, which is currently under implementation.
  Pending at PRS.

## Slide 9: Questions/Comments?
Zhengguo.Chu@ercot.com