## Slide 1
2025 UFE Analysis Report
Data Loading and Aggregation
ERCOT
May 2026

## Slide 2: UFE Basics 1
UFE (Unaccounted For Energy) is computed as follows:
UFE = Generation – (Load + Losses)
Negative UFE indicates load/losses are overestimated
Sources of UFE include:
■ Generation Measurement Errors
■ DC Tie Inadvertent Energy
■ Load - Missing/Erroneous Usage Data
- Backcast Profile Error
- Load Profile ID Assignment Error
- Theft
■ Losses - Model Error
- Loss Calculation Error
- Loss Code Assignment Error

## Slide 3: UFE Basics 2
Net Generation for Settlement Interval
Profiled Energy Usage
Non-Metered Accounts
Interval Data
Energy Usage
Losses:
Transmission & Distribution
UFE
Net Generation
Compared to
Load Buildup
GAP - - - - - - >

## Slide 4: Protocol Language 11.6 – Unaccounted for Energy Analysis
11.6.1 Overview
(1) ERCOT will provide an annual Unaccounted For Energy (UFE) analysis report consisting of UFE data analysis from the preceding calendar year. This report will be based on final Settlement data and will be posted to the Market Information System (MIS) Public Area by April 30th. The appropriate …
11.6.2 Annual Unaccounted For Energy Analysis Report
The annual UFE analysis report will contain both ERCOT-wide and UFE allocation category quantities as follows:
(a) Total UFE MWHs;
(b) Total UFE cost;
(c) Percent of total UFE to ERCOT Load;
(d) Percent of total UFE cost; and
(e) Notice of any factors that may be contributing to UFE.

## Slide 5: Data Required Per Protocol Section 11.6.2
 | A – Total UFE MWHs | B – Total UFE Cost | C – Percent of Total UFE to ERCOT load | D – Percent of Total UFE Cost
TOTUFE_U1 | -1,143,511 | -$45,696,012 | -0.2305% | 100.00%
UFEIDR_U1 | -1,053,573 | -$42,204,159 | -0.2124% | 92.36%
UFENIDR_U1 | -8,777 | -$397,723 | -0.0018% | 0.87%
UFETRANS_U1 | -81,161 | -$3,094,131 | -0.0164% | 6.77%
Legend: | 
TOTUFE_U1 - Total ERCOT Wide UFE | 
UFEIDR_U1 - Distribution IDR UFE | 
UFENIDR_U1 - NIDR UFE | 
UFETRANS_U1 - Transmission IDR UFE | 
May 2025 WMS

## Slide 6: Average Daily % UFE (sorted low to high)

## Slide 7: UFE Monthly MWH

## Slide 8: UFE Monthly Cost

## Slide 9: Historical Yearly Values
 | MWH | COST | % of LOAD | AVG MCP
2007 | 2,914,297 | $206,949,832 | 0.90% | $52.77
2008 | 1,541,086 | $134,692,211 | 0.40% | $68.04
2009 | 1,351,187 | $44,857,873 | 0.40% | $30.89
2010 | 1,756,344 | $85,406,714 | 0.55% | $35.74
2011 | 1,453,256 | $31,666,952 | 0.43% | $43.30
2012 | 1,002,761 | $25,945,816 | 0.31% | $26.60
2013 | -395,393 | -$17,061,127 | -0.12% | $31.71
2014 | 298,578 | $2,286,431 | 0.09% | $38.02
2015 | 240,091 | $1,441,929 | 0.07% | $24.80
2016 | 644,293 | $11,037,155 | 0.18% | $22.60
2017 | -452,775 | -$20,469,613 | -0.13% | $26.53
2018 | 657,974 | $7,209,457 | 0.17% | $32.28
2019 | 252,851 | -$22,095,272 | 0.07% | $38.83
2020 | -265,915 | -$20,023,844 | -0.07% | $24.03
2021 | 356,388 | $246,439,449 | 0.09% | $150.40
2022 | 1,126,521 | $20,085,214 | 0.26% | $64.89
2023 | -1,078,199 | -$92,779,500 | -0.24% | $50.68
2024 | -4,080,762 | -$144,444,551 | -0.88% | $29.37
2025 | -1,143,511 | -$45,696,012 | -0.23% | $35.15
Notes: (1) Negative Cost indicates load/losses are overestimated. (2) [Loss Adjusted Load] + UFE = [Final Aggregation for Settlements]

## Slide 10: NPRR 1145 Implementation
Approved by Public Utility Commission in May 2023
Changed the 15-minute level ERCOT wide Transmission Loss Factors (TLFs) that are used in the settlement process from seasonal base case TLFs to State Estimator-calculated TLFs in Energy Management System (EMS).
Implemented March 28, 2025.

## Slide 11: UFE Post NPRR 1145 Implementation
In the first quarter of 2025, which used seasonal base case modeled TLFs, the UFE as a percent of total load was -0.65
In the first quarter of 2026, which used state estimator TLFs, the UFE as a percent of total load was -.01
Chart: January - March
| 2025 | 2026
UFE as Percent of Total Load | -0.0065394 | -7.793e-05

## Slide 12: 2025 Deemed Transmission Loss vs. UFE

## Slide 13: Transmission Loss Factor Calculation Review
13.2.2 Actual Transmission Loss Factor Calculations
ERCOT shall determine the Actual TLF for each interval in the Operating Day by dividing the sum of line and transformer MW losses by the total ERCOT Load as determined by the State Estimator in the Energy Management System (EMS).
The day after the Operating Day, ERCOT shall publish Actual TLFs to be used in Settlement calculations.
13.2.5 Actual Transmission Loss Factor Calculation
(1) The following formula shall be used by ERCOT’s State Estimator process to determine Actual TLFs.
TLF i = (ΣLINE_LOSSES i) + (ΣTRANSFORMER_LOSSES i) / ESL i

## Slide 14: QUESTIONS?