## Slide 1: NPRR1188 & NPRR1244: Nodal Dispatch, Energy Settlement & PFR Clarification for Controllable Load Resources Anthony Pataray Demand Integration - ERCOT May 15, 2026
Anticipated Go Live – January 2027
Outline:
Key Changes Introduced with NPRR 1188
Nodal Settlement for Controllable Load Resources
Energy Bid Curves (Replace RTM Energy Bids)
Separate Metering Requirement
New & Modified Resource Statuses
Grid Reliability & Market Efficiency Benefits
NPRR 1244 – CLR PFR Requirements

## Slide 2: Key Changes Introduced with NPRR 1188
CLRs (non-ALR) will be assigned a Resource Node Settlement Point
Dispatch will use the nodal shift factor at the CLR's actual location
Energy consumption will be settled at the nodal (LMP) price
RTM Energy Bids replaced by Resource-specific Energy Bid Curves (moved to Protocol Section 4)
In the DAM, Energy Bid Curves will be co-optimized with Ancillary Service offers
New resource statuses introduced: ONTEST, ONHOLD; OUTL restricted to zero-consumption outage only
CLR total energy consumption must be separately metered from all other load and generation at the site. This is the total energy consumption and not just the demand response/dispatchable capability.

## Slide 3: Nodal Settlement for Controllable Load Resources
 | Current Method | Post NPRR 1188
Dispatch | CLRs dispatched using zonal shift factors | CLRs dispatched using their actual nodal shift factor
Energy Settlement | CLR consumption settled at the zonal price | CLR consumption settled at the nodal (LMP) price
Price Signal | CLR receives/pays an averaged zonal price — not its true locational cost | CLR receives/pays the precise price signal at its node
Congestion Management | Zonal factors misrepresent CLR impact on transmission constraints | Nodal factors accurately reflect CLR impact, improving congestion management
DAM Co-Optimization | CLR Ancillary Service offers are NOT co-optimized with RTM Energy Bids | Energy Bid Curves are co-optimized with AS offers in the Day-Ahead Market
Co-located Resources | CLRs and co-located Generation Resources can only offer excess capacity after netting | Each resource offers its full independent capacity to ERCOT markets
Applies to CLRs that are not Aggregate Load Resources (ALRs). ALRs will continue to be settled zonally.

## Slide 4: Energy Bid Curves (Replace RTM Energy Bids)
New Sections 4.4.9.8, 4.4.9.8.1, 4.4.9.8.2 define Energy Bid Curve criteria and validation
Energy Bid Curves are Resource-specific
  Each QSE submits resource specific curves
In the DAM, Resource-specific Energy Bid Curves are co-optimized with Ancillary Service offers from the same Resource
CLR Energy Bid Curves are always inclusive with AS offers
Applies to both single-site CLRs and ALRs for the DAM co-optimization change
Not applicable to NCLRs
Reduces market inefficiency where AS and energy offers were previously optimized independently

## Slide 5: Separate Metering Requirement
Total CLR consumption must be separately metered from all other load and generation at the site. This is the total energy consumption and not just the demand response/dispatchable capability.
  Any New or Existing CLRs must have meters installed by TDSP
  Existing CLRs will need to have meters installed no later than December 31st, 2026, or risk being deregistered
For sites with TDSP-read meters (AMI, IDR, non-EPS): TDSP must separately meter CLR load before sending data to ERCOT
  ERCOT will NOT perform net metering calculations on incoming meter data — all netting is done by the TDSP prior to submitting data to ERCOT
For EPS read meters, the CLR load must be separately metered from all other loads or resources
Applies to CLRs that are not Aggregate Load Resources (ALRs)
Related document: OBDRR046 and Settlement Metering Operating Guide, Section 8 will also require revision, 10.2.2 (TDSP and DSP Metered Entities) and 10.2.3 (EPS Meters)

## Slide 6: New & Modified Resource Statuses
ONTEST (new): Load Resource is On-Line but blocked from SCED for operations testing purposes
ONHOLD (new): Load Resource is On-Line but temporarily unavailable for SCED dispatch due to a valid operational reason; Base Points set equal to telemetered net real power
ONL (existing): Load Resource is available for dispatch by SCED with an Energy Bid Curve, unchanged
OUTL (modified): Load Resource is completely unavailable,
  OUTL can ONLY be used when the Resource is Off-Line and energy consumption (NPF) is zero
Applicable to both CLRs and NCLRs
These changes improve operational transparency and ensure ERCOT visibility into LRs availability at all times

## Slide 7: Grid Reliability & Market Efficiency Benefits
Nodal dispatch improves congestion management by accurately representing CLR impact on transmission constraints
Correct locational price signals incentivize CLRs to respond efficiently to real-time grid conditions
DAM co-optimization of Energy Bid Curves and AS offers increases Day-Ahead Market efficiency
Full visibility of CLR capacity (including co-located resources) improves ERCOT's ability to manage reliability
  CLR consumption settled using the same method as Non-Wholesale Storage Load (non-WSL) charging load
    CLR energy from the grid: adjusted for losses and UFE; included in 4-CP, LRS, and UFE allocation
    CLR energy from co-located Generation Resource: NOT adjusted for losses; excluded from 4-CP and CARD
  Full capacity of both CLR and co-located Generation Resource can be independently offered into ERCOT markets
Increases Ancillary Service-qualified MWs visible in DAM, SASMs, and through self-arrangement

## Slide 8: NPRR 1244 – CLR PFR Requirements
Key Takeaway: Load Resources that lack PFR capability can now register as CLRs and provide ECRS
Current rule: to provide ECRS, a CLR must be SCED-qualified AND capable of providing Primary Frequency Response (PFR)
Upon NPRR 1244 Implementation
  ECRS eligibility for CLRs no longer requires PFR capability. A CLR qualified for SCED may provide ECRS regardless of PFR status
  PFR capability requirement retained for Reg-Up, Reg-Down, and RRS
PRC5 and PRC6 formulas updated
  Only CLRs active in SCED AND qualified for PFR required products count toward PRC

## Slide 9: Thank you!
ErcotLRandSODG@ercot.com