## Slide 1: Potential Price Correction for Real-Time Market Matthew Young Supervisor, Market Validation May 19, 2026
Impact Summary
Proxy Energy Offer Curves were not created correctly for Qualified Facilities with an Output Schedule.
There were 5 Operating Days that met criteria for Board Review. With the largest impact to a Counter Party being approximately $74 thousand.

## Slide 2: Energy Offer Curve Creation for Output Schedules
When a resource submits an Output Schedule, ERCOT creates a proxy Energy Offer Curve based around the submitted Output Schedule.
Target MW = submitted Output Schedule.
MWs below target = -$250/MWh.
MWs above target = Real-Time System Wide Offer Cap (RTSWCAP).

## Slide 3: Special Logic for Qualified Facilities
What is a qualified facility?
“A qualifying small power production facility or qualifying cogeneration facility under regulatory qualification criteria as defined in 16 U.S.C.A. § 796(17)(C) and (18)(B).”
The resources are treated as “must-take” or “must-run” facilities, meaning ERCOT accommodates their output rather than dispatching them economically.
When a Resource that is designated as a Qualified Facility submits an Output Schedule, the creation of their Energy Offer Curve has one key difference.
Target MW = Current telemetered MW Output

## Slide 4: Details on Price Impact Event
ERCOT discovered a software defect on January 29, 2026 affecting the Real-Time Market (RTM) between December 17, 2025 and January 29, 2026. ERCOT corrected the defect on January 29, 2026.
Security-Constrained Economic Dispatch failed to set the output schedules of Qualifying Facilities equal to their telemetered output.
ERCOT issued a market notice on February 5, 2026 (M-A020526-01) to preserve the ERCOT Board of Directors’ ability to review prices. The notice covered Operating Days (ODs) January 6, 2026 through January 29, 2026.
Due to a change in the RTM optimization engine on January 8, 2026, accurate prices for ODs January 6-7, 2026 could not be determined and so were excluded from the impact analysis.

## Slide 5: Impact Analysis Results
ERCOT Protocols Section 6.3(7)(b) requires that the absolute value impact to any single Counter-Party (CP) meet one of the following two criteria before seeking approval from the Board.
  2% and also greater than $20,000; or
  20% and also greater than $2,000.
ERCOT determined that the following Operating Days (ODs) met criteria for significance for the Real-Time Market (RTM).
Operating Day | Counter-Parties meeting criteria in Protocol Section 6.3(7)(b)(i) | Counter-Parties meeting criteria in Protocol Section 6.3(7)(b)(ii)
1/10/2026 | 1 | 0
1/22/2026 | 1 | 0
1/24/2026 | 1 | 1
1/25/2026 | 1 | 0
1/26/2026 | 0 | 1

## Slide 6: Impact Analysis Results
The maximum absolute value impact to Counter-Parties is shown here:
Operating Day | Maximum Amount | Maximum Percentage for Criteria (i)* | Maximum Percentage for Criteria (ii)**
1/10/2026 | $23,114.41 | 9.02% | n/a
1/22/2026 | $27,060.70 | 4.19% | n/a
1/24/2026 | $51,547.17 | 61.73% | 61.73%
1/25/2026 | $74,002.78 | 3.47% | n/a
1/26/2026 | $2,446.12 | n/a | 95.84%
* The maximum of percentage change to any single Counter-Party with impact more than $20,000
** The maximum of percentage change to any single Counter-Party with impact more than $2,000

## Slide 7: Impact Analysis Results
The maximum estimated change in charges due to ERCOT is shown here:
Operating Day | Change in Statement Charges Due to ERCOT | 
1/10/2026 | $5,991.26 | 0.074%
1/22/2026 | $(26,540.67) | 0.124%
1/24/2026 | $(227,722.13) | 0.254%
1/25/2026 | $(284,421.31) | 0.157%
1/26/2026 | $(52,364.11) | 0.055%
Negative amounts are increased payments to Market Participants; positive amounts are increased charges. The percent amount is the absolute value of the percent impact to the previously settlement net amount due to/from ERCOT.

## Slide 8: Conclusion
Our next steps will be to present the impact analysis results for the 5 ODs that met criteria to the June ERCOT Board of Directors meeting for price correction review.