## Slide 1: Analysis of Cost Allocation of Ancillary and Reliability Services in ERCOT Region Responsive to PURA § 39.1593 | PUC Project No. 58555 ERCOT Staff Technical Advisory Committee May 19, 2026
Discussion Outline:
Background and process
Allocation methods and cost drivers
Preliminary primary-effect results
Secondary-effects analysis
Summary and next steps

## Slide 2
Background and Process
2
Legislative Requirement
Public Utility Regulatory Act (PURA) §39.1593 requires evaluation by Dec. 1, 2026 of whether alternative Ancillary Service (AS) and Reliability Service (RS) cost allocation methods produce net savings to consumers compared with the current method of allocating costs to load.
Study Scope
Public Utility Commission (PUC) outlined the alternative methods, historical data period, and analytical areas ERCOT should evaluate in the study scope in PUC Project 58555 for this work.
ERCOT Deliverable & TAC Input
ERCOT report due to the PUC by the end of August 2026.
ERCOT is seeking TAC feedback on the study approach and assumptions before the analysis is finalized.
Project Schedule (from Study Scope)
Jan. 15, 2026
Project scope approved by PUC at Open Meeting.
Jan. – Aug. 2026
ERCOT analysis phase, with an anticipated six-month duration. ERCOT's final report scheduled for end of August 2026.
Sept. – Nov. 2026
PUC Staff-led workshop and request for public comment on ERCOT's final report in September, followed by proposed findings and recommendations filed in October, and PUC consideration in October and November.
Purpose of Today’s TAC Discussion
ERCOT is seeking TAC input on the study approach and allocation-method assumptions to inform ERCOT's analysis and prepare findings for the July TAC discussion and final report.

## Slide 3
Nomenclature for Today’s Discussion
3
Base Case: Current Load Ratio Share (LRS) allocation
Benchmark. AS/RS costs allocated primarily to QSEs representing load.
Method A: PURA § 39.1593(b)(1)
Based on forecast errors during high reliability-risk hours; semi-annual allocation across dispatchable, non-dispatchable, and load.
Method B: operational-risk allocation
Based on forecast errors during all hours; allocation reflects hourly operational risk drivers; daily allocation.
Method C: QSE capacity short allocation
Based on capacity short positions; costs charged first to capacity-short QSEs, with any residual uplift allocated by LRS.
Primary effects
Reallocate historical AS/RS costs using each method and compare to the Base Case.
Secondary effects
Assess how participant behavior, credit, settlement, and consumer-cost impacts could change.
Products in scope
AS: Regulation, RRS, ECRS, Non-Spin RS: BSS, ERS, FFSS, RMR, RUC, VSS * DRRS excluded because it is currently under development and historical pricing and quantity data does not exist.
Historical Basis and Expected Outputs
Use 2024-2025 historical data for AS and RS; estimate allocation by method and service; assess consumer net savings and implementation under each alternative.

## Slide 4
Cost Drivers by Service for Methods A and B
4
Methods A and B allocate costs based on the operational risk the service is procured to address but apply it to different sets of hours.
How Applied
Method A: Applies the service-to-risk mapping during high reliability risk hours.
Method B: Applies the same mapping across all hours.
Reliability Services: 100% allocated to load for Methods A and B.
Service | Cost Driver | Allocation Categories
Regulation Service | 5-minute net-load ramp forecast error | Load + Non-Dispatchable
RRS | Frequency response for large-unit trips | Dispatchable
ECRS | Intra-hour net-load uncertainty | Load + Non-Dispatchable
Non-Spin | Sustained net-load uncertainty and forced outages | Dispatchable + Load + Non-Dispatchable

## Slide 5
Method A – Analysis Hours and Preliminary Results
Method A calculations use the seasonal ramp hours shown below and any low reserve hours included in the analysis. The information below summarize preliminary 2024–2025 results.
Hours used in Method A
Season | Morning Ramp Hours | Evening Ramp Hours
Winter | Hours Ending 5, 6, and 7 | Hours Ending 16, 17, and 18
Spring | Hours Ending 5, 6, and 7 | Hours Ending 18, 19, and 20
Summer | Hours Ending 5, 6, and 7 | Hours Ending 18, 19, 20, and 21
Fall | Hours Ending 5, 6, and 7 | Hours Ending 17, 18, and 19
2024–2025 Preliminary Results by Service
Dispatchable (D)
Non-Dispatchable (ND)
Load
Regulation
ND 52%
Load 48%
$57.1M
Non-Spin
D 28%
ND 44%
Load 28%
$261.7M
Dollar totals ($M)
Service | D | ND | Load | Total
Regulation | — | $29.9 | $27.2 | $57.1
RRS | $198.9 | — | — | $198.9
ECRS | — | $119.6 | $61.0 | $180.5
Non-Spin | $72.5 | $115.8 | $73.5 | $261.7
ECRS
ND 66%
Load 34%
$180.5M
RRS
D 100%
$198.9M
* Totals may not add due to rounding.
** There were no hours in 2024 or 2025 that met the low PRC definition as outlined in study scope.

## Slide 6
Method B – Preliminary Results
The information below summarize preliminary 2024–2025 results under the all-hour framework.
2024–2025 Preliminary Results by Service
Dispatchable (D)
Non-Dispatchable (ND)
Load
Regulation
ND 52%
Load 48%
$57.1M
Non-Spin
D 28%
ND 37%
Load 36%
$261.7M
Dollar totals ($M)
Service | D | ND | Load | Total
Regulation | — | $29.8 | $27.3 | $57.1
RRS | $198.9 | — | — | $198.9
ECRS | — | $115.2 | $65.4 | $180.5
Non-Spin | $73.2 | $95.6 | $93.0 | $261.7
6
ECRS
ND 64%
Load 36%
$180.5M
RRS
D 100%
$198.9M
* Totals may not add due to rounding.

## Slide 7
7
Method C – QSE Capacity Short Approach
Method C allocates AS and RS costs based on QSE capacity short positions using the RUC capacity short Adjustment Period equations that were in effect prior to the implementation of RTC (Protocols § 5.7.4.1.1). Refer to Slide 13 in the Appendix for the Settlement Equations.
How Method C Works
1
Capacity Shortfall Calculation
Each QSE’s capacity shortfall (RUCSF) is computed per 15-minute Settlement Interval using real-time metered load, COP capacity, trades, and DC Tie imports.
2
Capacity-Short Charge (RUCCSAMT)
AS/RS costs are charged to QSEs proportional to their share of total capacity shortfall for each interval, subject to a cap.
3
LRS Uplift (LARUCAMT)
If capacity-short charges are insufficient to cover total cost, the shortfall is uplifted to all QSEs by Load Ratio Share.
QSE Classification Categories
Category Description
Generator QSE represents only generation
Retailer QSE represents only load
Utility QSE represents both generation and load
Power Marketer QSE does not represent generation or load
Equation Modifications
Replace the RUC Make-Whole Amount (RUCMWAMTTOT) with the appropriate AS or RS cost
Replace RUC Capacity Total (RUCCAPTOT) with the corresponding MW quantity
For IRRs, the HSL was used in place of High Ancillary Service Limit at Adjustment Period (HASLADJ)
RUC costs are drawn directly from ERCOT systems, as they are already allocated on a capacity-short basis

## Slide 8
8
Method C – Preliminary Results for AS
The information below summarizes preliminary 2024–2025 results under capacity short framework by QSE category for AS.
Generator
Power Marketer
Retailer
Utility
2024–2025 grand total by Service
RRS
33.2%
33.8%
26.7%
$198.9M
6.3%
ECRS
32.8%
33.3%
27.4%
$180.5M
6.5%
Non-Spin
32.7%
33.9%
27.2%
$261.7M
6.2%
Regulation
34.2%
33.9%
25.9%
$57.1M
6.0%
Service | Generator | Power Marketer | Retailer | Utility | Total
Regulation | $3.4 | $19.5 | $19.4 | $14.8 | $57.1
RRS | $12.4 | $66.0 | $67.3 | $53.2 | $198.9
ECRS | $11.6 | $59.2 | $60.2 | $49.4 | $180.5
Non-Spin | $16.2 | $85.7 | $88.6 | $71.2 | $261.7
Dollar totals ($M)

## Slide 9
9
Method C – Preliminary Results for RS
The information below summarizes preliminary 2024–2025 results under capacity short framework by QSE category for RS.
2024–2025 total by Service
Generator
Power Marketer
Retailer
Utility
* RMR data is only available for Mar. - Dec. 2025. VSS excluded — no Settlement data. ERS excludes Dec. 2025 as Settlement for that contract has not occurred.
BSS
38.4%
35.4%
22.0%
$15.3M
ERS
38.3%
35.4%
22.2%
$133.4M
FFSS
37.2%
35.3%
23.2%
$80.7M
RMR
39.9%
34.5%
22.0%
$64.1M
RUC
33.1%
32.7%
28.0%
$23.9M
4.2%
4.1%
4.3%
3.6%
6.2%
Service | Generator | Power Marketer | Retailer | Utility | Total
BSS | $0.6 | $5.9 | $5.4 | $3.4 | $15.3
ERS | $5.5 | $51.1 | $47.3 | $29.6 | $133.4
FFSS | $3.4 | $30.0 | $28.5 | $18.7 | $80.7
RMR | $2.3 | $25.6 | $22.1 | $14.1 | $64.1
RUC | $1.5 | $7.9 | $7.8 | $6.7 | $23.9
Dollar totals ($M)

## Slide 10
Estimating Secondary Effects
Primary cost reallocation does not, by itself, determine consumer impact. ERCOT is also evaluating how alternative methods could affect market behavior, settlement timing, credit exposure, and consumer costs.
Objectives
Behavior-change analysis support
1. Consumer net savings
Assess whether each method could produce consumer net savings; focus primarily on wholesale market activities.
2. Market Participant behavior
Evaluate whether new AS/RS cost exposure could change operational, trading, maintenance, or investment decisions, and how those responses could affect reliability and costs.
3. Settlement and credit impacts
Assess Method A semi-annual settlement impacts, including advance charges for expected obligations, delayed true-ups, and potential barriers for smaller entities.
ERCOT has engaged a consultant to support the Market Participant behavior-change analysis, including:
Cost signals: Translate Methods A, B, and C into practical exposure metrics, such as $/MW, $/MWh, or QSE capacity-short exposure.
Risk-driver incentives: Assess whether new AS/RS cost exposure could incentivize participants to modify behavior pertaining to the drivers used in the alternative allocation methods, such as forecast error, forced-outage exposure, or capacity-short positions.
Participant response options: Identify practical actions, including offer/bid changes, hedging, QSE trades, self-arrangement, maintenance timing, availability, load response, and firming.
Costs to act: Estimate what it would cost participants to take responsive actions and compare that cost with the AS/RS exposure which would be avoided by such actions.
Potential market outcomes: Assess potential effects on dispatch, AS requirements and costs over time, energy and AS prices, reliability, and consumer net savings.
Near- and Long-term impacts: Separately assess near-term operating and trading responses and longer-term maintenance, investment, resource mix, and firming decisions.
Current status: ERCOT is conducting this work now and expects to share directional and qualitative findings with TAC in July.

## Slide 11: Summary and Next Steps
Summary
ERCOT is evaluating the Base Case and three alternative AS/RS cost allocation methods identified in the PUC study scope.
Primary-effect analysis estimates how historical AS/RS costs would be reallocated under each method by service and cost category; this deck presents preliminary results for Methods A, B, and C.
Secondary-effects analysis will evaluate how alternative cost signals could affect market behavior, settlement timing, credit exposure, reliability, and consumer net savings; secondary-effects work is currently underway
TAC feedback requested by May 29, 2026
ERCOT requests feedback on the study approach, allocation-method assumptions, preliminary results, and secondary-effects categories so input can be considered and incorporated before the July TAC update.
Next steps
Continue quality review of Method A, B and C preliminary results.
Continue secondary-effects analysis and develop directional and qualitative findings.
Present updated findings to TAC on July 29, 2026.
Use TAC feedback to support ERCOT’s final report to the PUC by the end of August 2026.

## Slide 12: Thank you!

## Slide 13
7
Appendix - Method C Capacity Short Settlement
Settlement Equations
RUCCSAMTi,q = (−1) × Max [RUCSFRSi,q × RUCMWAMTTOTh, 2 × RUCSFi,q × RUCMWAMTTOTh / RUCCAPTOTh] / 4
Where:
RUCSFRSi,q = RUCSFi,q / RUCSFTOTi
RUCSFTOTi = RUCSFi,q
RUCSFi,q = Max(0, RTAMLq,p,i × 4 − RUCCAPADJq,i)
RUCCAPADJq,i = HASLADJq,r,h + (RUCCPADJq,h – RUCCSADJq,h) + ( DAEPq,p,h – DAESq,p,h) + ( RTQQEPADJq,p,i – RTQQESADJq,p,i) + DCIMPADJq,p,i
LARUCAMTq,i = (−1) × (RUCMWAMTTOTh / 4 + RUCCSAMTTOTi) × LRSq,i
Variables
RUCCSAMT – $ – Capacity Short Amount
RUCSFRS – Capacity Shortfall Ratio Share
RUCSF – MW – Capacity Shortfall Quantity
RUCMWAMTTOT – $ – Total cost of the AS or RS Settlement
RUCCAPTOT – MW – Total MW of the RS or AS Settlement
RUCSFTOT – MW – Capacity Shortfall Quantity Total
RTAML – MWh – Real-Time Adjusted Meter Load
RUCCAPADJ – MW – Calculated Capacity for the QSE
HASLADJ – MW – High Ancillary Service Limit at Adjustment Period
RUCCPADJ – MW – Capacity Purchases at Adjustment Period
RUCCSADJ – MW – Capacity Sales at Adjustment Period
DAEP – MW – Day-Ahead Energy Purchase
DAES – MW – Day-Ahead Energy Sale
RTQQEPADJ – MW – Real-Time QSE to QSE Energy Purchase
RTQQESADJ – MW – Real- Time QSE to QSE Energy Sale
DCIMPADJ – MW – DC tie Import
LARUCAMT – $ – Load-Allocated Capacity Short Amount
RUCCSAMTTOT – $ – Total Capacity Short Amount
LRS – Load-Ratio Share